## Slide 1: Extended TXOP Sharing
Date: 2023-01-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: TXOP Sharing
802.11be supports the following: [11be Motion 119 ]
  Sharing AP and shared AP may not have the same primary 20 MHz channel
  The primary 20 MHz channel of the shared AP shall be within the BSS operating channel width of the sharing AP.
  The primary 20 MHz channel of the sharing AP shall be within the BSS operating channel width of the shared AP.

## Slide 3: Recap: VHT/HE/EHT BSS Operation
An VHT/HE STA that is an AP or mesh VHT/HE STA should not start a VHT/HE BSS with a 20 MHz operating channel width on a channel that is the secondary 20 MHz channel of any existing BSSs with a 40 MHz, 80 MHz, 160 MHz, or 80+80 MHz operating channel width, or is overlapped with the secondary 40 MHz channel of any existing BSSs with a 160 MHz or 80+80 MHz operating channel width.
If an VHT/HE AP or a mesh VHT/HE STA starts a VHT/HE BSS that occupies some or all channels of any existing BSSs, the AP or mesh STA may select a primary channel of the new VHT/HE BSS that is identical to the primary channel of any one of the existing BSSs.
If an AP or a mesh STA selects a primary channel for a new VHT BSS with a 40 MHz, 80 MHz, 160 MHz, or 80+80 MHz operating channel width from among the channels on which no beacons are detected during the OBSS scans, then the selected primary channel meets the following conditions
  It shall not be identical to the secondary 20 MHz channel of any existing BSSs with a 40 MHz, 80 MHz, 160 MHz, or 80+80 MHz operating channel width.
  It should not overlap with the secondary 40 MHz channel of any existing BSSs with a 160 MHz or 80+80 MHz operating channel width
In the enterprise WLAN, in order to avoid overlapped BSS operating channel among neighbor APs, the AP will select the operating channel with the BW narrower than the AP’s BW capability.
Observation:
  It is unlikely that the OBSS APs in enterprise WLAN have overlapped BSS operating channels.

## Slide 4: Sharing/Shared AP per BSS Operating Channel with Channel Puncture
802.11UHR (Wi-Fi 8) supports the following:
  Sharing AP and shared AP may not have the same primary 20 MHz channel
  The primary 20 MHz channel of the shared AP shall be within the BSS operating channel width of the sharing AP and is not the punctured 20MHz channel of the sharing AP.
  The primary 20 MHz channel of the sharing AP shall be within the BSS operating channel width of the shared AP and is not the punctured 20MHz channel of the shared AP.

## Slide 5: BW of Sharing AP’s Soliciting PPDU
Option1:
  The sharing AP can use the BW wider than its operating BW for transmitting the soliciting PPDU as the initial frame of the TXOP to the shared AP.
    The observation is that such frame exchange is out the scope of the BSS.
    The operating BW information needs to be shared between sharing AP and shared AP.
Option 2:
  The sharing AP can use the BW no more than than its operating BW for transmitting the soliciting PPDU as the initial frame of the TXOP to the shared AP.

## Slide 6: BW within Shared Time
11be TXOP sharing is extended for TXOP sharing with neighbor APs, e.g. in the same ESS or different ESS through the negotiation.
Option1:
  The shared AP can’t use the 20MHz channels that are not covered by the PPDU carrying soliciting frame, e.g. MU-RTS TXS.
    The punctured 20MHz channel by the sharing AP can’t be used by the shared AP during the shared time allocated by the sharing AP.
    the operating BW, channel puncture need to shared among shared AP and sharing AP. Otherwise the channel puncture information needs to be carried in the soliciting frame.
Option 2:
  The shared AP can use the 20MHz channels that are not covered by the PPDU carrying soliciting frame, e.g. MU-RTS TXS.
    The punctured 20MHz channel by the sharing AP can be used by the shared AP during the shared time allocated by the sharing AP.

## Slide 7: Shared AP Identification in Soliciting Frame
Option1:
  Individual address (BSSID of shared AP) is the RA of the soliciting frame.
    Not in line with MU-RTS rules if MU-RTS TXS is used as the soliciting frame.
Option 2:
  Specific AID value in AID12 field as the identifier of solicited shared AP.

## Slide 8: Resource Request for Shared AP’s TXOP Sharing
SCS based resource request is not suitable since a shared AP will use its own EDCA to do the frames exchange.
Solicited and unsolicited methods can be used for shared AP’s resource request.
  TB PPDU should not be used for solicited method of shared AP’s resource request.
The resource request should provide the following information
  Medium time
  BW
  Delay bound of the first frame and the last frame within the solicited medium time.

## Slide 9: Shared Time Returning
A shared AP may not be able to use all its allocated medium time.
The method of returning unused medium time to the sharing AP can be used.
  The HE Control field carries the explicit indication.

## Slide 10: Duration Field and Virtual Carrier Sensing
The soliciting frame for TXOP sharing has Duration field being 0.
If in a TXOP a NAV timer of a STA is set by one of sharing AP, the STAs associated with the shared AP ignores the NAV timer for the frame exchanges with the shared AP.
  Option 1: the intra NAV is set.
  Option 2: the basic NAV is set and is ignored.

## Slide 11: Single TXOP Shared Time or Multiple TXOP Shared Time
TXOP sharing method 1
MU-RTS
TXS
DL OFDMA
In 80MHz
UL
OFDMA In 80MHz
Sharing AP
shared AP
shared AP
shared AP
Coordinated DL OFDMA
In 80MHz
Coordinated UL
OFDMA In 80MHz
service period for blue and orange APs
MU-RTS TXS is used by the sharing AP to allocate its TXOP time to the shared AP(s) and/or the STAs associated with the sharing AP.
Option 1:
  One MU RTS TXS allocates one time period of a TXOP to one shared AP (basic mode) or more than one AP (shared APs or shared AP(s) + sharing AP as enhanced mode).
CTS
MU-RTS
TXS
CTS
CTS

## Slide 12: Single TXOP Shared Time or Multiple TXOP Shared Time
TXOP sharing method 2
UL PPDU
DL BA
DL OFDMA
In 80MHz
UL OFDMA
In 80MHz
DL OFDMA
In 80MHz
UL OFDMA
In 80MHz
DL OFDMA
In 80MHz
UL OFDMA
In 80MHz
orange AP’s service period
(CTFS transmission 2)
green AP’s service period
(CTFS transmission 3)
red AP’s service period
(CTFS transmission 4)
Option 2:
  One MU RTS TXS allocates multiple time periods of a TXOP where each time period is allocated to one shared AP or more than one AP (shared AP and additional sharing AP)
Prefer option 1.
MU-RTS
TXS
CTS

## Slide 13: Same Primary 20MHz channel of Sharing and Shared APs
When the sharing AP and the shared APs have the same primary 20MHz channel, some works need to be done to enable the TXOP sharing among the APs:
  Option 1:
    A sharing/shared AP negotiates the primary channel switch for the shared OFDMA so that the different BSSs will the different 20MHz channels to decode their PHY SIG or trigger information.
  Option 2:
    When the sharing AP and at least one shared AP have the same primary 20MHz channel, only one of them can be in allocated time of TXOP sharing, e.g. allocating a time period of the TXOP to the shared AP, or allocating a time period of the TXOP to the sharing AP and the other shared APs for shared OFDMA.
    Option 2 is simpler.

## Slide 14: Sharing and Shared AP per BW Capability
802.11UHR (Wi-Fi 8) supports the following: the sharing AP can send the soliciting frame to allocate its TXOP to the shared AP whose primary 20MHz channel is covered by the supported BW of the sharing AP.
  Sharing AP and shared AP may not have the same primary 20 MHz channel
  The primary 20 MHz channel of the shared AP shall be within the channel width supported by the sharing AP and is not the punctured 20MHz channel of the sharing AP.
  The primary 20 MHz channel of the sharing AP shall be within the BSS operating channel width supported by the shared AP and is not the punctured 20MHz channel of the shared AP.