## Slide 1: AP Coordination
Date: 2023-02-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: R-TWT
802.11be supports the following:
  An AP announces R-TWT schedule.
    An associated STA with the AP supporting R-TWT needs to make sure that its TXOP ends at the beginning of the AP’s R-TWT active SP.
      This is also true for the APs in the same multiple BSSID set and co-hosted AP set.
    Within the R-TWT SPs, the frames of the R-TWT TIDs are serviced first.

## Slide 3: Announcement of AP’s R-TWT SPs and 1-hop AP’s R-TWT SPs
Each AP announces its R-TWT schedule (R-TWT SPs) in its Beacon frame or other management frame.
  The usage of other management frame can avoid the Beacon bloating.
Each AP announces the R-TWT schedule of its neighbor APs.
  The R-TWT schedule information and the owner of the R-TWT, SSID.
The neighbor’s R-TWT information can also be acquired through the central management entity.
AP1
AP2
AP3
AP1 can hear the Beacon of AP2 and AP3. AP2 can’t hear AP3’s Beacon.
AP3 can’t hear AP2’s Beacon.
AP1 announces its R-TWT SPs, and R-TWT SPs of its neighbor AP2 and AP3.
Central management entity

## Slide 4: Usage of 2-hop AP’s R-TWT SPs
With the information of 1-hop neighbor AP’s R-TWT SPs from the neighbor AP, an AP can acquire 2-hop neighbor ÄP’s schedule information.
The additional information can increase the medium efficiency, e.g. when the R-TWT APs of an AP and its 2-hop AP overlap with each other.
  In order to avoid interference between the overlapped TWT SPs (e.g. overlapped R-TWT SPS of AP2 and AP3 in the figure), AP2 and AP3 may restrict the maximal Tx Power of some associated STAs through spatial reuse operation.
AP1
AP2
AP3
AP1 can hear the Beacon of AP2 and AP3. AP2 can’t hear AP3’s Beacon.
AP3 can’t hear AP2’s Beacon.
AP1 announces its R-TWT SPs, and R-TWT SPs of its neighbor AP2 and AP3.
AP2 selects its R-TWT SPs that do not overlap with AP1’s R-TWT SPs, and should
overlap with AP3’s R-TWT SPs.
Central management entity
AP1
AP2
AP3
AP2’s R-TWT SP
AP1’s R-TWT SP
AP3’s R-TWT SP
AP1
AP2
AP3
AP1’s R-TWT SP
AP3’s R-TWT SP
Medium time that AP2’s BSS can use
AP2’s R-TWT SP
APs’ R-TWT SPs without 2-hop AP’s information
APs’ R-TWT SPs with 2-hop AP’s information

## Slide 5: STA’s Notification of Neighbor AP’s R-TWT SPs and R-TWT Selection Restriction
A STA reports the R-TWT SPs of its neighbor APs to its associated AP and reports the R-TWT SPs of neighbor AP’s neighbor AP.
  The STA’s report can happen when the neighbor’s updated/new R-TWT SPs are overlapped with the R-TWT SPs that the STA is the member.
  Another method is that when a STA detects R-TWT SP overlapping with neighbor BSS, the STA initiates the new R-TWT SP negotiation with the inclusion of its neighbor BSS’s R-TWT SPs.
    The inclusion of such information can avoid the AP to select the TWT SP information Whose APs overlap with R-TWT SP of STA’s neighbor AP.
AP1
AP2
AP1 can’t hear the Beacon of AP2. AP2 can’t hear AP1’s Beacon.
STA21 associated with AP2 can hear AP1’s Beacon.
STA21

## Slide 6: Coordination among APs with Different SSIDs
An AP (AP1) can announce whether it respect the R-TWT SPs of its neighbor AP (AP2) when AP1 and AP2 are not in the same ESS. Or AP1 and AP2 needs to negotiate the agreement to respect the R-TWT SPs of the peer AP.
  When AP1 and AP2 announces such support or successfully negotiate the R-TWT SP respect, AP1(AP2) will announce the R-TWT SPs of AP2 (AP1) and indicate that the associated R-TWT STAs need to respect AP2’s (AP1’s) R-TWT SPs.
    The STAs associated with AP1 (AP2) will stop its TXOP at the beginning of AP2’s (AP1’s) R-TWT Ps.
    AP1 (AP2) will stop its TXOP at the beginning of AP2’s (AP1’s) R-TWT Ps.
For APs within the same ESS, this indication/negotiation may also be used.

## Slide 7: Selective consideration of the neighbor AP’s R-TWT SP
When an AP announces neighbor AP’s R-TWT SP schedule information to associated non-AP STAs, the AP may announce additional information indicating which non-AP STA (e.g., some of associated non-AP STAs) should follow the R-TWT rule for the neighbor AP R-TWT SP (e.g., considering the overlapping quiet interval, finishing its TXOP before the R-TWT starts).
  This additional information can be
    A Broadcast TWT ID of which member non-AP STA should consider the neighbor AP’s R-TWT SP, or may not consider it (depending on the definition of the information)
    Receiving of the inter-BSS frame from the neighbor BSS by the non-AP STA with additional conditions such as a measurement duration and a threshold of the signal quality (e.g., RSSI, RCPI, or RSNI etc.)
      If a non-AP STA (e.g., STA21) receives an inter-BSS frame of the neighbor BSS (e.g., a Beacon frame sent by the neighbor AP) that exceeds the indicated threshold of the signal quality during a certain duration, the non-AP STA should consider the neighbor AP’s R-TWT SP.
      Otherwise, a non-AP STA (e.g., STA22) may ignore the neighbor AP’s R-TWT SP
  In addition, an AP may transmit to a non-AP STA an individually addressed management/action frame including the neighbor AP’s R-TWT SP schedule information of that the non-AP STA should follow the R-TWT rule and optionally the additional information as in described above.
AP1
AP2
AP2 announces AP1’s R-TWT SP schedule info
STA21 associated with AP2 can hear AP1’s Beacon.
STA22 associated with AP2 can’t hear AP1’s Beacon
STA21
STA22