## Slide 1: Triggered Beamforming in UHR
Date: 2023-02-20
Authors:

## Slide 2: Introduction
Increased throughput, improved reliability and more efficient use of the spectrum are important goals of UHR [1]
One classical approach to improve the SNR and therefore improve the throughput, reliability and spectrum usage is employing beamforming
  Not only is the SNR at the intended receiver improved, but interference to non-intended receivers is typically reduced
Beamforming has been supported since 802.11n, and is widely used in practice
  Both single-user beamforming as well as downlink multi-user MIMO (where beamforming is used to not only increase the SNR but also to reduce the Multi-User Interference)
In this contribution we propose that beamforming for triggered transmission is supported within UHR

## Slide 3: UL BF Limitations for a TB PPDU in 11ax/be
Since 11n, BF has been supported for both DL and UL for a non-triggered transmission (i.e. SU as well as DL MU-MIMO transmissions)
  There are devices in the market that support UL BF
In 11ax/be, BF isn’t supported for a TB PPDU
  Protocol-related: AP needs to trigger STAs to transmit Sounding NDP, AP needs to provide triggered STAs with precoders
  Signaling-related: AP needs to indicate to triggered STAs to apply precoder, STAs cannot indicate in TB PPDU that the transmission is precoded
The above-described issues need to be addressed in order to efficiently support BF for TB PPDUs (described in more detail in [2])

## Slide 4: Performance and Complexity
In [2] we described a high-level protocol required for supporting BF in TB PPDUs, and presented link-level and goodput results showing the impact of BF on TB PPDUs
  Assuming entire protocol and practical PPDU durations (e.g. Trigger Frame, Block-ACK, BFR etc.)
  Several channel models
We also considered the (small) impact on the complexity
A similar high-level protocol was presented in [3], and the performance gap demonstrated for beamforming applied to triggered UL MU-MIMO is very significant

## Slide 5: Conclusions
Beamforming is an important feature of 802.11, and is widely used in products, in both DL & UL
Since 11ax, triggered transmissions (TB PPDUs) are commonly used in the UL
However, beamforming is not supported for TB PPDUs (both OFDMA and MU-MIMO)
  Adding support is expected to improve the throughput & reliability across the entire SNR range, aligning with UHR’s scope
  The additional complexity is rather minor
We propose that beamforming for triggered transmissions is supported within UHR

## Slide 6: References
[1] 11-23/0028r6: PAR Discussion (Laurent Cariou)
[2] 11-20/1672r2: UL Beamforming for TB PPDUs in 11be (Shimi Shilo et al)
[3] 11-23/0027r1: Uplink MU MIMO Improvements (Sigurd Schelstraete et al)
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”