## Slide 1
Proposal for OTA MAC Change
Date: 2023-03-02
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission presents ideas on OTA MAC Address change while a STA is associated for non-MLD STAs

## Slide 3: Summary
Allowing SA and DA MAC addresses to change separately would improve the privacy of transmissions by making it more difficult to correlate the downstream and upstream transmissions to a STA.
Using a EDP Active bit can allow STAs to understand which devices can support MAC transition during association.
Using an OTA MAC Change Count field in a Beacon frame can allow STAs to ensure synchronization with the AP. The need for more bits is TBD.

## Slide 4: Requirements
The following requirements all deal with changing a STA’s OTA MAC address.
6 | 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP.
7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection.
8 | 11bi shall define a mechanism for a CPE AP to initiate changing the OTA MAC Addresses of a set of associated CPE Client’s in the BSS (those CPE Clients in Associate STA State 4) without any loss of connection.
12 | 11bi shall define a mechanism for a CPE Client and CPE AP to establish the CPE Client’s DS MAC Address without the CPE Client’s DS MAC Address being transmitted in the clear.
39 | 11bi shall define a mechanism for a BPE AP and a BPE Client to change the OTA MAC addresses, SN and PN they use for unicast transmissions.

## Slide 5: MAC change while associated
Proposal:
  Use separate unrelated random OTA MAC addresses for SA and DA values for a STA.
  For clarity, I’ll name the MAC addresses from the perspective of the STA they refer to:
    SMAC is used by the STA for its outgoing transmissions.
    DMAC is used by the STA to set up its receive address filtering.
  From the perspective of the AP (assuming the STA is a non-AP STA), the DMAC is used for its transmissions to the STA, and the SMAC is used to identify transmissions from that STA.
Advantages:
  Using unrelated values for DA and SA obscures the relationship between DS and US traffic when there is more than one STA associated to an AP.
  For example – in [2], it discusses the captured traffic is sorted using the device MAC address
  Disadvantage:
  Device design has assumed for a long time that the DA and SA are the same value. Breaking that paradigm may be challenging.

## Slide 6
STA
AP
STA associates/authenticates with AP and shared PMK is known to both, as well as initial STA OTA MAC (MAC1)
STA indicates to AP that it supports MAC Change While Associated (EDP Active bit = 1) (MAC1)
AP initiates MAC change
Queues are emptied in both directions using previous MAC1
STA transmits new US traffic using (SMAC1) as SA
AP transmits new DS traffic using (DMAC1) as DA
Example change sequence

## Slide 7: MAC generation
In 11-22/114r3, the following formula was proposed:
@MAC (n+1) = PRF-128/46(ERCM Key, “ERCM”, @MAC(n), 128)
Where the ERCM key is passed in a separate action frame exchange, and the leftmost 46 bits are selected.
Since a PMK is already available, the following is proposed:
@PairMAC (n+1) = PRF-128/46(PMK, “PairMAC”, @PairMAC(n), 128)
Where the PMK is the current Pairwise Master Key
The leftmost 46 bits are selected for SA MAC used to TX from a non-AP STA
The next 46 bits are selected for the DA MAC used for traffic to the same non-AP STA.
Alternatively,
@SMAC (n+1) = PRF-128/46(PMK, “SMAC”, @SMAC(n), 128)
@DMAC (n+1) = PRF-128/46(PMK, “DMAC”, @DMAC(n), 128)
Where the PMK is the current Pairwise Master Key
The leftmost 46 bits are selected for each MAC (SMAC to mark traffic TX from a non-AP STA, DMAC used to mark traffic TX to the same non-AP STA).
Using an existing key avoids additional messaging exchanges.
Changing the SA and DA MACs separately removes the linkage between DS and US traffic.

## Slide 8: OTA MAC change while associated
  Proposal:
  STA indicates to other STAs that it can support a MAC Change while associated by setting the Enhanced Data Privacy (EDP) Active to 1
  A STA can avoid OTA MAC change while associated by not including that bit or setting it to 0. For instance, if a STA cannot support a transition, it can clear the bit until it can support such a transition.
  If an AP STA sets the bit, then any associated STAs that also support this feature should be prepared for a transition to begin unless they have not set their EDP bit to 1.
  If an AP has only one STA with EDP active, the AP may choose to put off changing OTA MAC address until there are at least 2 STAs supporting the feature.

## Slide 9: Trigger and Synchronization of OTA MAC change while associated
    To allow for a STA to synchronize its OTA MAC addresses with the AP, a new field in the Beacon frame is proposed called the OTA MAC Rotation Count field.
    As the counter increases, it signals to all STAs that a change has happened
    If a STA has been dozing or lost communication briefly or suffered a restart, thus missing an OTA MAC address change, the STA can discover that it is out of sync with the AP by checking the OTA MAC Rotation Count field in the Beacon frame.
    Each time the PMK is changed or reinitialized, the OTA MAC Rotation Count field is cleared. Each time an OTA MAC rotation is executed, the counter is incremented.
    Since the sequence of MAC addresses linked to a STA is fixed once the PMK and starting STA MAC address is known, a STA can consult the OTA MAC Rotation Count field to find out how many iterations of the MAC address generation utility must be run to get back in sync with the AP.
    For example, if the STA last knew that the OTA MAC Rotation Count field was at 501 and then sees the field is at 503, it knows that it must take the OTA MAC information from instance 501 and iterate the OTA MAC generation algorithm twice to get back in sync with the AP, assuming that the PMK is unchanged.

## Slide 10: Straw Poll 1
Is the group interested in text to separate the SA and DA for OTA MAC address rotation?

## Slide 11: References
[1] 11-22/114r3 – Enhanced Random and Changing MAC Address
[2] The Dark Side(-Channel) of Mobile Devices: A Survey on Network Traffic Analysis, IEEE Communications Surveys & Tutorials, Vol. 20, Issue 4. pp 2658-2713, 2018.