## Slide 1: Considerations on Seamless Roaming
Date: 2023-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | 
 |  |  |  | js.choi@lge.com
Sunhee Baek |  |  |  | 
 |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10225 Willow Creek Rd, San Diego, CA, USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
For a quite long time, we’ve tried to solve issues of STAs moving from a BSS to another BSS
  E.g., using Fast Transition (FT) Protocol
  However, we are still experiencing the break to transmit/receive data during a roaming due to authentication and reassociation procedures (with additional delay)
It is significantly important to avoid such interruption and delay as customers have always expected while the approved UHR PAR [1] has a scope of considering mobility between BSSs
  We need some mechanisms to achieve high reliability with reducing the delay
Therefore, in this contribution, we share some considerations to achieve seamless roaming in UHR
  Especially, with the perspective of AP MLD domain [2]

## Slide 3: Overview of Current Roaming
Non-AP MLD disassociates with the currently associated AP MLD (AP MLD 1) when intending to roam to another AP MLD (AP MLD 2)
Non-AP MLD authenticates and reassociate with AP MLD 2 (e.g., over-the-air case in fast transition (FT))
  After successful setup and authentication, the non-AP MLD negotiates some agreements with AP MLD 2 again (e.g., BA agreement)

## Slide 4: Potential Considerations
Maintenance of Contexts/Agreements
  When authenticated and reassociated, necessary security keys (e.g., PTK) are established (e.g., /w.o 4-way handshake in FT) and some agreements (e.g., BA) are reset
    It leads to additional delay which prevents data frame exchange seamlessly
  We need method(s) where most or all of them can be maintained even during/after roaming
Avoidance of data interruption
  Before data path to a new AP MLD, i.e., before creating the DS-to-STA mapping for the AP as a result of reassociation, the AP cannot transmit any Data frames (as Class 3 frame) to the roaming STA
    The AP wouldn’t guarantee whether it can be transmitted to the STA (without capa. negotiation)
  We need method(s) to enable data frame exchanges during roaming by making data paths

## Slide 5: Potential Considerations (Cont’d)
Light Frame Exchange
  Current Authentication and Reassociation frames overhead are heavy to support seamless roaming
  We need light frames compared to existing ones where during their exchange, the new AP MLD and STAs can negotiate security key, capabilities, and operational parameters

## Slide 6: Observations on AP MLD from 11be
As a good candidate to resolve those considerations, we can consider an architecture where APs (involved in roaming) are in an AP MLD [2], which can have the followings on some level
  MLD-level contexts/agreements (e.g., PTK, BA agreements) can be maintained
  MLD-level DS-to-STA mapping (i.e., data path)
  Usage of multi-link probe request/response to discover APs in the same AP MLD
Additionally, to enable above-mentioned ones, we need mechanism(s) existing multi-link (ML) setup is reconfigured when roaming by involving the new AP(s) to be roamed without any tear-down (disassociation)
  We may reuse Reconfiguration Multi-link Element to change the link(s) for roaming

## Slide 7: AP MLD for Roaming
APs in AP Group 1 and 2 are affiliated with the same AP MLD
  APs in the same group may be in a physical device (collocated)
Roaming would be generally needed between groups
  We may allow for a non-AP MLD to be connected with APs in multiple groups (e.g., AP 2 and AP 4)

## Slide 8: Examples of Roaming Procedure
Assuming ML setup reconfiguration can be performed without tear-down
  Non-AP MLD may change one or more link(s) at a time
  Non-AP MLD may add additional link(s) temporarily for a STA
    After roaming, the previous links will be deleted

## Slide 9: Further Considerations
Identification of Group
  Each group may be identified necessarily due to lack of ID space
  The identification (if defined) would be utilized in discovery (e.g., multi-link probe request/response) and multi-link setup (e.g., reconfiguration)
Upper (Common) MAC sublayers in AP MLD
  We can think about where upper MAC sublayer exists, e.g., per AP Group and/or across all of AP Groups (i.e., centralized)
    It can depend on which parameters, which is at MLD-level in 11be, should be at MLD-level across AP groups or AP Group-level (like MLD-level in 11be)
      At least, it would be better to have an Upper (Common) MAC sublayer across all of AP groups

## Slide 10: Conclusion
In this contribution, we’ve shared considerations to achieve seamless roaming in UHR in terms of
  Maintenance of Contexts/Agreements
  Avoidance of data interruption
  Light Frame Exchange
To resolve those considerations, we provide some examples of roaming based on ML setup reconfiguration based on AP MLD domain as a good candidate feature for seamless roaming with further considerations
  Identification of Group
  Upper (Common) MAC sublayer in AP MLD

## Slide 11: References
[1] 23/0480r0, UHR Proposed PAR
[2] 23/1910r3, Seamless Roaming for UHR