## Slide 1: Beacon Design
Date: 2023-02-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Summary
Each AP schedules the Beacon transmission at its TBTTs separated by the beacon intervals.
When a new MAC+PHY generation is defined, an AP that supports the new MAC+PHY generation carries capabilities elements of the old MAC+PHY generation, operation elements of the old MAC+PHY generation besides the capabilities element and operation element of the new MAC+PHY generation in its Beacon, Probe Response, (Re)Association Response.
When a new MAC+PHY generation is defined, a STA that supports the new MAC+PHY generation carries capabilities elements of the old MAC+PHY generation, operation elements of the old MAC+PHY generation besides the capabilities element and operation element of the new MAC+PHY generation in its Probe Request, (Re)Association Request.
An AP can announce the MAC+PHY generation requirement of an associated STA in order to join its BSS.
  If a STA doesn’t support the MAC+PHY generation, it can’t associate with the AP
The beacon length (and the length of the Probe Request/Response, (Re)Association Request/Response) can become smaller with the following operation:
  If a STA that supports a MAC+PHY generation or the order generations can’t join a BSS, the beacon (and Probe Response, Association Response) of the BSS will not carry the capabilities parameters, operation parameters of the MAC+PHY generation.
The information announced by an AP at TBTT can be transmitted in more than one frame to avoid the Beacon decoding issue where the legacy STAs discard the long Beacon.

## Slide 3: Beacon in WLAN
Each AP schedules the Beacon transmission at its TBTTs separated by beacon the intervals.
An AP in 5GHz band carries the following capabilities elements and operation elements
  28-cotet HT Capabilities element, 14-octet VHT Capabilities element, 24-octet to 40-octet HE Capabilities element, 5-octet HE 6 GHz Band Capabilities, >=19-octet EHT Capabilities element, 9-octet to 13-octet Multi-link Capabilities element.
  24-octet HT Operation element, 7-octet VHT Operation element, 9-octet to 13-octet HE Operation element, 8-octet to 13-octet EHT Operation element.
An AP in 2.4 GHz band carries the following capabilities elements and operation elements
  28-cotet HT Capabilities element, 24-octet to 40-octet HE Capabilities element, 5-octet HE 6 GHz Band Capabilities, >=19-octet EHT Capabilities element, 9-octet to 13-octet Multi-link Capabilities element.
  24-octet HT Operation element, 9-octet to 13-octet HE Operation element, 8-octet to 13-octet EHT Operation element
An AP in 6 GHz band carries the following capabilities elements and operation elements
  24-octet to 40-octet HE Capabilities element, 5-octet HE 6 GHz Band Capabilities, >=19-octet EHT Capabilities element, 9-octet to 13-octet Multi-link Capabilities element,.
  9-octet to 13-octet HE Operation element, 8-octet to 13-octet EHT Operation element.
The Beacon length of UHR, NG UHR… will keep increasing for including the new capabilities, operation elements.

## Slide 4: BSS Membership Selector
The membership selector announced in Supported Rates and BSS Membership Selectors element through Supported Rates field in an AP’s Beacon is used to announce the minimal MAC+PHY generation that an associated STA needs to support.

## Slide 5: Wi-Fi Chip Shipment
In the future, the market share of the old PHY types will become less and less
  This can give higher chance to enable the BSS without legacy STAs.
  The designed protocol should harmonize with it.
Wi-Fi chipset shipment forecast by IDC towards 2023

## Slide 6: Capabilities Common to >1 MAC+PHY Generations in HT, VHT, HE, EHT Capabilities
.
NOTE: The red circle shows the fields that are used for multiple MAC+PHY
generations.

## Slide 7: Capabilities Common to >1 MAC+PHY Generations in HT, VHT, HE, EHT Capabilities
NOTE1: The red circle shows the fields that are used for multiple MAC+PHY generations.
NOTE2: Only one of the Maximum MPDU Length field and Maximum A-MSDU Length is needed.

## Slide 8: Capabilities Common to >1 MAC+PHY Generations in HT, VHT, HE, EHT Capabilities
NOTE1: The red circle shows the fields that are used for multiple
MAC+PHY generations.

## Slide 9: Capabilities Common to >1 MAC+PHY Generations in HT, VHT, HE, EHT Capabilities
NOTE1: The red circle shows the fields that are used for multiple MAC+PHY generations.

## Slide 10: Light Beacon Design 1
When an AP announces the mandatory support of the nth MAC+PHY generation of the associated STAs, the Beacon frames broadcasted by the AP will not carry the capabilities elements and operation elements of <nth MAC+PHY generations.
The capabilities that are common to multiple MAC+ PHY generations are carried in an element that is independent from the capabilities elements related to the specific generations.
The discussion and rules can be applied to the related information in Probe Request/Response, (Re)Association Request/Response also.

## Slide 11: Variant of Light Beacon Design 1
When an AP announces the mandatory support of the nth MAC+PHY generation of the associated STAs, the Beacon frames broadcasted by the AP will not carry the information in the various capabilities elements and operation elements that is for <nth MAC+PHY generations only.
The following are the examples in the Beacon whose BSS allows associated EHT STAs and associated UHR STAs:

## Slide 12: Beacon Design 2
The BSS operating parameters and capabilities are announced through the Beacon frame and the Beacon Extension frame.
  The Beacon Extension frame is transmitted immediately after the Beacon frame.
  The Beacon Extension frame will not carry the information of the PHY/MAC generations that are older than EHT.
  Either the Beacon or the Beacon Extension frame can carry the information of the PHY/MAC generations that are older than EHT.
The Critical Update Flag and Nontransmitted BSSID Critical Update Flag are applied to the information of Beacon frame and the Beacon Extension frame.
One element and its Fragment elements can’t be separately transmitted in Beacon and the Beacon Extension
The AP can transmit the Beacon frame only when the AP doesn’t accept the further association and there is no critical update being carried by the Beacon Extension.
  .