## Slide 1: TXOP Protection of Non-Primary Channel
Date: 2023-03-01
Authors:

## Slide 2: Introduction
An SST non-AP STA may access the non-primary channel during TWT SPs if it negotiates SST operation with an SST AP.
In [1] and [2], dynamic subband operation (e.g., TXOP based switching to secondary channel) and non-primary channel access (when the primary channel being busy) were discussed to utilize wide-bandwidth more efficiently in UHR .
In the coordinated TDMA/OFDMA scenario, the sharing AP may allocate a non-primary channel to the shared AP.
  For example, the primary 20MHz channel of the sharing AP may be different from that of the shared AP [3].
MU-RTS and CTS frames are transmitted on the channels including the primary channel (e.g., primary 20MHz, 40MHz, 80MHz, 80+80MHz, 160MHz, and 320MHz) to protect the TXOP.
In this document, we will discuss TXOP protection of the non-primary channel through the enhanced MU-RTS and CTS frame exchange.

## Slide 3: Limitation of existing TXOP protection (1/3)
Issue #1: If any 20MHz subchannel of the allocated RU in an MU-RTS Trigger frame is busy, a non-AP STA shall not respond with a CTS frame.
  It may incur the resource waste and decrease the spectrum utilization if the AP intends to allocate the resource to the non-AP STA other than the busy 20MHz subchannel after MU-RTS/CTS frame exchange.

## Slide 4: Limitation of existing TXOP protection (2/3)
Issue #2: An AP may not be aware of which non-AP STA responds with a CTS frame in response to an MU-RTS Trigger frame
  For example, no transmission of the CTS frame on the primary 40MHz channel may not be recognized by the AP when the CTS frame is received on the primary 80MHz channel from other non-AP STA.
  It may incur the resource waste when the AP allocates an RU on the primary 40MHz to the non-AP STA after the MU-RTS/CTS frame exchange.

## Slide 5: Limitation of existing TXOP protection (3/3)
Issue #3: Since transmission of the CTS frame only on the non-primary channel is not allowed, TXOP protection may not be provided to:
  An SST non-AP STA
  A non-AP STA performing non-primary channel access
  A non-AP STA switching to the secondary channel for dynamic subband operation
  A shared AP that has different primary channel from that of a sharing AP for C-TDMA/OFDMA

## Slide 6: TXOP protection of the non-primary channel (1/2)
Option 1: CTS frame transmission on a secondary channel only
  E.g., A CTS frame in a non-HT (duplicate) PPDU can be transmitted on the secondary 20MHz, 40MHz, 80MHz, etc. (e.g., STA2 and STA3)

## Slide 7: TXOP protection of the non-primary channel (2/2)
Option 2: CTS frame transmission on the primary 20MHz channel and the secondary channel
  E.g., A CTS frame can be transmitted on the primary 20MHz channel and the secondary channel in a punctured non-HT duplicate PPDU (e.g., STA2)

## Slide 8: Pros. & Cons. of option 1 and option 2
Option 1: CTS frame transmission on a secondary channel only
  Pros: Applicable to various scenarios such as SST operation, non-primary channel access and dynamic sub-band operation
  Cons: A TXOP may be interfered or cancelled if a CTS frame is not received on the primary 20MHz channel in response to an MU-RTS Trigger frame
Option 2: CTS frame transmission on the primary 20MHz channel and the secondary channel
  Pros: Ensuring the TXOP protection of the primary 20MHz channel
  Cons: May not be applicable to various scenarios such as SST operation, non-primary channel access and dynamic sub-band operation
Option 1 and option 2 can be used appropriately to various cases

## Slide 9: Summary
The existing TXOP protection based on the primary channel has some limitations as shown in this document.
TXOP protection needs to be extended to protection of the non-primary channel.
CTS frame transmission in response to an MU-RTS Trigger frame can be conducted on the non-primary channel with or without the primary 20MHz channel.

## Slide 10: References
[1] 11-22/2204, Dynamic Sub-band Operation
[2] 11-23/0034, Non-Primary Channel Utilization
[3] 11-23/0041, Considerations on Coordinated TDMA