## Slide 1: Trigger Frame Protection
Date: 2023-03-06
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Ido Ouzieli |  |  |  | 
Danny Alexander |  |  |  | 
Daniel F Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Robert Stacey |  |  |  | 
Ehud Reshef |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Goal of UHR:
  The Study Group will investigate technology which may improve reliability of WLAN connectivity, reduce latencies, increase manageability, increase throughput including at different SNR levels, and reduce device level power consumption.
We discuss the consideration of reliability for wireless connectivity and power consumption using Trigger frame

## Slide 3: Usage of Trigger frame
Trigger frame has been used significantly in a BSS in 802.11ax and 802.11be
  MU-RTS/BSRP frame for initiation of various power save operation like SMPS and eMLSR
  MU-BAR/GCR MU-BAR to solicit block ack
  Basic Trigger frame/BFRP/BSRP/BQRP to solicit data and reports
    Client continues to send useless data, which wastes power and medium
    Client may have to shift window without PBAC or lose capability to move window quickly with PBAC by using ADDBA with PBAC
    Client has to wake up for nothing and lose power. Similar to the attack of wakeup packet in 11ba

## Slide 4: Usage of Trigger frame
Trigger frame has been used significantly in a BSS in 802.11ax and 802.11be without protection
  Attacker sends MU-RTS/BSRP frame for useless initiation of various power save operation like SMPS and eMLSR
    Client has to wake up for nothing and lose power. Similar to the attack of WUR frame in 11ba
  Attacker sends MU-BAR/GCR MU-BAR to solicit block ack
    Client may have to shift window without PBAC or lose capability to move window quickly by using separate management frame with PBAC
  Attacker sends Basic Trigger frame/BFRP/BSRP/BQRP to solicit data and reports
    Client sends useless data/padding, which wastes power and medium

## Slide 5: Proposal: Trigger frame protection
With Trigger frame protection, all the attack scenarios for client can be prevented directly
  Client does not respond to fake MU-RTS/BSRP and wake up to lose power
  Client can still move window and respond BA based on MU-BAR
  Client does not respond to fake Trigger variant with long duration
Trigger frame protection can be achieved with similar method of Beacon frame protection
  Use BIP
  Use cipher suite indicated in group management cipher suite
  Have a key ID field, PN field, MIC field signaling inside the protected Tigger frame

## Slide 6: Further high level consideration
One key/PN under Multiple BSSID with one Trigger frame similar to the design of BIGTK
Key/PN may be the same as BIGTK/BIPN but due to lower layer processing Trigger frame, which is a control frame, separate replay counter is needed if we go this route
Different key for each link of MLD similar to BIGTK and delivered with similar approach of BIGTK if different
AAD construction includes FC/RA/TA with appropriate mask similar to Beacon protection
Fields before FCS can be part of the MIC computation
Rekey can use group key handshake like BIGTK

## Slide 7: Conclusion
We discuss the consideration of reliability for wireless connectivity using Trigger frame in a BSS
We propose to have Trigger frame protection to prevent attack that drain power and resolve issues addressed by PBAC in a better way
Various design consideration under Beacon protection can be reused in Trigger frame protection

## Slide 8: Straw Poll #1
Do you support to consider Trigger frame protection in UHR?