## Slide 1: R-TWT Multi-AP Coordination
Date: 2023-05-05
Authors:

## Slide 2: Problem Statement
UHR is aiming for improving tail latency and jitter compared to 802.11be including scenarios of overlapping Basic Service Sets (BSSs)
R-TWT is a suitable candidate from 802.11be for providing enhanced medium protection and predictable latency for latency sensitive applications
Coordination among neighboring BSSs can further enhance R-TWT operation and medium protection
This document explores candidate solutions for multi-AP coordination for R-TWT

## Slide 3: Recap: R-TWT Operation in 802.11be
Uses broadcast TWT (802.11ax) signaling as baseline, with enhancements
  AP advertises R-TWT schedules via TWT element in Management frames in the BSS (e.g., Beacon, Probe response)
  Indication of R-TWT UL/DL TIDs during membership setup to identify latency sensitive traffic
Provides enhanced medium access protection and provisions for predictable latency
  R-TWT supporting STAs must end any TXOP at SP start boundary
  Optional usage of overlapping quiet intervals to limit interference from legacy (non-EHT) devices
  Prioritization of traffic belonging to R-TWT UL/DL TIDs per membership
  Spec recommends membership negotiated as Trigger-enabled for efficient medium access

## Slide 4: Next: Extending R-TWT for Multi-AP deployments in UHR
Several contributions in UHR have discussed R-TWT enhancements with multi-AP coordination
  11-23/0226r0: Coordination of R-TWT for Multi-AP Deployment, Abdel K. Ajami (Qualcomm) et.al.
  11-23/0250r0: AP coordination with R-TWT, Liwen Chu (NXP) et.al.
  11-23/0970r0: rTWT for Multi-AP, Laurent Cariou (Intel) et.al.
This contribution shares our view and introduces further discussion on this topic

## Slide 5: Extending R-TWT with Multi-AP Coordination Solution
R-TWT in 11be focuses on building the basic signaling and solution for single BSS case. It’s a first step. To scale up its effectiveness in wider deployments, we should consider tackling the problem further in multiple BSS environments
  R-TWT schedules outside of multiple or co-hosted BSSID sets are currently not advertised inside an AP’s BSS
Interference from OBSS could result in delay in medium acquisition by member R-TWT STAs from SP start time, if OBSS traffic continues into the SP, delaying delivery of latency sensitive traffic
The peer-to-peer(s) link, esp. when none of the STAs are associated with the infra-AP, also falls into this multi-BSS/OBSS scenario, and would benefit from a solution in this direction
R-TWT SPs in neighboring BSSs could overlap in time, resulting in reduced medium access efficiency. Coordination in usage of SPs will help mitigate contention and improve predictable delivery of low latency traffic

## Slide 6: R-TWT Schedule Coordination
Neighboring APs may exchange R-TWT schedule information and advertise OBSS schedules in their respective BSS
R-TWT supporting STAs in neighboring BSSs follow the R-TWT SP start time protection rule, suppressing OBSS interference
An AP may consider OBSS schedules when devising schedules in its own BSS (implementation dependent or further rules TBD)
AP coordination for allocation of resources within SPs

## Slide 7: Modes of Schedule Coordination
Two types of schedule coordination:
  OBSS schedules: Announcing schedules from OBSS for SP start time protection
    R-TWT supporting STAs end any TXOP at SP start
    Non-interfering transmissions may still happen within the BSS (spatial reuse)
AP1
STA11
AP2
STA2
STA12
DATA
BA
Trigger
AP1 announces AP2’s R-TWT schedules in its BSS in beacons
R-TWT SP start
STA12 ensures its TXOP ends at R-TWT SP start boundary
STA12 doesn’t initiate further TXOP as it defers to transmissions in BSS2
DATA
BA+DATA
BA
beacon
DATA
BA
STA11 initiates TXOP as it is not suppressed by AP2’s TX
AP1 may respond to STA11 if its inter-BSS NAV is not set
*AP1 and AP2 may exchange schedule info on the
same or different channel, or on a backhaul link
*Assuming all APs and STAs support R-TWT
R-TWT SP
AP1
AP2
STA11
STA2
STA12

## Slide 8: Modes of Schedule Coordination
Two types of schedule coordination:
  OBSS schedules: Announcing schedules from OBSS for SP start time protection
    R-TWT supporting STAs end any TXOP at SP start
    Non-interfering transmissions may still happen within the BSS (spatial reuse)
  Multi BSS schedules: APs may devise and announce coordinated schedules
    Reduces number of schedules being advertised/devised
    Schedule has the same TWT parameters (e.g., start time, duration, period) and advertised in respective BSSs
    STAs from multiple BSS may be members of this schedule (negotiated with respective APs)
    TXOP-level coordination for efficient medium access

## Slide 9: Modes of Schedule Coordination
Further thoughts on “Multi-BSS” schedules
  Having a joint schedule, which serves STAs in multiple BSS, may improve medium efficiency compared to advertising separate “OBSS schedules” where R-TWT supporting STAs have to end TXOP at start boundary of each schedule
  APs may coordinate using other features (e.g., enhanced spatial reuse) to allow multiple R-TWT scheduled STAs to be served concurrently in their respective BSSs to enhance efficiency (beyond the scope of R-TWT operation)
  AP coordination and triggered access will be key to prioritizing latency sensitive traffic delivery and reducing contention
  It may also be helpful with mobility/roaming. E.g., STA switching between APs in an ESS may remain member of the same schedule while “handed over” between APs. Any associated QoS Char IE etc. may also be retained (further signaling needed between APs)
  TXOP-level allocation within SPs can further improve STA’s power saving and devise resource allocations that closely fulfil STA’s requirements for latency sensitive traffic delivery

## Slide 10: Signaling for Schedule Information
APs may acquire schedule information in other BSSs:
  Passively: By listening to beacons from neighboring BSSs
  Actively: By sharing schedule information via a new individually addressed frame
    Frame could carry additional information about schedules helping with coordination
    Schedules may be shared and coordinated on before announcing in respective BSSs
    Could also be shared via a central management entity in ESSs
TWT element already provides basis for schedule announcement
  Restricted TWT Schedule Info field provides further info about advertised schedules
    Value 3 could be expanded to include OBSS/Multi-
    BSS schedules
    For such schedules, TWT element may carry an identifier for the originating BSS, or to identify between “OBSS” and “Multi-BSS” schedules

## Slide 11: Further thoughts on gaps in signaling
Several signaling gaps were discussed in 802.11be and deferred to next round
  TID indication in Trigger frames and BSR Control field
    Basic Trigger frame can only indicate a Preferred AC, and not directly indicate a TID for soliciting UL
    For enhanced SP coordination within BSS and OBSS to solicit UL traffic, TID indication in Trigger frames will be useful
    Similar issue with AC level buffer reporting in BSR Control
  Explicit signaling for SP management becomes necessary
    R-TWT schedules may need to be extended in case R-TWT TID traffic is not delivered within the SP
    When coordinating and managing schedules in multiple BSS, this problem becomes even more relevant and critical
    Explicit signaling helps with better schedule management (SP termination and extension)
  Enhanced support for p2p traffic
    Member STA’s p2p traffic could be provisioned via AP e.g., via enhanced TXOP sharing for more efficient medium utilization and coordination between infra and p2p link
    Signaling enhancements are needed to indicate requirements for p2p traffic and its delivery

## Slide 12: Conclusion
We introduced concepts and solutions for R-TWT schedule coordination between multiple APs in neighboring BSS to enhance R-TWT operation in UHR
Two modes/levels of schedule coordination are identified
We discuss existing and new signaling for advertisement of such schedules between APs and between AP and their associated STAs
Extending R-TWT operation for multi-AP coordination will facilitate in mitigating OBSS interference during SPs and providing predictable latency for low latency traffic