## Slide 1: KPIs for Industrial Automation Use Cases
Date: 2023-03-DD
Authors:
Name | Affiliations | Address | Phone | e-mail
Akira Kishida | NTT | 1-1, Hikarinooka Yokosuka-Shi, Kanagawa 239-0847, Japan | +81-46-859-2093 | akira.kishida.fs@hco.ntt.co.jp
Yusuke Asai | NTT |  |  | 
Yasushi Takatori | NTT |  |  | 
Kengo Nagata | NTT |  |  | 
Ryo Nagatsu | NTT |  |  | 

## Slide 2: Introduction
The SP in the January meeting confirmed that Wi-Fi business use cases such as robotics and industrial automation for industrial IoT, logistics, and smart agriculture are considered important targets for UHR amendment[1].
The number of latency bound and reliability for industrial automation use cases can be utilized for the target of the UHR PAR.
To show the advancement compared to the EHT, deterministic (periodic) and non-deterministic (sporadic) low latency traffic are important for industrial automation, and UHR should consider covering both types of QoS traffic.
This contribution discusses KPIs for industrial automation from the RTA report [2] as KPIs for consideration in the UHR PAR.

## Slide 3: Specific target numbers for KPIs in the PAR
EHT PAR includes at least one feature that realizes improved worst case latency/jitter for the “Scope of the project.”
  The target values of those metrics are not clarified and defined in the Scope of the project part.
In January discussions, the 802.11 WG chair mentioned as follows. [3]
  We have not a resolution for this topic…some resolutions are required.
  Therefore, we introduce the KPIs and the numbers of industrial automation from the RTA report for the UHR PAR.
“Given the process of establishing the program, we need the numbers. It is clear the group and the SA needs to do. Need several use cases, like some numbers to meet the VR requirements.”
(from discussions from UHR SG Jan 2023 meeting minutes)

## Slide 4: KPIs for industrial automation
The RTA report [2] introduces KPIs of Latency bound, reliability, and throughput for each industrial automation service class including AR/VR.
We could consider Class A and B applications as targets, and an indicated number of 10-1ms latency bound is worth considering for the target of the UHR PAR.
  This table defines the latency bound as the worst-case one-way latency measured at the application layer. Reliability is expressed as the percentage of packets expected to be received within the latency bound.

## Slide 5: Types of traffic of industrial automation
Use Cases in the IEC/IEEE 60802 [4] indicates industrial automation traffic type summary as shown.
Some traffic types are sporadic traffic, such as network control, alarms/events, etc.
Latency bound is an important KPI here, and the KPI for not only deterministic (periodic) but also non-deterministic (sporadic) low latency traffic should be considered for UHR.

## Slide 6: Candidate technologies proposed in UHR SG
Several contributions [5]-[14] proposed so far in the UHR SG improve latency characteristics for deterministic (periodic) and/or non-deterministic (sporadic) low latency traffic.
  Channel access enhancement (including R-TWT, triggered access) [7][9][10][11][14]
  Preemption [5][8][13]
  Multi-AP enhancement [6]
  Overhead reduction [9][12]
UHR should manage latency bound and reliability by enhancing and combining those technologies.

## Slide 7: Target number of the latency bound in the PAR
Latency bound in the wireless links is case-sensitive because it depends on the environments of Wi-Fi networks, which vary according to each use case.
The RTA report shows requirements as the numbers of latency bound and reliability for industrial automation use cases.
  We can utilize these as the target number for UHR PAR.
The UHR PAR could express the target for latency bound as follows;
  "This amendment defines at least one mode of operation capable of XXX of latency bound in industrial automation scenarios."
  According to the RTA report, requirements of Class B applications that a range of 10-1ms latency bound can be considered for the target number by the reference.
    Class B includes several use cases, such as AR/VR, remote HMI, hard real-time cyclic control, machine tools, and production lines.

## Slide 8: Summary
We introduced and discussed the target number of KPIs for industrial automation from the RTA report and the IEC/IEEE 60802 document.
Deterministic (periodic) and non-deterministic (sporadic) low latency traffic should be considered for UHR.
We could indicate the target number for the latency bound of industrial automation in the UHR PAR.

## Slide 9: SP 1
Do you agree that UHR target improvement for deterministic (periodic) and non-deterministic (sporadic) latency characteristics?
  -Yes
  -No
  -Abstain

## Slide 10: SP 2
Do you agree that the UHR PAR should have the target number for the latency bound and reliability of industrial automation?
  NOTE: Use cases of industrial automation are described in the RTA report [2].
  -Yes
  -No
  -Abstain

## Slide 11: SP 3
What industrial automation class is the most suitable for the target of the UHR PAR?
  NOTE: Industrial automation classes are described in the RTA report [2].
  -Class A only
  -Class A and B
  -Class A, B, and C
  -None of then

## Slide 12: References
[1] Akira Kishida, et al., “Considerations on UHR PAR and KPIs,” IEEE 802.11-22/1919r5
[2] Kate Meng, et al., “RTA report draft,” IEEE 802.11-18/2009r6
[3] Ross Jian Yu, “UHR SG Jan 2023 meeting minutes,” IEEE 802.11-23/0094r0
[4] Belliardi Rudy , et al., “IEC/IEEE 60802 Use Cases for Industrial Automation (TSN-IA Profile for Industrial Automation),”
[5] Wook Bong Lee, et al., “Latency Reduction Scheme for UHR,” IEEE 802.11-22/1393r0
[6] Liuming Lu, et al., “Multi-AP Coordination for Low Latency Traffic Delivery,” IEEE 802.11-22/1556r1
[7] Tongxin Shu, et al., “Requirements of Low Latency in UHR,” IEEE 802.11-22/1519r1
[8] Thomas Handte, et al., “Latency and Reliability enhancements for UHR,” IEEE 802.11-22/1880r1
[9] Dmitry Akhmetov, et al., “Challenges to achieve low latency,” IEEE 802.11-22/1926r0
[10] Ziyang Guo, et al., “Follow-up on Latency Reduction with Machine Learning Techniques,” IEEE 802.11-22/1931r1
[11] Kazi Huq, et al., “Enhanced Trigger-Based Uplink Transmission,” IEEE 802.11-22/2009r6
[12] Leonardo Lanante, “PPDU Design for Short Frames,” IEEE 802.11-22/1939r0
[13] Kiseon Ryu, et al., “Low Latency Support in UHR,” IEEE 802.11-23/0018r1
[14] Liuming Lu, et al., “Urgency-based Delivery of Latency Sensitive Traffic,” IEEE 802.11-23/0045r1
[15] Osama Aboul-Magd, “802.11 HEW SG Proposed PAR,” IEEE 802.11-14/0165r1