## Slide 1: Follow-up on TWT based Multi-AP Coordination
Date: 03-30-2023
Authors:

## Slide 2: Abstract
In this contribution, we follow up on TWT-based multi-AP coordination for UHR [1].

## Slide 3: Motivation
  Multi-AP Coordination is one of the key features that will be discussed in UHR SG and IEEE 802.11bn [2]
  Several types of multi-AP coordination have been discussed in both UHR SG and the early phase of 802.11be.
    Coordinated OFDMA
    Coordinated Beamforming
    Coordinated spatial reuse
    Joint Transmission
  Coordination among neighboring APs by sharing the clients’ wake-up pattern info can be beneficial for interference management.
    The coordinating APs can share TWT information of the STAs in their BSS and thereby provide assistance in either reducing OBSS interference or improving signal power during the TWT SP [1, 3]
    We refer to such mechanism as coordinated TWT (C-TWT).

## Slide 4: MAP TWT Coordination Modes
There can be different modes of TWT coordination—
Mode-1: Client-centric assistance
  TWT coordination can cater to specific STA to reduce its OBSS interference
  The victim STA can request the coordinating APs to assist in reducing the OBSS interference during its TWT SPs (either individual TWT or broadcast TWT)
    The request can be made to its associated AP.
      The associated AP can then share the victim STA’s TWT agreement/schedule with the coordinating AP and request to reduce interference towards the victim STA.
    Alternatively, the request can be made directly to the aggressor AP
      If the aggressor AP is within the coordinating AP set with associating AP, the aggressor AP can respect the request and reduce interference towards the victim STA.
    Within the TWT SP of the victim STA, the aggressor AP can use any conventional MAP mechanism, e.g. coordinated beamforming or joint transmission (for SINR boost)
Mode-2: Network-wide cooperation
  TWT coordination can be performed to assist a group of STAs in a BSS
  An AP can request its neighboring AP to reduce interference during TWT SPs of a B-TWT/R-TWT schedule.
  During the TWT SPs, the neighboring AP can mute its transmission (C-TDMA) or use a different channel than what the requesting AP is using.

## Slide 5: Need for MAP coordination for R-TWT
Restricted TWT is an important tool developed in 11be for low-latency traffic prioritization.
  The R-TWT supporting STAs in the BSS that are not members of an R-TWT schedule end their TXOP before an R-TWT SP corresponding to the R-TWT schedule starts (in the figure, STA1 ends TXOP before STA2’s R-TWT SP starts)
  This gives priority to AP (in trigger-based R-TWT) and R-TWT member STAs to win the contention for the R-TWT SPs.
However, the R-TWT supporting STAs in the neighboring BSS may not obey the rules to protect the R-TWT SPs of another BSS
  Transmission in the neighbor BSS may continue occupying the channel during the R-TWT SPs of the first BSS (in the figure, AP2 doesn’t end TXOP before STA2’s R-TWT SP starts)
  This OBSS interference may disrupt the latency-sensitive traffic of the R-TWT scheduled STAs.
  ** Based on the association shown in the figure in the previous slide

## Slide 6: MAP coordination for R-TWT
Coordination among neighboring APs for protecting R-TWT SPs can be beneficial for latency-sensitive applications.
  The sharing AP can request the shared AP to protect the R-TWT SPs of the sharing AP
Types for protection for OBSS R-TWT (in terms of protection-level):
  Type-1 :
    The shared AP and all its associated STAs end their TXOP before the sharing AP’s R-TWT SP
    The shared AP and all its associated STAs can’t transmit during the R-TWT SP of the sharing AP
  Type-2 :
    The shared AP and all its associated STAs end their TXOP before the sharing AP’s R-TWT SP starts
    The shared AP and all its associated STAs can start contending for the channel at the start of the sharing AP’s R-TWT SP
  Type-3:
    The shared AP ends its TXOP if it is not serving a low latency STA (e.g., serving its own R-TWT scheduled STA)
    The non-AP STAs in the shared AP’s BSS don’t end their TXOP if the TXOP has been obtained for low-latency traffic (e.g., R-TWT scheduled STA)
    Otherwise, the shared AP and all its associated STAs end TXOP before the start of the sharing AP’s R-TWT SP
    After ending the TXOP before the sharing AP’s R-TWT SP starts, the shared AP and all its associated STAs can start contending during the R-TWT SP
  Type-4:
    Only the shared AP ends its TXOP before the sharing AP’s R-TWT SP starts
    The non-AP STAs in the shared APs BSS don’t end their TXOP before the sharing AP’s R-TWT SP starts
    After ending the TXOP before the sharing AP’s R-TWT SP starts, the shared AP can start contending during the R-TWT SP
  * Note: The above rules are for R-TWT supporting STAs-only.
  ** TWT Sharing AP: The AP that has an R-TWT schedule in its BSS and initiates a TWT coordination request (e.g., AP1 in the previous slide)
  *** TWT Shared AP: The recipient of the TWT coordination request (e.g., AP2 in the previous slide)

## Slide 7: Elements of Coordinated TWT
The coordinating APs need to share their TWT information (e.g., R-TWT schedule information) to agree on whether to coordinate on TWT or not
Negotiation: There can be different types of multi-AP TWT negotiation
  Implicit MAP TWT agreement:
    The same MAP coordination cluster can be used for different types of MAP coordination mechanisms.
    If two APs fall within the same MAP coordination cluster, any mode of coordination is possible within the APs (C-OFDMA, C-SR, C-TWT, etc.).
    When the sharing AP shares a TWT schedule information with the shared AP in a coordination request, the shared AP will respect the request
    No further negotiation is needed for specific TWT coordination
  Explicit MAP TWT negotiation
    In this mode of negotiation, the sharing AP sends a TWT coordination request to the shared AP (e.g. the request may contain one or more TWT elements)
      Either using management frames or through backhaul
    The shared AP will evaluate the request (e.g. checks whether it overlaps with its own R-TWT schedule)
    The shared AP sends the TWT coordination response frame indicating acceptance, rejection, etc.
    Agreement to coordinate on another MAP mechanism (e.g. C-OFDMA, C-BF, C-SR) does not imply agreement to coordinate on C-TWT.
Announcement: Shared AP’s action
  If the shared AP accepts the TWT coordination request, then it advertises the same R-TWT schedule in its own BSS (MAP TSF synchronization needed)
  Handling Fairness:
    There can be separate priority labels tagged with this advertisement (e.g. indicating that this is an OBSS request)
    Can indicate which channel and bandwidth to use during the RTWT SP
    Can indicate which SP(s) in the sequence of SPs need to be respected.

## Slide 8: Summary
Multi-AP coordination can be an enabling technology for next-generation WLAN systems
In this presentation, we highlight the aspects of TWT-based multi-AP coordination for UHR.

## Slide 9: References
[1] IEEE 802.11-22/1530r1, “Multi-AP coordination for next-generation Wi-Fi”, Sept 2022.
[2] IEEE 802.11-22/932r0, “Thoughts on Beyond 802.11be”, July 2022.
[3] IEEE 802.11-22/1046r3, “Multi-AP: TWT Information Sharing”, Sept 2021.