## Slide 1: Discussion on Multi-AP Coordination
Date: 2023-03-11
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on the architecture needed for multi-AP operations, including various coordination operations as well as roaming support, and general MLD operation support.

## Slide 3: Introduction
Multi-AP has been proposed as a UHR feature, including coordinated operations such as
  Coordinated OFDMA/beamforming
  Coordinated rTWT/TWT
  Joint transmission
  Coordinated spatial reuse
These multi-AP operations involve APs that are not co-located
Seamless roaming support has also been proposed for UHR [1][2][3][4]
  Seamless roaming support also involves APs that are not co-located
  Seamless roaming support can be easily viewed as a coordinated multi-AP operation
It would be beneficial to have one architecture setup for all multi-AP operations including roaming as well as for general MLD operations
  An architecture for roaming support only, for example, may be too limiting
In this contribution, we want to look at the multi-AP architecture from a general multi-AP coordination point of view

## Slide 4: Seamless roaming discussions
  Two architectures for seamless roaming have been proposed by previous contributions [1][2][3][4]:
    Option 1: individual APs that are affiliated with a mobility domain MLD, with the MLD potentially implemented in the DS or with one of the APs [1][2]
      APs that are not co-located are affiliated with the same MLD
    Option 2: AP MLDs containing co-located APs while there is an over-arching logical entity (e.g., a roaming AP MLD) that may provide smooth roaming [3]
      Co-located APs are affiliated with an AP MLD, while the various AP MLDs that are not co-located share an over-arching roaming AP MLD
  In this contribution, we want to look at the pros and cons for both options

## Slide 5: Seamless roaming architecture discussions (1)
  Option 1: individual APs that are affiliated with a mobility domain AP MLD, with the MLD potentially implemented in the DS or with one of the APs
    Pro:
      Can support roaming
      No need to define additional logical entities
    Con:
      May not be able to support 11be-level MLD functions
        Limited number of links
        Changes and reconfigurations potentially require more delay since MLD functionality may be implemented elsewhere
      May not be able to support association for EHT non-AP MLDs [4]
    Not clear whether the mobility domain AP MLD is the same logical entity that provides regular service to non-AP MLDs, or just for roaming

## Slide 6: Seamless roaming architecture discussions (2)
  Option 2: AP MLDs containing co-located APs while there is an over-arching logical entity (e.g., a roaming AP MLD) that may provide smooth roaming [3]
    Pro:
      Can support roaming
      Can support 11be-level MLD functions
      Can support association for EHT non-AP MLD
      Limited changes need to be defined for general AP MLD operations
    Con:
      Need to define additional signaling and logical entity that is the over-arching roaming MLD
    In addition, roaming AP MLD should be transparent to UHR non-AP MLDs for easy discovery of roaming candidates

## Slide 7: Seamless roaming architecture discussions (3)
  In addition, it is beneficial to evaluate the two options from general multi-AP operations perspective
  Option 1: individual APs that are affiliated with a mobility domain AP MLD, with the MLD potentially implemented in the DS or with one of the APs
    Not clear whether this architecture is sufficient to support other multi-AP coordination, or it is just for roaming
    Need to define mechanisms for multi-AP coordination
  Option 2: AP MLDs containing co-located APs while there is an over-arching logical entity (e.g., a roaming AP MLD) that may provide smooth roaming [3]
    Can provides all 11be AP MLD functionalities
    Need to define additional signaling to support multi-AP coordination, but in our opinion, it is a more natural architecture for coordination between AP MLDs
    May be reused for support multi-AP operations for 11be AP MLDs using software update

## Slide 8: Conclusions
  Two architectures for seamless roaming have been proposed by previous contributions [1][2][3]:
    Option 1: individual APs that are affiliated with a mobility domain MLD, with the MLD potentially implemented in the DS or with one of the APs [1][2]
    Option 2: AP MLDs containing co-located APs while there is an over-arching logical entity (e.g., a roaming AP MLD) that may provide smooth roaming [3]
  In this contribution, we looked at the pros and cons for both options
    From the perspective of seamless roaming support
    From the perspective of general multi-AP operations
    From the perspective of general MLD operation support
  Option 2 provides an architecture that is better for general multi-AP operations including seamless roaming support

## Slide 9
References
[1] 11-22/1910r3, Seamless Roaming for UHR, Duncan Ho
[2] 11-23/237, Considerations on Seamless Roaming, Insun Jang
[3] 11-23/0170, Smooth Roaming, Liwen Chu
[4] 11-23/231, Thoughts on Seamless Roaming Under Non-collocated AP MLD Architecture, Guoguang Huang
[5] 11-23/324, Roaming Requirements, Brian Hart