## Slide 1: Improved reliability in presence of interference or other device activities
Date: 2023-04-06
Authors:

## Slide 2: In-device coexistence issue
In device coexistence with Bluetooth (BT) has always been an issue.
  So far, this was contained in the 2.4 GHz band only.
  BT will now be able to operate at both 5 and 6 GHz, which makes the problem bigger than it was before.
  EU Regulatory is already in process of enabling Bluetooth, ZigBee and BLE operation in 5 and 6 GHz band.
There are other sources of interference
  other wireless technologies
  with multi-link operation, we have other sorts of interference that can arise, and that may be sometimes difficult to predict.
    Multilink NSTR operation is a good example where a transmission on one link by a STA of a non-AP MLD may impact the reception of a collocated STA of the same non-AP MLD by generating some cross-link interference, …
  In-device coexistence (spurs, modulation between components, …)

## Slide 3: Other activities
A STA can be associated to an infrastructure AP and have P2P or mobile AP operation at the same time, …
Such STA typically needs to multiplex in time its operation for infrastructure AP and for P2P
  A STA currently uses power mode changes with infra AP in order to signal unavailabilities (very inefficient)
  Negotiation of TWT SP operation could help, but difficult to describe properly the client constraints, which makes negotiation difficult or impossible
Lack of a clear mechanism for a STA to inform an infrastructure AP of its constraints for P2P operation, especially a clear indication of a Service Period or Period of Time during which the STA shall be considered as in doze state and unavailable

## Slide 4: Predictable/unpredictable interference
1 Some interference may be predictable
  For such interference, tools are needed in order to define properly the period during which the interference occurs, and possibly characterize the interference
    Some BT can be scheduled in some cases
2 Other interference are difficult to predict long in advance
  This is often the case for BT interference
  We therefore need solutions in order to react properly when interference occurs, and not have reactions that impact even more a Wi-Fi connection.
3 Other possible interference situation
  Some interference are in the middle
    For instance, periodicity for interference period is known, but interference may not always occur during such period

## Slide 5: Interference impact
Obviously, when interference occurs, it impacts ongoing transmissions/receptions
  Reducing SINR if interference occurs during reception, often leading to packet losses
  Or forcing unavailability of the STA with very short notice
    Stopping ongoing transmission if priority is given within the device for another wireless technology, …
Double punishment:
  When interference occurs to a received PPDU and causes packet losses, not only can some packets be lost, but the rate selection mechanisms on the transmitter side may get adjusted to lower the rate of subsequent transmissions, as the transmitter does not know that the packet losses was not due to the channel conditions but was due to unexpected and infrequent interference.

## Slide 6: Proposals for 1) predictable interference and other predictable activities on client side
Need a tool to inform the AP of SPs during which the STA is unavailable because of in-device coexistence, or because it is performing other functions (scanning, P2P, …) *
  Need a tool so that the STA can inform the AP of when these period will happen, and whether they are periodic or not
  During these periods, the AP shall consider the STA in doze state
*Also a very useful tool to ensure that a regular infrastructure AP that wants to do power save will efficiently select its power save inactivities
As described previously, in some situations, the interference will impact only some frequencies (only some subcarriers) and either during a restricted time or possibly all the time (spurs, …)
  Need to be able to report interference on a specific frequency zone (RU for instance)
  In such case, normative behavior on AP side would then be similar to the following:
    AP shall apply a static puncturing specifically for operation with the STA
    AP shall assign to the STA only RUs that don’t overlap with this interfered region

## Slide 7: Proposals for 1) predictable interference and other predictable activities on client side
Define a new signaling for such interference/unavailability reporting
Or reuse and enhance existing tools and make it mandatory
  Colocated Interference Report element
    Provides most of the needed signaling for reporting interference
    Misses the normative behavior on AP side (consider STA in doze state): easy to add
  Reusing TWT is less straightforward and TWT already complex: STA sends unsolicited TWT Response frame, including a TWT element describing the service period(s) with an explicit indication (e.g. Responder PM) that the STA will be unavailable during that SP (reverse concept than today), and ensure that no other TWT rules would apply.

## Slide 8: Proposals for 2) unpredictable interference
a) Add signaling in BA in case of unexpected interference to ensure no double punishment (explained before)
b) Shortening/truncation of a TxOP due to upcoming interference, as a TxOP responder or TxOP holder

## Slide 9: 2) a) Rate selection in case of interference
We propose to add a signaling indication in a BlockAck frame that is sent (by a responder) as immediate response to a PPDU transmission (sent by an initiator) in order to indicate to the initiator of the PPDU that the PPDU reception suffered from an unusual interference, which was the main cause of packet losses.
  Could be a simple 1-bit field to indicate that the PPDU reception suffered from interference or not or it could be more advanced to locate more accurately the interference impact if needed
Expected behavior: Initiator will not take into account statistics of this PPDU for updating its rate selection algorithm
  Note that this could fit in the more general Link adaptation mechanism (rate selection based on feedbacks in the BA) if we define one in UHR

## Slide 10: 2) a) Rate selection in case of interference
Continued..
If the transmitter already dropped the rate, it would also be good to have a way to bring the rate back up
  This can be a complementary signaling to specifically ask to go back to immediately preceding rate
  As mentioned in previous slide, this can fit in a more general link adaptation mechanism in BA, such as a simple tool to ask to go up one rate, go down one rate, or keep current rate…

## Slide 11: 2) b) TxOP shortening/truncation
Define a mechanism so that a recipient of a PPDU transmission can indicate, at the beginning of the TxOP that it will be available only until a specific point in time, and not after because it knows an interferer will be present at that time
  Max availability period indication in CTS frame, using signaling equivalent to Dynamic Bandwidth negotiation or alternatively using the Duration field by modifying the duration field setting rules or as an A-ctrl feedback similarly to BQR feedback
  Similar feedback can be provided in a BA frame during a TxOP for completeness

## Slide 12: 2) b) TxOP shortening/truncation
PPDUs could also be shortened/truncated:
  If we define a preemption mechanism (see other discussions), we can use it so that initiator and even a responder can terminate early a PPDU in case of sudden interference or decision to prioritize another wireless technology
example with preemption period between PPDUs
1 ms
1 ms
1 ms
1 ms
Full contention
period
Preemption period/pause
BA
1 ms
1 ms
Full contention
period
BA
Initiator terminates early (TS: termination signal (could be a CF-end))
Indication needed for BA, if needed
Interference
Time Initiator is aware of
incoming interference
TS

## Slide 13: Conclusion
UHR is the opportunity to improve reliability in presence of interference or other device activities
We propose several solutions, for predictable or unpredictable interferences/activities
  Long term indication of periodic service periods during which a STA shall be considered in doze
  Signaling in BA in case of unexpected interference to ensure no double punishment (unfavorable rate adaptation)
  Shortening/truncation of a TxOP due to upcoming interference, as a TxOP responder or TxOP holder