## Slide 1: Improve Roaming between MLDs
Date: 2023-03-07
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Daniel F Bravo |  |  |  | 
Ido Ouzieli |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Goal of UHR:
  The Study Group will investigate technology which may improve reliability of WLAN connectivity, reduce latencies, increase manageability, increase throughput including at different SNR levels, and reduce device level power consumption.
We discuss how to improve roaming between MLDs to reduce latencies and increase manageability

## Slide 3: How can we improve roaming between MLDs?
Existing roaming procedure:
  Authentication
  Association
  Key negotiation
  DS starts to forward data for transmission
  Frame exchange to do various setup
There are existing methods to optimize some of the steps, but there are no existing methods to allow data continuity, i.e., without the need to flush data and restart
To improve roaming, believe that the trend is to allow data continuity and continue to optimize the steps
  We discuss the critical design consideration of data continuity in this presentation.
Current AP MLD
Target AP MLD
Roam

## Slide 4: Caveat on the design
There have been naming discussion on the framework
  To start, two AP MLDs are required for legacy compatibility with EHT. Hence, can not simply merge existing AP MLDs
  EHT AP MLD requirements like STR, group addressed SN assignment and TSF requirements, etc will not work among two non-collocated AP MLDs and will not scall to all AP MLDs (100?) in an enterprise network
  Existing MLD framework can not be used without change.
If we just discuss required functionalities, we need a new framework with right design of requirements that allow data continuity and control interactions among multiple AP MLDs to improve roaming.
Current AP MLD
Target AP MLD
????

## Slide 5: Data continuity consideration
Unlike collocated APs for AP MLD, where received reordering buffer can be implemented locally within the AP MLD, there is a question on where to keep the received reordering buffer
  A cloud based received reordering buffer needs a lot of memory to keep the buffer for every non-AP MLD connects to the new framework
  In practice, the receive reordering buffer will be in the edge like today, i.e., in either Current AP MLD or Target AP MLD. However, having transmission on both Current AP MLD and Target AP MLD means parameter sync and/or a potential long delay depending on the backhaul
For simplicity, we consider all TIDs transmission in one AP MLD as a starting point, which does not need any instantaneous parameter sync
Current AP MLD
Target AP MLD
Central Receive reordering buffer
Current AP MLD
Target AP MLD
Central Receive reordering buffer
Non-AP MLD

## Slide 6: Data continuity consideration
For simplicity, we focus on transmission and operation to either current AP MLD or target AP MLD as a starting point, which does not need any instantaneous parameter sync
Realistic consideration and should be the first basic mode to be considered
Current AP MLD
Target AP MLD
Central Receive reordering buffer
Non-AP MLD
Target AP MLD
Current AP MLD
Central Receive reordering buffer
Non-AP MLD
Roam

## Slide 7: Data transfer consideration
To achieve the basic mode, data needs to be duplicated and transferred from current AP MLD to target AP MLD before roaming
  Duplicate data is a heavy requirement
    Do not want to duplicate data to all other AP MLDs by default
    Need non-AP MLD to indicate when this is really needed to start the duplicate and transfer
  There can be optimization like transferring high priority TID first or pipeline operation, but this should be left for implementation specific consideration (spec does not define scheduling algorithm)
  When client wants to roam, client roams even when the data transfer is not finished and do not need to wait for a defined finish point
Required functionalities:
  Have a method for a non-AP MLD to indicate that current AP MLD starts duplicate data transfer to target AP MLD
  Define contexts that can be preserved between MLDs
  Have a method for a non-AP MLD to switch data transmission and operation from current AP MLD to target AP MLD
Current AP MLD
Target AP MLD
Current AP MLD
Target AP MLD
Non-AP MLD
Non-AP MLD
Current AP MLD
Target AP MLD
Non-AP MLD
Roam and continue transfer
Start transfer

## Slide 8: Conclusion
We discuss how to improve roaming between MLDs by designing mechanisms to allow data continuity
  A new framework with right design of requirements that control interactions between AP MLDs is required to achieve data continuity
We note that the proposed mechanism improves roaming but may not guarantee specific latency requirement for roaming like withing xxx milliseconds
  Exact performance depends heavily on backhaul capability (wireless/ethernet/fiber), roaming speed (client runs or walks), and scheduling algorithms to duplicate data
The proposals introduce tools to improve roaming and have lossless operation (always) and seamless operation (when possible)

## Slide 9: Straw Poll
Do you support to define a framework that controls interaction among multiple AP MLDs to improve non-AP MLD roaming between AP MLDs?