## Slide 1: Coordinated Spatial Reuse for UHR
Date: 2023-03-07
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Ross Jian Yu |  |  |  | 

## Slide 2: Introduction
Multi-AP coordination has been extensively discussed in TGbe, as well as EHT SG.
Many modes of multi-AP coordination have been proposed and analyzed, including:
  Joint transmission (JT) ; Coordinated Beamforming (co-BF) ; Coordinated UL MU MIMO (co-UL-MU-MIMO) ; Coordinated Spatial Reuse (co-SR) ; Coordinated OFDMA (co-OFDMA), Coordinated TDMA (co-TDMA)
Moreover, several motions have passed in TGbe, aiming to define the above modes [1].
However, due to the introduction of MLO in MAC, and 320MHz+4K QAM in PHY, the PAR of EHT can be satisfied already, making Multi-AP coordination a good candidate for the next generation, which can be seen from the long contribution list in UHR on this feature [2-15].

## Slide 3: Co-SR Recap (1)
Among all the modes in Multi-AP coordination, we focus on co-SR in this contribution.
The basic operations of co-SR is illustrated in the figure below:
  After successfully contending the channel, the sharing AP can initiate the co-SR transmission by sending a co-SR Trigger frame.
  The sharing AP and the shared APs use the same channel for data transmission at the same time.
Co-SR Trigger Frame
AP1
(sharing AP)
DL Data Frame (or basic TF)
DL Data Frame (or basic TF)
BA (or UL Data Frame)
BA (or UL Data Frame)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
(BA)
(BA)

## Slide 4: Co-SR Recap (2)
One of the reasons that we focus on co-SR is that it is a natural extension to the existing spatial reuse (SR) scheme defined in TGax
SR is defined as a distributed channel access scheme, where the interference to the ongoing transmission is not controllable
Comparatively, co-SR can control the interference to the primary transmission by choosing the appropriate shared AP, and the corresponding TX power.
ongoing transmission
-72dBm
-82dBm
SR transmitter in this region will cause more interference
SR transmitter in this region will cause less interference

## Slide 5: Co-SR Recap (3)
Another reason that we focus on co-SR is that it provides a nice balance between performance gain and implementation complexity
Comparing with co-OFDMA co-TDMA, it increases throughput and decreases delay, but the latter can not provide throughput gain
Comparing with JT and co-BF, it doesn’t need the multi-AP sounding procedure, resulting in less overhead and implementation complexity.

## Slide 6: Performance gain
Some simulation level performance gain is illustrated in [16-18] [9]
Besides, we also built a hardware demo to test the actual performance of co-SR
Settings:
  AP number: 2
  Inter-AP distance: 22m
  AP TX power: 15dBm
  Non-AP STA number: 3 per AP
  BW: 40MHz
  NSS per non-AP STA: 2
  Traffic: DL full buffer (UDP)
  Test duration: 5min
  Non-AP STA placement:
    case1 – near to the AP ;
    case2 – medium distance to the AP
 | Average SINR | Co-SR off/on | Test 1 | Test 2 | Test 3 | Average | Throughput Gain
Case 1 | 33.8dB | off | 473 | 476 | 476 | 475 | 
 |  | on | 598 | 608 | 604 | 603.33 | 27.02%
Case 2 | 25.2dB | off | 388 | 390 | 384 | 387.33 | 
 |  | on | 455 | 462 | 455 | 457.33 | 18.07%
Unit: MBps

## Slide 7: Conclusion
We suggest that the TG for UHR should define co-SR
Hardware test results show that the throughput gain of co-SR can be up to 27%

## Slide 8: References
[1] 11-20-1935-66-00be-Compendium of straw polls and potential changes to the Specification Framework Document - Part 2
[2] 11-22-1512-00-0uhr-Multi-AP Coordination for UHR
[3] 11-22-1515-00-0uhr-A candidate feature: Multi-AP
[4] 11-22-1516-00-0uhr-Considerations on Multi-AP Coordination
[5] 11-22-1567-00-0uhr-C-OFDMA throughput analysis in various mesh backhaul scenarios
[6] 11-22-1530-00-0uhr-Multi AP coordination for next-generation Wi-Fi
[7] 11-22-1556-00-0uhr-Multi-AP Coordination for Low Latency Traffic Delivery
[8] 11-22-1394-00-0uhr-Virtual BSS And Multi AP Transmissions
[9] 11-22-1822-00-0uhr-Recap on Coordinated Spatial Reuse Operation
[10] 11-22-1895-00-0uhr-Thoughts on M-AP Coordination Principles
[11] 11-22-1899-00-0uhr-Multi-AP Operation for Low Latency Traffic Delivery - Follow up
[12] 11-22-1821-00-0uhr-System Level Simulation of Co-BF and Joint Tx
[13] 11-22-2188-00-0uhr-Joint Transmission for UHR -A Refresher and New Results
[14] 11-23-0041-00-0uhr-Considerations on Coordinated TDMA
[15] 11-23-0058-00-0uhr-Spatial Reuse in Coordinated M-AP for UHR
[16] 11-19-0103-01-0eht-ap-coordination-in-eht
[17] 11-20-0576-01-00be-coordinated-spatial-reuse-protocol
[18] 11-20-0107-01-00be-multi-ap-coordination-for-spatial-reuse