## Slide 1
Proposal for MLD OTA MAC Change
Date: 2023-03-08
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission presents ideas on OTA MAC Address change while a STA is associated for MLD STAs

## Slide 3: Summary
For MLDs, changing the increment used for sequence numbers and packet numbers would simplify the ability to change OTA MAC addresses. If that increment change was implemented generally, it would also simplify MAC change actions since SN/PN changes would no longer need to be tied to the MAC changes.

## Slide 4: Requirements
The following requirements all deal with changing a STA’s OTA MAC address.
6 | 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP.
7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection.
8 | 11bi shall define a mechanism for a CPE AP to initiate changing the OTA MAC Addresses of a set of associated CPE Client’s in the BSS (those CPE Clients in Associate STA State 4) without any loss of connection.
12 | 11bi shall define a mechanism for a CPE Client and CPE AP to establish the CPE Client’s DS MAC Address without the CPE Client’s DS MAC Address being transmitted in the clear.
39 | 11bi shall define a mechanism for a BPE AP and a BPE Client to change the OTA MAC addresses, SN and PN they use for unicast transmissions.

## Slide 5: Thoughts on MLO and MAC change
Ideally, since the individual affiliated STAs use their own MAC addresses (35.3.2), a MAC transition event within an MLD should be able to proceed within each affiliated AP independently. The only complication is that the AP MLD sets the SN/PN for each flow.
Theoretically, even if the affiliated STAs all change their addresses, the new address will be linked to the old one by the SN/PN unless that is changed as well.
MPDU Header creation
PHY –
scrambler
A-MPDU- aggregation
SN assignment
PN assignment
MPDU encryption
MPDU Header creation
PHY –
scrambler
A-MPDU- aggregation
MLD Upper Layer MAC –
Per AP MLD
Lower MAC –
Per Affiliated AP-STA

## Slide 6: Alternatives for MLD OTA MAC address change during association
Because the SN/PN are changed at the upper MAC level of an AP MLD, all the queues across the entire MLD would need to be flushed to ensure a safe transition. This could cause an unreasonable amount of delay for some packets/flows if one or more of the links either have excessive traffic or large amounts of retransmissions.
Alternatively, the scheme for incrementing SN/PN could be changed to use a random increment so that the sequence would not be simple to link between before and after the OTA MAC addresses changed.
For example,
  @SN(n+1) = PRF-128/46(PMK, “sequence”, @SN(n), 128)
  Where the PMK is the current Pairwise Master Key
  Chunks of 12 bits are used for the OTA sequence number beginning with the left most 12 bits, then the next 12 bits (13-24), etc.
  Using a randomized sequence number would allow each affiliated AP to manage its OTA MAC rotation independently.

## Slide 7: MAC generation for MLD
Within an MLD the same PMK is used for all of the links, but each link uses a separate MAC address in its unicast transmissions.
Since a single PMK is available, the following is proposed for MLO:
@PairMAC (n+1) = PRF-128/46(PMK, “concatenate(“PairMAC”,STA-MAC), @PairMAC(n), 128)
Where the PMK is the current Pairwise Master Key
Where the text string is a concatenation of the affiliated STA for that link’s original MAC address and the string “PairMAC”
The leftmost 46 bits are selected for SA MAC used to TX from an affiliated non-AP STA
The next 46 bits are selected for the DA MAC used for traffic to the same affiliated non-AP STA.
Alternatively,
@SMAC (n+1) = PRF-128/46(PMK, concatenate(“SMAC”,STA-MAC), @SMAC(n), 128)
@DMAC (n+1) = PRF-128/46(PMK, concatenate(“DMAC”,STA-MAC), @DMAC(n), 128)
Where the PMK is the current Pairwise Master Key used for the AP-MLD
Where the text string is a concatenation of the affiliated STA for that link’s original MAC address and the string “SMAC” or “DMAC”
The leftmost 46 bits are selected for each MAC (SMAC to mark traffic TX from a non-AP STA, DMAC used to mark traffic TX to the same non-AP STA).
Using an existing key avoids additional messaging exchanges.
Changing the SA and DA MACs separately removes the linkage between DS and US traffic.

## Slide 8: Straw Poll 2
Is the group interested in text to change the increments of sequence numbers and packet numbers for at least MLDs from +1 to +/- random amount, subject only to a lack of repeat numbers within 10 frames?

## Slide 9: References
11-22/114r3 – Enhanced Random and Changing MAC Address