## Slide 1: Enhanced Security Discussion
Date: 2023-02-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Security in 802.11
The unicast Data/Management frames can be protected through PTK.
The broadcast Data frames can be protected by GTK.
The broadcast Management frames can be protected by IGTK.
The Beacon frames can be protected by BIGTK.
The PBA is proposed to further give protection to BA agreement
  Some potential issues need to be addressed.

## Slide 3: Control Frame Protection
Same as Data/Management frame, there are unicast Control frames, broadcast Control frames.
If the protection is applied to Control frames, both unicast and broadcast frames should be protected.
  The unicast Control frames and broadcast Control frames should use the different keys, CPTK, CGTK.
Under MLO, the CGTK should be per link key.
Under MLO, the CPTK should be per link key.

## Slide 4: Protected Control Frame
The different methods can be considered for protected Control frames
  Option 1: Reuse the current control subtype
    The carrying of PN, Key ID, MIC should be designed carefully so that the non-UHR devices are not be confused.
      For Control frame with per STA field, the PN, Key ID, MIC can be carried in the Per STA fields with specific AID value, (User Info field in Trigger frame, Per STA field in NDPA, Per AID TID Info field in Mul-STA BA)
      The optimization could be no explicit transmission of MIC, e.g. by using the similar method of 11ba.
      The design is kind of ugly since many per STA fields are needed.
      The method is difficult for unicast frame.
  Option 2: define the new control subtype for protected control frame

## Slide 5: PBA Enhancement
Once the MU BAR, BAR is protected, the PBA can use the protected MU BAR, BAR to adjust the scoreboard context and reorder buffer.
  The protected ADDBA Request is not needed.
However a 3rd-party device can still use the Data frame to let the BA agreement recipient to adjust its scoreboard context and reorder buffer, the reason is that the replay check is done after the reorder buffer.
The solution could be to allow the decryption and replay check before the BA creation, SN protection.

## Slide 6: Additional Processing Time Before the Responding
The SIFS may not be enough for some device to provide the protected response with SIFS inter-frame space.
In order to address this, the transmitter of the protected responder can announce the padding requirement.
  The transmitter of the soliciting frame needs to add the padding, e.g. MPDU delimiters, padding fields, to guarantee the padding requirement of the transmitter of the responder.

## Slide 7: Summary
The methods to further improve the security of 802.11 are discussed.
  Unicast Control frame protection,
  Broadcast Control frame protection,
  BA agreement protection.
It is not an easy work to further improve the security of 802.11