## Slide 1: Enhanced rTWT and Multiple AP Operations
Date: 2023-05-01
Authors:

## Slide 2
Abstract
Three levels of MAP coordination in rTWT are discussed
  rTWT protection from OBSS transmissions.
  Coordinated MAP transmissions on overlapping rTWT SPs.
  rTWT Schedules allowing OBSS STAs to participate.
Mechanisms are considered to enable MAP rTWT transmissions
  Buffer status report.

## Slide 3
Introduction
rTWT has been introduced in 802.11be to provide a mechanism for low latency transmissions. A protection mechanism which ensures the rTWT supporting STAs in the BSS to terminate their TXOPs/transmissions before a rTWT service period (SP) was introduced.
Multi-AP (MAP) operations may benefit from such a scheduling mechanism.
In this contribution, we discuss several design considerations for rTWT enhancement when MAP operation is considered.

## Slide 4
rTWT Protection from OBSS Transmissions
Different rTWT protection methods were discussed in UHR:
  In [1], two levels of coordinated medium access were proposed.
    Level 1 ensures APs to end their TXOP before the other APs coordinated transmission.
    Level 2 ensures APs/STAs to end their TXOP before the other APs coordinated transmission.
  In [2][3][5], an AP advertises an OBSS rTWT SP to protect an existing rTWT SP from another AP.
  In [6], different types of MAP coordination, e.g. depending on if shared AP and associated STAs end their TXOP before rTWT SPs, are discussed.

## Slide 5
rTWT Protection from OBSS Transmissions
One problem of OBSS rTWT protection is that BSSs are not synchronized.
  OBSS STAs may not have the same TSF value to obey the rTWT protection.
Methods proposed in [1][2][3][5] may solve this issue with extra overhead in Beacon or other management frames.
  rTWT protection of only OBSS AP transmissions requires less overhead than that of both OBSS AP and STA transmissions.
In addition, overlapping rTWT SPs may not always be bad.
  Multi-AP coordination may be possible for overlapping rTWT SPs to achieve more efficient spectrum usage.
  It may be better to allow APs to determine if it allows overlapping transmissions.
It is beneficial to allow APs to indicate whether
  Its rTWT SP is under OBSS rTWT protection (i.e., not allowing OBSS transmissions).
  It is willing to respect OBSS rTWT protection from other APs.

## Slide 6
Coordinated MAP Transmissions on Overlapping rTWT SPs
Coordinated MAP transmissions on overlapping rTWT were discussed [1-5].
Different rTWT schedules may be with different SP periodicities.
  Thus, if a rTWT schedule is established without considering MAP coordination, some rTWT SPs of the schedule may overlap with other rTWT schedule(s) and the rest may not.
Two different MAP coordination schemes for rTWT transmissions may be considered:
  Option 1 (rTWT schedule level coordination): Establish MAP coordinated rTWT schedules so that all rTWT SPs in the rTWT schedule are overlapping or non-overlapping.
  Option 2 (rTWT SP level coordination): Establish rTWT schedule without considering MAP coordination. The APs announce to its associated STAs if coordinated MAP transmissions (e.g., C-SR, C-OFDMA, etc.) happen for overlapping rTWT SPs.

## Slide 7
rTWT Schedules Allowing OBSS STAs to Participate
We may further consider to allow OBSS STAs to participate in a rTWT schedule.
Use case:
  An OBSS STA with low latency traffic may not be able to participate in rTWT schedules from its associated AP.
  A STA is roaming from one AP to another.
Design considerations:
  Need a MAP architecture to enable this.

## Slide 8: Buffer Status
TXOP sharing, allowing an AP to share the TXOP with a STA for UL/P2P transmission, is supported in rTWT in 802.11be.
Some contributions suggested extending the idea to allow TXOP sharing with an AP.
A r-TWT scheduling AP should know the buffer status of the r-TWT scheduled AP/STA to share a time slot with it.
  TID related buffer status is preferred since rTWT is using DL/UL TID to prioritize the latency sensitive traffic.
  P2P related buffer status is preferred to allow the AP to perform Triggered TXOP Sharing Mode 2.
  Aggregated AP buffer status is needed when coordinated MAP transmission is considered.
Reconsider contributions in 802.11be or new solutions to address this issue.

## Slide 9
Summary
rTWT protection from OBSS transmissions should be considered to better support low latency transmissions.
Coordinated MAP transmissions on overlapping rTWT SPs improves the channel usage.
rTWT Schedules allowing OBSS STAs to participate could further benefit the low latency traffic delivery.
Updated buffer status report is needed to better support rTWT operation.

## Slide 10: References
IEEE 802.11-23/0226, Coordination of R-TWT for Multi-AP Deployment
IEEE 802.11-23/0297, R-TWT for Multi-AP
IEEE 802.11-23/0250, AP Coordination with rTWT
IEEE 802.11-23/0046, Multi-AP Coordination for Low Latency Traffic Delivery: Usage Scenarios and potential features
IEEE 802.11-23/0291, R-TWT Multi-AP Coordination
IEEE 802.11-23/0291, Follow-up on TWT-based Multi-AP Coordination