## Slide 1: Enhanced Scheduling Method for Low Latency Traffic
Date: 2023-05-16
Authors:

## Slide 2: Introduction
“Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs” is one of the main targets for enhancing reliability in P802.11bn [1]
UHR contributions on latency so far can be categorized under
  Multi-AP operation [2 - 4]
  PPDU design [5 - 6]
  Frame overhead reduction [7 - 8]
  Latency improvement by AI/ML [9 - 10]
  Preemption/Scheduling [11 - 14]
In this contribution, we consider scheduling methods for low latency traffic

## Slide 3: Support for LL Traffic
Deterministic low latency traffic
  Periodic patterns with burst arrival of packets in each interval
  Can be supported by R-TWT and SCS in 11be
    If an R-TWT scheduling AP has established SCS stream(s) described by QoS Characteristics element(s) with an R-TWT scheduled STA whose TID and Direction fields match an R-TWT TID and its specified direction for an R-TWT schedule established with the R-TWT scheduled STA, the AP should follow the rules specified in 35.17 (EHT SCS procedure) for scheduling of downlink or uplink QoS Data frames
Event-based low latency traffic
  Non-periodic, unpredictable patterns, traffic dynamically changing
  Hard to schedule by AP
  May not be supported by existing 11be procedures (e.g., R-TWT, SCS)
  Preemption and event-based scheduling methods needed

## Slide 4: Handling Event-based LL Data
For deterministic latency sensitive traffic, SCS procedure is negotiated. Based on the SCS procedure, AP may use the QoS parameters (e.g., delay bound, user priority, etc.) to schedule the traffic
For event-based latency sensitive traffic, STA may send a BSR to the AP for a Triggered TXOP Sharing. However, AP may not immediately schedule the STA for the Triggered TXOP Sharing as the AP may not know how urgent the traffic is
For more efficient scheduling of the event-based latency sensitive traffic, we introduce a new scheduling method consisting of requesting an urgent TXOP sharing in UHR

## Slide 5: Existing Procedure
AP
STA1
STA2
BSR
MRTT (STA1)
CTS
PPDU
BA
Event-based LL traffic occurs
Long delay
STA may send a BSR to the AP, where the AP may not be aware of the new latency sensitive traffic parameters
Instead of the requesting STA, AP may allocate resources to other STAs that have already reported their QoS parameters by SCS procedures
As a result, the latency sensitive traffic of the requesting STA may be delayed
MU-RTS TXS Trigger (MRTT) (allocation to other STAs)

## Slide 6: Proposed Approach
Since AC/TID-based scheduling may not be appropriate for event-based low latency traffic, the level of urgency may be transmitted by the STA to the AP [13]
  Determining which frames are “more urgent” should be further discussed
Request for urgent packet transmission may be transmitted by the STA
Additionally, QoS Characteristics element information regarding new urgent traffic and BSR information may be transmitted in the same frame
AP may accept/reject the request for urgent packet transmission
AP may update the QoS Characteristics element information and allocate STA for TXOP (instead of the SCS request/response frame exchange)

## Slide 7: Proposed Procedure
AP
STA1
CTS
PPDU
BA
Time allocated by MRTT
MRTT
STA2
Frame(Urgent
TX Request)
The request frame may comprise a request for urgent packet transmission, updated QoS Characteristics element information and BSR information
Upon receiving the frame, AP may accept/reject the request
Event-based LL traffic occurs. STA1 has to send data frames immediately
Latency sensitive data to be transmitted by this time
(No negotiation for QoS parameters)
Data TXed on time
ACCEPT
(Accept OR Reject by AP)

## Slide 8: Proposed Procedure
Alternatively, AP may not accept the request for urgent packet transmission, but may still update the QoS Characteristics element information
  E.g., when the urgent data transmission may not be completed within the delay bound due to another urgent STA allocation
Latency sensitive data to be transmitted by this time
Data TX is not permitted
(No negotiation for QoS parameters)
AP
STA1
CTS
PPDU
(STA3)
Time allocated by MRTT
MRTT
STA2
Frame(Urgent
TX Request)
Event-based LL traffic occurs. STA1 has to send data frames immediately
REJECT

## Slide 9: Conclusion
Event-based low latency traffic should be supported in UHR
Existing 11be procedures may not support event-based LL traffic
New scheduling methods for supporting (event-based) urgent packet transmission should be considered in 11bn
For enhanced reliability, a STA may request the AP for an urgent TXOP sharing with a frame including a request for urgent packet transmission, QoS Characteristics element information and BSR information

## Slide 10: References
[1] 23/0480r0, UHR Proposed PAR
[2] 22/1556r1, Multi-AP Coordination for Low Latency Traffic Delivery
[3] 22/1899r0, Multi-AP Operation for Low Latency Traffic Delivery - Follow up
[4] 23/0046r2, Multi-AP Coordination for Low Latency Traffic Delivery: Usage Scenarios and Potential Features
[5] 22/1393r0, Latency Reduction Scheme for UHR
[6] 22/1939r0, PPDU Design for Short Frames
[7] 22/1923r1, Enhanced Trigger-Based Uplink Transmission
[8] 22/1926r0, Challenges to Achieve Low Latency
[9] 22/1519r0, Requirements of Low Latency in UHR
[10] 22/1931r0, Follow-up on Latency Reduction with ML Techniques
[11] 22/1880r1, Latency and Reliability Enhancements for UHR
[12] 23/0018r1, Low Latency Support in UHR
[13] 23/0045r1, Urgency-based Delivery of Latency Sensitive Traffic
[14] 23/0069r1, Considerations on Latency Improvement