## Slide 1: Enhancements to Channel Access for UHR
Date: 2023-03-10
Authors:
Name | Affiliations | Address | Phone | Email
Nima Namvar | Charter Communications |  |  | c-nima.namvar@charter.com
Maulik Vaidya |  |  |  | maulik.vaidya@ieee.org
doc.: IEEE 802.11-23/0381-00-0uhr
Notes: November 2012

## Slide 2: Abstract
The purpose of this proposal is to enable the utilization of uplink channel quality (UCQ) in a controlled access mode, with the aim of enabling the AP to make informed decisions regarding the allocation of WM to STAs, based on the channel quality.
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 3: Overview
Background
EDCA/HCCA Shortcomings
HCCA Enhancements
Compatibility with MLO
Example of Enhanced HCCA frame Exchange under MLO
Conclusions
Straw Polls
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 4: Background
The Ultra High Reliability (UHR) study group (SG) was formed to develop PAR for the new 802.11 amendment. The focus will be on
  Improve reliability of WLAN connectivity
  Reduce latencies
  Increase manageability
  Increase throughput including at different SNR levels
  Reduce device-level power consumption
The main takeaway from the previous UHR meetings is the the potential features that address multiple objectives would be considered with higher priority.
EDCA channel access doesn’t provide enough flexibility for intelligent allocation of WM, thus leading to avoidable delay and congestion. Limiting EDCA use has been proposed in [1].
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 5: EDCA/HCCA Shortcomings
The multi-interface availability introduced in 802.11be as well as the OFDMA scheme introduced in 802.11ax allow to naturally think of a standard protocol in SME for allocating the WM resources to the STAs in a controlled manner.
At present, the EDCA mechanism grants distributed access to STAs based on different UP classes. Similarly, the polled access provided by the HCCA mechanism utilizes only the TID and BSR information to grant TXOP to the STAs. Neither of these mechanisms takes into account channel quality as a factor for scheduling resources among STAs.
Competing unlicensed technologies operating in the same bands, such as LAA and NR-U, are capable of making decision on channel access based on channel quality, thereby allowing more room to optimize the system performance
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 6: HCCA Enhancements
To meet the emerging applications’ stringent latency and aggressive throughput requirements, a refined channel access technique is necessary.
Controlled access schema allow more flexibility for resource optimization.
The current HCCA mechanism is only poorly adopted by the vendors.
Enhancements to HCCA is a promising solution to address the envisioned UHR technical challenges. In particular, HCCA can benefit from a variety of readily available technologies to optimize the WM resource allocation strategy, tailored to the latency and reliability requirements of the emerging applications.
Providing CQI and channel load information to the AP can result in a more efficient and better control over the wireless resources, such as link/tone allocation in controlled access mode.
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 7: HCCA Enhancements
The channel measurement requires Request/Respose/Ack frame exchanges as per the current base standard, which adds considerable overhead to the network.
The channel measurement can be reported back to the AP during the CAP or in a periodic manner without an initial request by the AP. This feature, reduces the signaling overhead and allows better TXOP allocation to the STAs based on more parameters compared to EDCA.
Enhanced HCCA mechanism:
  To start an HCCA TXOP, the HC gains control of the WM by waiting a shorter time before initiating the first transmission of the TXOP than STAs using the EDCA procedures.
  Once the HC gains the control over channel, it sends a poll frame to STA, initiating the CAP.
  The STA respond with QoS+ frame, including the CQI and channel load as well as QoS parameters.
  The AP allocates polled TXOP to the STAs based on the received QoS frames.
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 8: Compatibility with MLO
In the context of MLO, the HC functionality should be implemented in the upper-MAC (UMAC) in the SME for each MLD device.
If the HCCA is supported by both the AP MLD and the STA MLD, the STA MLD gathers the instantaneous CQI at each interface according to the set of enabled interfaces at different links.
During the CAP, the STA MLD reports the CQI of all links to the AP within a single QoS frame, which is transmitted over all/one active link(s).
If the CQI is poor over several subsequent CAPs, the AP can potentially direct all the STA traffic to other available links and temporarily teardown that particular link. It is important to note that the teardown is performed on a per link basis, not per STA basis as is the case in the current 802.11be draft Standard.
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 9: Example of Enhanced HCCA under MLO
2.4 GHz
5 GHz
6 GHz
2.4 GHz
5 GHz
6 GHz
STA 1
STA 3
STA 2
AP 3
AP 1
AP 2
non-AP MLD
AP MLD
Poll Frame. [B]
UP TB PPDU [I]
Block Ack [I]
QoS+ Frame. [I]
Trigger Frame [I]
Alternate Sequence [I] = Individually addressed
[B] = broadcast address This example shows two sessions of resource allocation based on the QoS+ frame which includes CQI and channel load per individual link, in addition to the base QoS parameters. The Poll frame is transmitted over one or more active links and the QoS+ frames is similarly sent over one or more active links to the AP MLD. Upon receiving the QoS+ frame, the AP sends a TF in which the operating band/channel as well as the tones (in case of OFDMA) is carried to the STA MLD for the specified TXOP duration.
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 10: Conclusion
This presentation discussed a long-standing need for bringing the channel quality into the picture for scheduling wireless resources (tones/links).
Other technologies which have multi-channel (wideband) operation in the unlicensed spectrum, do implement similar feature to optimize the network performance.
Proposed enhancements to the HCCA considers CQI and load measurements over all STAs to distribute traffic over different links for different devices.
Exploiting channel quality information is crucial for optimizing wireless resources in WiFi.
The proposed enhancements in HCCA is compatible with a wide range of capabilities for the transmitter/receiver and also coexistence with legacy devices.
Nima
doc.: IEEE 802.11-23/0381-00-0uhr

## Slide 11: Straw Poll 1
Do you support the following feature in UHR:
  Enhancements to the base HCCA: The concept in which an AP requests channel measurement from the associated STAs and exploit that for scheduling TXOPs over different links/bands/tones (depending on the underlying technology of the STAs)
  Y/N/A
Nima
doc.: IEEE 802.11-23/0381-00-0uhr