## Slide 1: TGbi – Anonymizing frames and A1 filtering
Date: 2023-05-13
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
J. Levy | Interdigital |  |  | 

## Slide 2: Abstract
Some works in IEEE 802.11bi propose anonymizing A1 and A2 addresses by rotating the transmitting and receiving MAC addresses.
  DCN 2021/1539r0
  DCN 2023/133r0
Such a mechanism have implications on how a STA performs A1 filtering, since the A1 may change, some challenges discussed are:
  An A1 MAC address is only used as receiver address for a period of time
  When an A1 MAC address changes, retransmissions may use the “previous” MAC address.
  How are the MAC address transitions coordinated between the transmitter and the receiver.
This document proposes a mechanism enabling A1 filtering in such a scenario
  Proposal includes discussion on the anonymization/de-anonymization block

## Slide 3: Background
A1 address filtering is done right after CRC validation
  Some implementations may do Block Ack Scoreboarding right after
The process itself is not defined in the spec
It considers filtering based on:
  MAC address of the receiving STA
  dot11GroupAddressesTable

## Slide 4: Current description for A1 filtering (11me D2.0)
A1 filtering described in 10.2.8 - MAC data service
  A MAC performs address filtering on the Address 1 field in each MPDU contained in a PPDU and, for non-GLK non-AP STAs, on the DA of each MSDU within an A-MSDU.
  In the case of a non-GLK STA receiver, when the Address 1 field or DA field contains a group address, address filtering is performed by comparing the value in the Address 1 field or DA field to all values in the dot11GroupAddressesTable and the broadcast address value.
  If the Address 1 field of an MPDU carrying an A-MSDU does not match any address at a receiving STA, then the entire A-MSDU is discarded.

## Slide 5: Current proposals
2022/1870r0 (SRT, Graham) – Protection against Spoof AP using Probe: Requires STAs to use two MAC addresses simultaneously -> Requires list of addresses (2) for A1 filtering. There is no interim, both addresses available at same time.
2023/268r0 (Cox, Carol) - Proposal for OTA MAC Change -> Requires signaling change of MAC address, requires emptying queues, signaling in beacon, MAC addresses are generated in sequence, requires sync.
2023/328r0 (Cox, Carol) – Proposal for MLD OTA MAC Change -> similar features as previous, requires flushing queues since it assumes no simultaneous use of MAC Addresses.
2023/411r0 (Canon, Julien) – Obfuscation of Multiple CPE Parameters -> assumes simultaneous use of MAC addresses during interim.

## Slide 6: Summary of background
All proposals either assume an interim where queues need to be flushed, stop transmission, recompute parameters and resume or assume simultaneous use of several addresses
The use of multiple addresses in A1 filtering is already accepted in the standard for Group Addresses

## Slide 7: Proposal
Use a solution similar to what is used for dot11GroupAddressesTable
A group of the A1 and A2 addresses allows for different addresses to be used each direction of the communication
Anonymization/de-anonymization works by selecting addresses from the above sets

## Slide 8: Example for A1 and A2 anonymization

## Slide 9: Example of Operation
STA A
STA B
DSMAC_A
DSMAC_B
otaMAC_A1
otaMAC_A2
otaMAC_A3
otaMAC_B1
otaMAC_B2
otaMAC_B3
At T1 STA A and B have declared 3 otaMAC addresses each, each frame can be sent using 9 combinations of otaMAC addresses

## Slide 10: Example of Operation
STA A
STA B
DSMAC_A
DSMAC_B
otaMAC_A1
otaMAC_A2
otaMAC_A3
otaMAC_B1
otaMAC_B2
otaMAC_B3
At T2 STA A decides to remove otaMAC_A1, so it stops using it and waits for T seconds (tbd), after this period, it signals to STA B the removal of the address from the set (if T is big enough, all queues and retx has been already exhausted)

## Slide 11: Example of Operation
STA A
STA B
DSMAC_A
DSMAC_B
otaMAC_B1
otaMAC_B2
otaMAC_B3
At T3 STA A decides to add otaMAC_A4, so it signals to STA B the addition of the address to the set:
otaMAC_A2
otaMAC_A3
otaMAC_A4

## Slide 12: Anonymization process (from A)
The transmitting process starts by the anonymization process of the frame, by the STA processing a MDPU to be transmitted (A).
  Frame[A1=DSMAC_B, A2=DSMAC_A]
It first finds the list of otaMACs binded to the Rx (A1, DSMAC_B) address on the MPDU (list of MAC addresses stored in the Peer_Set).
Once found, the transmitting STA may choose among all the otaMAC addresses stored in the Peer_Set (A1) and the otaMAC addresses signaled to B (Own_Set) for A2.
The MPDU is then modified, exchanging the A1 and A2 addresses by the newly selected transmitting and receiving otaMAC and MPDU processing continues using the current 802.11 process to transmit the frame.
  Frame[A1=otaMAC_B1||otaMAC_B2, A2=otaMAC_A1||otaMAC_A2]
Note: if this process is coupled with the CCMP encapsulation process proposed in DCN 2023/416r0. Then the anonymization process can be done decoupled from the CCMP encapsulation

## Slide 13: A1 filtering/De-anonymization/reception process (from B)
The receiving process starts by the STA (B) receiving a unicast frame and performing A1 filtering.
  Frame[A1=otaMAC_B1||otaMAC_B2, A2=otaMAC_A1||otaMAC_A2]
The receiving STA compares the A1 address in the received frame to the list of otaMAC addresses stored in its Own_Set.
If found, processing can continue, otherwise the frame should be discarded.
After checking A1, the EP receiving STA checks for the A2 address, comparing it to the otaMAC addresses stored in the Peer_Sets.
If found, the frame is modified, exchanging the A1 address by the DSMAC of the receiving DSMAC (DSMAC_B) and the A2 by the transmitting DSMAC (DSMAC_A).
  Frame[A1=DSMAC_B, A2=DSMAC_A]
Note: if this process is coupled with the CCMP de/capsulation process proposed in DCN 2023/416r0. Then the de-anonymization process can be done decoupled from the CCMP decapsulation

## Slide 14: Anonymization of other parameters
The anonymization block can process the rest of parameters requiring obfuscation.
For example, for a transmitting STA, the SN used in frames may be computed as follows:
First, a Hash function of the otaMAC addresses used in the frame together with the Salt parameter stored per peer: SN_salt=Hash (otaMAC_A1, otaMAC_A2, Salt);
Second, the new SN to be added to the frame is computed by performing the XOR operation of the original SN and the SN_salt: SN_new= SN XOR SN_salt;
On reception, the STA computes first the SN_salt by using the exchanged Salt:
SN_salt=Hash(otaMAC_A1, otaMAC_A2, Salt) and later is able to obtain the original SN by performing the XOR operation: SN_original= SN_new XOR SN_salt.
Therefore after de-anonymization, we obtain the exact same MPDU before anonymization and there is no further impact in the MAC layer operation

## Slide 15: Anonymization/de-anonymization architecture
Packet number assignment
Null
Anonymization
MPDU Encryption…
Null
Null
Null
MPDU Header+CRC creation/validation
Replay detection
Synra processing
Block ACK buffering
MPDU Encryption…
Duplicate Detection
Block ACK Scoreboarding
De-anonymization
Address 1 filtering
Tx STA
Rx STA
  Frame[A1=DSMAC_B, A2=DSMAC_A, SN]
  Frame[A1=otaMAC_B1||otaMAC_B2, A2=otaMAC_A1||otaMAC_A2, SN1]
  Frame[A1=otaMAC_B1||otaMAC_B2, A2=otaMAC_A1||otaMAC_A2, SN1]
  Frame[A1=DSMAC_B, A2=DSMAC_A, SN]
Select addresses in Own and Peer MAC address Sets
Ofuscate other fields
Filter A1 addresses in Own Set, change A1 and A2 to DSMAC, de-ofuscate other parameters

## Slide 16: State required
Anonymization/de-anonymization
Set of MAC addresses used to transmit (A2 addresses), this can be per peer STA or a set for all peer STAs
Set of MAC addresses used by receiver (A1 addresses)
Salt used per peer (will come back to this later, assume e.g., 12 bits)
Example: AP using 10 addresses for tx, 90 peers with 10 addresses per peer, +1 salt per peer = (10+900)x48 + 90x12 = 44760 bits of extra memory required
Example: AP using 100 addresses for tx, 2000 peers with 10 addresses per peer, +1 salt per peer = (100+20000)x48 + 2000x12 = 989Kbits of extra memory
A1 filtering
N receiving addresses x 48, e.g., 20 receiving addresses x 48 = 960 bits
It can be more if A2 addresses per peer STA are used (TBD)

## Slide 17: Benefits/drawbacks of the approach
The proposal enables communication between two STAs that use anonymized MAC addresses for A1 and A2 in each direction of the communication  high level of ofuscation
Proposed use of address sets reduce the complexity of managing the addresses, it reduces non steady state periods and allows for retransmissions
  No need to empty queues, any address can be used any time
MAC addresses can be added/removed any time, retransmitions should not modify addresses, a STA can decide to stop using an address, signal its removal and actually take it out from the set considering enough time to not face problems.
May require increased memory space  this can be bounded by setting a maximum size of the sets