## Slide 1: Spatial Reuse Improvements for UHR
Date: 2023-05-15
Authors:

## Slide 2: Abstract
The UHR PAR has in its scope improving the efficient use of medium compared to 802.11be.
Spatial reuse is one of the mechanisms that can improve the efficient use of medium by increasing the number of successful transmission in an area.
Coordination among APs can further improve SR gains for coordinating APs and their associated STAs.
In this proposal, we focus on other aspects of spatial reuse that may be improved with or without AP coordination.

## Slide 3: 802.11ax/be PSR based spatial reuse
802.11ax and 802.11be support Parameterized Spatial Reuse (PSR) feature enabling an OBSS STA to transmit a PPDU overlapping a TB PPDU transmission. The OBSS transmission is constrained in power and duration.
PSR based SR has some limitations including
  It requires reception of the triggering PPDU (for inter-BSS classification) which may not always occur.
  The mechanism is PHY version dependent. 802.11be will not understand the PSR parameters in a UHR TB PPDU.

## Slide 4: Limitation regarding PSR based SR opportunity
In the figure, STAs 2 and 3 are OBSS STAs with respect to AP1/STA1.
Ideally, far STAs from AP1 are better PSRT PPDU transmitters i.e. STA 3 instead of STA 2 because their level of interference is lower.
However, according to the current 802.11be draft
  An EHT STA identifies a PSR opportunity if the following two conditions are met:
  1)The EHT STA receives a PHY-RXSTART.indication corresponding to the reception of a PSRR PPDU that is identified as an inter-BSS PPDU.
  2)An PSRT PPDU is queued for transmission and the intended transmit power of the PSRT PPDU in dBm shall meet the following condition in Equation (35-5)
Because only STAs that hear the AP (high interference) can perform PSR based SR, the gains will be limited (i.e. only STA 2 can transmit)
AP 1
STA 1
STA 2
AP coverage area
STA 3
High interference
Low interference

## Slide 5: Proposal: TF-less PSR-based SR
Enable STAs to transmit using PSR-based SR even without receiving the trigger frame. There are several options for computing the transmit power without receiving an actual PSRR PPDU.
1. Based on a previously received beacon power from the PSRR PPDU transmitting AP [1].
2. Based on a parameter received from the associated AP [2].
3. Based on a predetermined reference power level equal to the RX sensitivity plus margin.

## Slide 6: Limitation regarding version dependent SR fields
If UHR supports PSR based SR, 11be devices will not be able to understand the SR fields. SR field information may only be obtained by fully decoding the PSRR PPDU
As much as possible, we want to allow UHR STAs to use PSR based SR on future PPDU (beyond UHR) formats. This benefits beyond UHR devices too.
The straightforward solution is to designate SR fields as version independent fields. However SR fields contain substantial number of bits to designate as version independent.

## Slide 7: Proposal: version independent SR fields
Version independent SR fields
A field or bit (SP) may indicate that there
is spatial reuse field present in the U-SIG
- For example, if the SP bit is 0,
bits B3-B10 in U-SIG 2 is for
spatial reuse.
- If the SP bit is 1, bits B3-B10 is
not for spatial reuse.

## Slide 8: Conclusion
We presented limitations of PSR-based SR and provided candidate solutions.
The proposed solutions can improve SR gains for UHR when C-SR is not possible.

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0058-00-0uhr-spatial-reuse-in-coordinated-m-ap-for-uhr.pptx
[2] https://mentor.ieee.org/802.11/dcn/20/11-20-1880-01-00be-sr-field-in-tb-ppdu.pptx