## Slide 1: Non-AP initiated TXOP sharing
Date: 2023-04-14
Authors:
Name | Affiliations | Address | Phone | email
Shawn (Sanghyun) Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0523 | shawn.kim@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Greg Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 2: Motivation
Improving the tail of the latency distribution and jitter is one of objectives of UHR[1]
To improve latency/jitter, the AP needs to perform more flexible scheduling by taking into account the requirements of each STA
However, a challenge arises when a non-AP STA is the TXOP holder, as the AP is limited to a passive role as a TXOP responder
  Moreover, the AP of a BSS where a non-AP STA is a TXOP holder is limited in participating in Multi-AP Operation, which is considered as one of the key functions of UHR
Therefore, To enhance the network manageability of the AP that is a TXOP responder, it is necessary to introduce techniques in UHR
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 3: Candidate solutions
Two solutions can be considered to increase the manageability of AP
  Option 1: Reusing Triggered TXOP Sharing (TXS)[2]
    Concept: non-AP STAs share their TXOP with the AP
  Option 2: Reusing Reverse Direction (RD) protocol
    Concept: non-AP STAs transmit the RDG PPDU
Reusing the TXS procedure defined in EHT could be a better starting point
  As a RD responder, AP’s manageability is still limited (10.29.2 Reverse direction (RD) frame exchange sequence):
    shall schedule at least one MPDU/Trigger frame for the RD initiator
    shall trigger full-BW UL MU-MIMO
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 4: Recap: Triggered TXOP sharing procedure[3]
The TXOP sharing procedure defined in EHT allows an AP to share its TXOP with a non-AP STA, allowing the non-AP STA to manage the frame exchange sequence
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 5: Non-AP initiated TXOP sharing
Reusing Triggered TXOP Sharing (TXS)
  The AP can initiate MU operations for its BSS or M-AP operations during the time allocated by the non-AP STA
April 2023
Sanghyun Kim (WILUS), et al.
AP
Non-AP STA1
Ctrl frame
(e.g., TXS)
Non-AP STA2
Response
(e.g., CTS, Trigger frame)
TXOP
TB PPDU
TB PPDU
DL MU PPDU
M-AP
Ctrl frame
TXOP shared by the non-AP STA1
TXOP
Shared AP
Coordinated operations

## Slide 6: Remaining problems
Problems
  Inefficiency in BW utilization
    BW of the shared TXOP might be limited according to the non-AP STA’s operating BW
      AP cannot fully utilize its performance[4]
        *Note that there could be still 20 MHz-only STA in the UHR BSS
  NAV set by the non-AP STA
    Some APs may not be able to participate in M-AP operation due to the NAV set by the non-AP STA that is a TXOP holder
Direction to go
  The AP should become the TXOP holder, and the bandwidth should be able to expand
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 7: Proposed enhancement for the non-AP initiated TXOP sharing
April 2023
Sanghyun Kim (WILUS), et al.
During the shared TXOP, the AP can gain the rights to access the wider channel by invoking the backoff procedure and ignoring the NAV set by the non-AP STA
  AP can determine whether to invoke the backoff procedure
  *The other STAs do not contend the channel because their NAV is non-zero
  *The non-AP STA can invoke backoff to perform TXOP recovery during the shared TXOP by the AP (when the TXOP sharing mode is 2)
Once the AP obtains the rights, the AP can manage the network as a TXOP holder
AP
3
Response frame (P80)
2
1
0
Non-AP STA
Ctrl frame
(on P80)
0
IDLE
320 MHz PPDU
(e.g., MU-RTS)
MU & M-AP operations
TXOP
TXOP shared by the non-AP STA (P80)
TXOP of AP (320 MHz)
TXOP has been terminated
TXOP

## Slide 8: Considerations
ETSI Regulations[5]
  AP's channel access for wider BW after the backoff procedure is a regulation-compliant operation (please see APPENDIX)
Fair coexistence with legacy BSS
  There might be a rule for limiting the length of the TXOP for the AP
    e.g., (End of the AP’s TXOP) - (Initial frame of the non-AP STA) ≤ TBD threshold
      Therefore, it may be recommended for non-AP STAs to share their TXOP with the AP as soon as they acquire the TXOP
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 9: A brief analysis of the proposed solution
April 2023
Sanghyun Kim (WILUS), et al.
Pros
  Reducing Latency/Jitter
    Due to the increased manageability of AP
  TPUT Increase
    Due to MU/M-AP operations
    Due to the extended BW
Cons
  Overhead
    Additional backoff procedure does introduce overhead, but benefits (extra BW & M-AP operation) seem outweigh the overhead

## Slide 10: Summary
We proposed sharing the TXOP acquired by non-AP STAs with the AP
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 11: Straw Poll 1
Do you agree to define a procedure in UHR for a non-AP STA to share its TXOP with the associated AP?
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 12: Straw Poll 2
Do you agree to define a procedure in UHR that allows an AP to initiate its TXOP during the time allocated by the non-AP STA?
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 13: References
[1] 11-23/480r0 UHR proposed PAR (Laurent, Intel)
[2] 11-23/41r0 Considerations on Coordinated TDMA (Yanjun, Qualcomm)
[3] TGbe D3.0 (35.2.1.2 Triggered TXOP sharing procedure)
[4] 11-22/2204r0 Dynamic Subband Operation (Sindhu, Broadcom)
[5] ETSI EN 301 893v2.1.50e, 5 GHz WAS/RLAN; Harmonised Standard for access to radio spectrum https://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2023/BRAN(23)118013r3_Rapporteur_s_copy_of_EN_301_893.zip
April 2023
Sanghyun Kim (WILUS), et al.

## Slide 14: Appendix (ETSI regulations)
Summary (4.2.7.3.2.3 Multi-channel operation)[5]
  Option 1
    Device may use any combination/grouping of channels, if it satisfies the channel access requirements for an initiating device on each such operating channel
      Need to separately gain the right to access each channel (per-20 MHz)
  Option 2
    Device that uses a combination/grouping of adjacent 20 MHz channels that is a subset of the 40/80/160 MHz channels may transmit on any of the 20 MHz channels, if:
      The device has gained the right to the primary channel as defined in 4.2.7.3.2.6 and
      The device performs CCA of at least 23 us immediately before the intended transmission on each of the other operating channel
        *4.2.7.3.2.6 is equivalent/similar to the backoff procedure of Wi-Fi
April 2023
Sanghyun Kim (WILUS), et al.