## Slide 1: Low latency traffic delivery in UHR
Date: 2023-04-07
Authors:
April 2023
Name | Affiliations | Address | Phone | Email
Si-Chan Noh | NEWRACOM |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com
Heejung Yu | Korea Univ. |  |  | heejungyu@korea.ac.kr
Il-Gu Lee | Sungshin Women’s Univ. |  |  | iglee@sungshin.ac.kr

## Slide 2: Introduction
Improving the tail of the latency distribution and jitter is one of the main requirement in the UHR group as described in the approved PAR[1]
There are many latency improvement contributions as follows:
  Preemption [2], [3]
  Multi-AP Operation for low latency (LL) traffic [4], [5]
  AI/ML [6]
In this presentation, we discuss a basic transmission approach allow LL traffic in perspective of flexible “punctured channel information” considering puncturing scheme in 11ax and 11be

## Slide 3: Problem statement
How to deal with LL traffic in 802.11 networks without collision/interference and no waiting in the middle of the TXOP of the other client?
  In case of dedicated scheduling which is assigns resource without the contention between LL and non-LL traffic, the following conditions might be needed:
    assign resource in terms of certain condition
    indicate information about the assigned resource

## Slide 4: Approach : Using preamble puncturing
An AP can indicate the channels as punctured or non-punctured within its operating bandwidth
Load LL traffic into punctured channel could be one of candidates to support LL traffic
  It means, assign deterministic punctured channel for an event-based LL traffic, we can prevent collision of on-going non-LL traffic transmission
Non-Punctured
Non-Punctured
Punctured
Non-Punctured
Non-LL traffic
Non-LL traffic
LL traffic
Non-LL traffic

## Slide 5: Summary
It is challenging to deal with LL traffic in 802.11 networks without collision/interference and no waiting in the middle of the TXOP of the other client
We propose a basic approach allow LL traffic in perspective of flexible “punctured channel information” considering puncturing scheme in 11ax and 11be

## Slide 6: Reference
[1] 23/0480r0, UHR Proposed PAR
[2] 23/0018r1, Low Latency Support in UHR
[3] 23/0092r0, Preemption for Low Latency Application
[4] 22/1899r0, Multi-AP Operation for Low Latency Traffic Delivery – Follow up
[5] 22/1556r0, Multi-AP Coordination for Low Latency Traffic Delivery
[6] 22/1519r0, Requirements of Low Latency in UHR