## Slide 1: Secondary channel usage and secondary 20MHz channel backoff
Date: 2023-04-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: STA, AP Capabilities
The AP has higher capabilities than STAs.
  Wider BW
  Higher Tx power
  More NSS.
In order to better reuse secondary channels, 11ax update 11ah’s SST in individual TWT
  STAs can negotiate parking secondary channel in individual TWT SPs.

## Slide 3: Backoff Capabilities
An AP can announce the multiple subchannels of its operating channel where each subchannel includes multiple 20MHz channels.
  Each subchannel has one backoff 20MHz channel.
    The backoff 20MHz channel can’t be punctured in dynamic channel puncture operation.
A STA/AP can enable one of the following backoff procedure:
  PPDU detection through one subchannel only
  PPDU detection through multiple Backoff channels simultaneously.
A STA/AP can enable one of the following backoff procedure:
  Backoff in one 20 MHz channel.
    One special case is to do backoff in primary 20MHz channel only
  Backoff in multiple 20 MHz channels
    Backoff simultaneously in multiple 20MHz channels where each backoff channel is in one subchannel.
    Only one of the multiple backoff 20MHz channels where each backoff channel is in one subchannel can be used for backoff at any time.
      The backoff in channel other than primary 20MHz channel and doing frame exchanges other than primary 20MHz channel when the primary 20MHz channel is busy.

## Slide 4: Secondary Subchannel Parking
The SST is extended to the broadcast TWT agreement.
  During the broadcast TWT membership negotiation, a STA can negotiate the secondary subchannel parking with the AP.
  Once the parked secondary subchannel and the related broadcast TWT membership are successfully negotiated, the STA switch to the negotiated subchannel at the beginning of the negotiated broadcast TWT SP and stay in the subchannel until the end of the TWT SP.
The SST is extended to the 320MHz BSS.
Primary 20MHz channel
(the specific backoff 20MHz channel)
80MHZ channel 1
(subchannel1)
(primary subchannel)
80MHZ channel 2
(subchannel2)
80MHZ channel 3
(subchannel3)
80MHZ channel 4
(subchannel4)
Backoff 20MHz channel 2
Backoff 20MHz channel 3
Backoff 20MHz channel 4
BSS operating channel
STA1, 5, 9 park on subchannel 2
STA10, 16 park on subchannel 3
STA 6, 8, 12 park on subchannel 4
Other STAs don’t negotiate the parked subchannel
Broadcast TWT SP
Broadcast TWT SP

## Slide 5: Dynamic Secondary Subchannel
When in a BSS the carrier sensing in primary 20MHz channel indicates the OBSS’s TXOP, the AP and associated STAs in the BSS switch to a nonprimary subchannel for the frame exchanges until the end of the OBSS’s TXOP.
The rules for the dynamic channel switch should guarantee the synchronization of the dynamic switch
  No one side switch while another side doesn’t switch.
    From primary subchannel to a nonprimary subchannel
    From one nonprimary subchannel to another nonprimary subchannel
  The priority of the nonprimary subchannels should be defined.
The rules for the dynamic channel switch should try to avoid the blindness when switch back to the primary subchannel.
Primary 20MHz channel
(the specific backoff 20MHz channel)
80MHZ channel 1
(subchannel1)
(primary subchannel)
80MHZ channel 2
(subchannel2)
80MHZ channel 3
(subchannel3)
80MHZ channel 4
(subchannel4)
Backoff 20MHz channel 2
Backoff 20MHz channel 3
Backoff 20MHz channel 4
BSS operating channel
Highest priority
Lowest priority

## Slide 6: Medium Synchronization under Secondary Channel Access
When switching to a nonprimary subchannel, the AP/STA that try to initiate the frame exchanges lose the medium synchronization.
The medium synchronization that is similar to 11be may be required.
  The different transition delays of AP/STAs needs to be considered.
  The methods to guarantee that the solicited TXOP responder(s) are ready for the frame exchanges should be defined.
The dynamic channel switch may have higher chance to lose the medium synchronization that 11be cases
  STR AP MLD and NSTR/EMLSR/EMLR non-AP MLD.
    The AP MLD always keeps the medium synchronization in all the links.
  NSTR mobile AP MLD and NSTR non-AP MLD
    When a TXOP doesn’t include both long DL PPDU and long UL PPDU, one side will keep the synchronization in the unused link.
  Dynamic channel switch
    When a TXOP doesn’t cover a nonprimary subchannel and TXOP holder/responder can’t do multiple subchannel’s frame decoding, both AP and STA will lose the medium synchronization.

## Slide 7: RU Coding
In baseline, the RU Index of the DL MU PPDU and UL TB PPDU is decided per the primary 20MHz channel
a TXOP may have a BW that is wider than the BW of a subchannel.
The RU usage may have some collision when the following happen
  a TXOP with a BW that is wider than the BW of a subchannel
  the different STAs may have different view of the backoff 20MHz channels.
Primary 20MHz
channel
80MHZ channel 1
(subchannel1)
(primary subchannel)
80MHZ channel 2
(subchannel2)
80MHZ channel 3
(subchannel3)
80MHZ channel 4
(subchannel4)
Backoff 20MHz
channel 2
Backoff 20MHz
channel 3
Backoff 20MHz
channel 4
BSS operating channel
STAs that switch to subchannel2 assume the
RU index based on Backoff 20MHz channel 2.
STAs that are in subchannel2 assume the
RU index based on Backoff 20MHz channel 1.
The two TB PPDUs have the same BW values with different channel puncture.

## Slide 8: Conclusions
The methods to improve the BSS throughput through dynamic subchannel switch are discussed.
With the SST, the requirement of the dynamic channel switch at STA side is not needed.
  This is easy to be adopted.
Without the SST, the requirement of the dynamic channel switch at AP side and STA side is needed.
  the subchannel switch synchronization is required.
  The medium synchronization of 11be may need some changes.
  The RU Index definition needs to be clarified.