## Slide 1: Smooth Roaming Follow Up
Date: 2023-04-02
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Roaming AP MLD
Roaming AP MLD for smooth roaming support is defined that includes multiple AP MLDs.
  Roaming AP MLD support is optional at UHR non-AP MLD side.
  Roaming AP MLD is not visible to EHT non-AP MLDs and UHR non-AP MLDs without roaming support.
A MAC SAP address is defined for a roaming AP MLD.
The BA agreement is negotiated between an UHR non-AP MLD and the roaming AP MLD if the UHR non-AP MLD supports the roaming.
The PMKSA, PTK of an UHR non-AP MLD are negotiated between an UHR non-AP MLD and the roaming AP MLD.
Some non-link level MAC features are at MLD level while the other non-link level MAC features are at roaming MLD level.
Two types of roaming are MLD level roaming and optional Link level roaming where some restrictions should be added to link level roaming.
In a roaming AP MLD, the non-AP MLD can be identified by AP MLD roaming ID + AID.
  AID is defined by AP MLD.
The link of roaming AP MLD is identified by AP MLD roaming ID + Link ID.
  Link ID is defined by AP MLD.
AP MLD11
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD12
MLD common MAC
5GHz
AP121
6GHz
AP122
AP MLD13
MLD common MAC
5GHz
AP131
6GHz
AP132
AP MLD14
MLD common MAC
5GHz
AP141
6GHz
AP142
Roaming AP MLD1
Roaming AP
MLD common MAC
Visible to an EHT non-AP MLD and
UHR non-AP MLD without roaming support
Visible to an UHR non-AP MLD
support roaming
To/From DS
Data Path for non-AP MLDs
Without supporting roaming AP MLD
Data Path for non-AP MLDs
With supporting roaming AP MLD
To/From DS
To/From DS
Data Path for non-AP STAs
Without affiliated non-AP MLD

## Slide 3: Single Serving AP MLD Mode vs Multiple Serving AP MLD Mode
In a single serving AP MLD mode, all the setup links of a non-AP MLD associated with a roaming AP MLD belong to an AP MLD affiliated with the roaming AP MLD.
  This is the basic mode
In a multiple serving AP MLD mode, the the setup links of a non-AP MLD associated with a roaming AP MLD can belong to multiple AP MLDs affiliated with the roaming AP MLD.
Non-AP MLD11
MLD common MAC
5GHz
STA11
6GHz
STA12
Non-AP MLD11
MLD common MAC
5GHz
STA11
6GHz
STA12
One non-AP MLD with single serving AP MLD
One non-AP MLD with multiple serving AP MLDs
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC

## Slide 4: Single Serving AP MLD Mode, Multiple Serving AP MLD Mode
A roaming AP MLD announces whether it supports single or multiple serving AP MLD mode.
Usage of multiple serving AP MLD mode
  Option 1: The multiple serving AP MLD mode is a transient mode and is only used for roaming.
    The roaming AP MLD can announce the restriction (e.g. no simultaneous usage of the links of two AP MLDs and for roaming only, explicit indication of the link for the UL/DL traffic) for this mode.
  Option 2: the multiple serving AP MLD mode is a nontransient mode.
    This mode has strong implementation requirement unless some restrictions are added.
      Do we want to allow such option?
    If no restriction exists, it can work as a normal AP MLD and be associated by the EHT non-AP MLDs and UHR non-AP MLDs that don’t support roaming.
Non-AP MLD11
with roaming support
MLD common MAC
5GHz
STA11
6GHz
STA12
Non-AP MLD11
with roaming support
MLD common MAC
5GHz
STA11
6GHz
STA12
One non-AP MLD with single serving AP MLD
One non-AP MLD with multiple serving AP MLDs
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC
MLD common MAC
AP MLD21
MLD common MAC
5GHz
AP121
6GHz
AP122
AP MLD22
Roaming AP MLD
Roaming AP
MLD common MAC
MLD common MAC
5GHz
STA11
6GHz
STA12
EHT non-AP MLD
Co-located links
Visible to non-AP MLD
With roaming support
Visible to non-AP MLD
Without roaming support
?
Ok for transient mode.
Nontransient mode?

## Slide 5: General Rule of Feature Level
If the usage of a feature is at roaming AP MLD, the feature is at roaming AP MLD level.
If a non-AP MLD with multiple serving AP MLDs uses a feature that is serviced by more than one AP MLD, the feature is at roaming AP MLD level.
If after roaming operation a feature being used in the original serving AP MLD(s) can still be used in the new serving AP MLD(s), the feature is roaming AP MLD level.
Otherwise, the feature is AP MLD level.
Non-AP MLD11
MLD common MAC
5GHz
STA11
6GHz
STA12
Non-AP MLD11
MLD common MAC
5GHz
STA11
6GHz
STA12
One non-AP MLD with single serving AP MLD
One non-AP MLD with multiple serving AP MLDs
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC

## Slide 6: Frame Broadcasting
The sequence number space of the group-addressed QoS Data frames is at AP MLD level.
  All the APs affiliated with an AP MLD affiliated with a roaming AP MLD use the same sequence number to broadcast a broadcast data frame.
In the TIM element of an AP affiliated with AP MLD1 of a roaming AP MLD, the indication of the buffered group-addressed frames of another AP affiliated with AP MLD2 of the roaming AP MLD is not carried.

## Slide 7: MLD Features in Single Serving AP MLD Mode
Observation
  NSTR may not be able to be transferred from one serving AP MLD to another AP MLD.
  EMLSR/EMLMR mode may not be suitable to be transferred from one serving AP MLD to another AP MLD.
The NSTR support is at AP MLD level
The EMLSR mode support is at AP MLD level
The EMLMR mode support is at AP MLD level
The STR operation is at AP MLD level
TID-to-Link Mapping is at AP MLD level
Multi-Link Traffic Indication is at AP MLD level
Non-AP MLD11
MLD common MAC
5GHz
STA11
6GHz
STA12
One non-AP MLD with single serving AP MLD
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC

## Slide 8: Restriction under Multiple Serving AP MLD Mode
A serving AP MLD can’t support the nontransient multiple serving AP MLD mode unless one of the following is true
  The roaming AP MLD supports roaming MLD level reorder buffer, duplication detection
  One UL TID is not mapped to more than one serving AP MLD
  Explicit indication of the link for UL TID traffic
Additional requirement may be applied
Non-AP MLD11
MLD common MAC
5GHz
STA11
6GHz
STA12
One non-AP MLD with multiple serving AP MLDs
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD
Roaming AP
MLD common MAC

## Slide 9: NSTR Link Pair under Multiple Serving AP MLD Mode
Observation:
  the PPDUs simultaneously transmitted to a non-AP ML through a NSTR link pair of the non-AP MLD need to be end at the same time. The backoff counters of the two links need to be both 0.
    The real-time information exchange between APs is required to finish such operation.
    the two AP MLDs may not be able to support the simultaneous transmission in the NSTR link pair to the non-AP MLD.
proposal:
  A roaming AP MLD announces whether it supports the NSTR link pair whose links belong to two AP MLDs.
  When NSTR link pair is at roaming AP MLD level, either one of the following can be true
    the non-AP MLD always has one link in active mode or awake state at any time.
    The two AP MLDs can guarantee the ending time alignment of two PPDUs and aligned zero backoff counters

## Slide 10: EMLSR/EMLMR Mode under Multiple Serving AP MLD Mode
Observation:
  When an AP of an AP MLD initiates the frame exchanges with a STA of a non-AP MLD in an EMLSR/EMLMR link, another AP of the AP MLD can’t do the frame exchanges in another EMLSR/EMLMR link of the non-AP MLD.
    The information exchanges between APs of the AP MLD is required to support such operation.
    If two EMLSR/EMLMR links of a non-AP MLD belongs to two AP MLDs affiliated with a roaming AP MLD, the two AP MLDs may not be able to support such information exchange in real time.
Proposal:
  A roaming AP MLD announces whether it supports the EMLSR/EMLMR links when the EMLSR/EMLMR links belong to multiple AP MLDs of the roaming AP MLD.
  When EMLSR/EMLMR is at roaming AP MLD level, either one of the following can be true
    A non-AP MLD always has one link in active mode or awake state at any time.
    The roaming AP MLD can guarantee that when one link is doing frame exchanges with a non-AP MLD in multiple serving AP MLD mode, another link will not do the frame exchanges with the non-AP MLD.

## Slide 11: Other MLD Features under Multiple Serving AP MLD Mode
The STR operation is at roaming AP MLD level
TID-to-Link Mapping is at roaming AP MLD level
Multi-Link Traffic Indication is at roaming AP MLD level

## Slide 12: Summary
The roaming AP MLD + AP MLD architecture was discussed
  association, PMK/PTK, SN space of unicast data frames, SN space of management frame, BA agreement are at roaming AP MLD level.
  Group-addressed SN space is at AP MLD level
The modes of single serving AP MLD and multiple serving AP MLDs were discussed
  The single serving AP MLD mode is the basic mode
    Most of the other features are at AP MLD level.
  The multiple serving AP MLD mode is the enhanced mode. Some restriction should be added to such mode, e.g. only for roaming from one AP MLD to another AP MLD or no support of it
    Most of the other features are at roaming AP MLD level, i.e. roaming AP MLD + AP.