## Slide 1: Resource Management for Multi-AP Coordination
Date: 2023-04-01
Authors:

## Slide 2: Abstract
In this contribution, we discuss the issue of resource management for multi-AP coordination.
We discuss some solutions that can help to mitigate some of the problems that can arise and provide high level steps for the solutions

## Slide 3: Background
Multi-AP coordination
  There has been an increasing demand for Wi-Fi connectivity. As a result, multiple APs are co-deployed to meet the growing needs.
  The increasing density of AP deployment results in interference becoming an important problem that can degrade STA performance.
  In TGbe, many candidate multi-AP schemes have been considered for mitigating the interference:
    Co-SR, JTX, Co-BF, etc. [1-5]
AP controller
AP1
AP2
AP3
Fig. Example MAP framework with a central controller communicating with APs

## Slide 4: Motivation
Multi-AP schemes can involve:
  Overhead from AP-AP information exchange:
    APs can exchange a number of information amongst each other to facilitate the coordination.
    E.g., information from STA-side interference reports
  Data exchange between APs:
    Some schemes such as Joint Transmission can require data exchange between APs.
This can cause some issues in implementation of multi-AP schemes.
  Data management complexity,
  Increasing backhaul load, etc.
These issues can become more severe with
  An increasing number of traffic flows which are serviced through multi-AP coordination
  An increasing number of APs involved in multi-AP coordination
Efficient resource management is important to realize multi-AP schemes in next generation Wi-Fi networks.

## Slide 5: Considerations for resource management for multi-AP
In this presentation, we discuss two factors that can simplify the implementation of multi-AP coordination schemes:
  Selective flow control
  Flow requirement based AP selection

## Slide 6: Selective Flow Control
Not all traffic flows may need to be serviced via multi-AP coordination:
  Real time traffic flows:
    Can have strict latency and performance requirements. E.g., gaming traffic.
    Multi-AP coordination can be beneficial for improving user experience
  Non-real time traffic flows:
    May not have a strict latency and performance requirement. E.g., web browsing.
    Multi-AP coordination may not greatly improve the user experience
AP controller
AP1
AP2
AP3
MAP coordination for gaming
Non-real time traffic
Fig. Example illustration for selective flow control

## Slide 7: Selective Flow Control
High level steps involved in selective flow control:
STA determines which flows can benefit from MAP coordination.
  E.g., real time traffic flow
STA provides classification information to help the AP identify these flows.
  STA can reuse existing features in the spec. E.g. STA can provide classifier masks using TCLAS and TCLAS processing element
MAP framework uses the classifier mask to identify which flows need to be served via MAP schemes. Other flows can be served without any coordination.

## Slide 8: Flow Requirement Based AP Selection
Not all interfering APs in the MAP framework may need to be involved in coordination
  Primary APs: Coordinating with such APs is absolutely necessary to meet a particular flow’s latency and performance requirement.
  Secondary APs: Coordinating with such APs can help to further help improve performance. But flow’s latency and performance requirement can be met even without coordinating with them.
MAP framework includes primary APs for coordination.
Secondary APs can be included or skipped dynamically based on network conditions.
  E.g., STA faces interference from AP2 and AP3 for gaming traffic. AP2 is primary AP and AP3 is secondary AP. MAP framework selects AP3 only if the resulting backhaul load, data management complexity, etc. from involving AP3 can be tolerated at the time of coordination.
AP controller
AP1
AP2
Primary AP
AP3
Secondary AP
Coordinating with AP 2 alone can meet gaming traffic requirements
Fig. Example illustration for flow requirement based AP selection
STA

## Slide 9: Flow Requirement Based AP Selection
Steps involved in flow requirement based AP selection:
  STA can provide its performance expectation for a given flow. E.g., latency requirements
  STA can also provide reports to the AP about the interference it faces from neighboring APs
  MAP framework divides interfering APs of the STA into primary and secondary APs.
  At the time of coordination, MAP framework can dynamically omit secondary APs depending on network conditions.

## Slide 10: Summary
Multi-AP schemes can be an important part of next generation Wi-Fi networks to reduce interference and improve user experience
In this contribution, we discussed some of the issues that can arise in implementation of multi-AP schemes in a practical system
We discussed two approaches that can help to mitigate the complexity and backhaul load:
  Selective flow control
  Flow Requirement Based AP selection
We discuss the high level steps for the two approaches

## Slide 11: References
[1] 11-19-1919-03-00be-coordinated-ofdma
[2] 11-20-0548-02-00be-discussion-on-coordinated-ul-mu-mimo
[3] 11-20-0033-01-00be-coordinated-spatial-reuse-operation
[4] 11-20-0071-01-00be-joint-transmission-for-11be
[5] 11-20-0099-01-00be-coordinated-beamforming-for-802-11be