## Slide 1: Follow-up on Coordinated TDMA (C-TDMA)
Authors:
Name | Affiliations | Address | Phone | email
Yanjun Sun | Qualcomm |  |  | 
George Cherian |  |  |  | 
Abhishek Patil |  |  |  | 
Abdel Karim Ajami |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Duncan Ho |  |  |  | 
Gaurang Naik |  |  |  | 
Date: 2023-05-15

## Slide 2: Objective
Background
  Previous contributions in UHR for enabling C-TDMA aim to reuse EHT’s TXS framework (see [1, 2])
  However, the details are yet to be discussed
Objective
  Identify TXS functionalities that may need further expansion, in order to make them work across APs
Items to discuss in this contribution:
  Handling different processing delays at APs
  Handling hidden APs
  TXOP return among APs

## Slide 3: Handling Different Processing Delays at APs
Challenge: as discussed in [1], an UHR AP may need additional processing delays compared to a non-AP STA due to:
  The difference in architecture
  More complex scheduling decisions and higher workload
Candidate solutions:
  Option 1: Use extra padding to account for the additional processing time when sharing a TXOP
    Pros: Same as existing schemes
    Cons: Increased airtime usage for padding transmission which reduces the networks' efficiency
  Option 2: Advance/upfront notification to the shared AP on schedule allocation via a dedicated frame
    Pros: Works for all scenarios regardless of expected processing delays
      Sharing AP can schedule a shared AP or serve its own BSS accounting for the processing delays after transmitting the notification frame
    Cons: Need to define new signaling (namely the notification frame)
Notes: Reference: MinTrigProcTime, up to 16us; EMLSR Padding Delay, up to 256us

## Slide 4: Handling Hidden APs
Background: during the discussion of C-TDMA [1, 2], members suggested to keep the protocol flexible to schedule one or more shared APs
Challenge: When shared APs are hidden from each other, it can disrupt the C-TDMA sequence and reduce reliability
Candidate solution: A sharing AP transmits a dedicated frame (e.g., notification, i.e., same as option 2 of previous slide) to notify the neighboring AP(s) to defer contending based on the schedule
AP1 is hidden from AP3
AP2
(sharing AP)
AP3 (shared AP)
3. AP1 uses the shared TXOP
AP1 (shared AP)
2. Shares to AP1 (not setting NAV to allow AP1 to trigger uplink transmission from 11ax/be STAs)
4. Mistakenly believes the medium is idle, and start parallel TX
Time
5. AP2 cannot get back control of the TXOP due to the transmission from AP3
1. Win a TXOP
AP1 is hidden from AP3
AP2
(sharing AP)
AP3 (shared AP)
3. AP1 uses the shared TXOP
AP1 (shared AP)
2. Share to AP1 (not setting NAV to allow AP1 to trigger uplink transmission from 11ax/be STAs)
5. AP3 uses the shared TXOP
Time
4. AP2 gets control and shares to AP3
1. Notification
Defer contention based on the Notification

## Slide 5: TXOP return among APs
Recap: EHT’s TXS framework enables TXOP sharing with an associated STA and provides a mechanism for TXOP return
  TXS mode 1 is meant for uplink (UL) transmission and TXOP return at the sharing AP is based on not receiving any uplink (UL) frames for a PIFS time from the STA with whom the TXOP was shared.
  TXOP mode 2 can be used for p2p and TXOP return at the sharing AP is based on receiving a QoS Null or QoS Data frame containing a CAS Control field indicating return of the TXOP.
    This mode may be more suited for AP-to-AP TXOP sharing, as it allows the shared TXOP to be used for PPDUs not addressed to the sharing AP
Challenge:
  QoS Null/QoS Data Frames with CAS Control can be exchanged only between associated STAs (subject to their capabilities). Hence, this TXOP return mechanism may be challenging for AP-2-AP TXOP-sharing
Proposal: for TXOP return, to find baseline procedures that don’t require association among APs or capability knowledge

## Slide 6: CF-End for TXOP Return in C-TDMA
If a shared AP (AP2) wants to return the TXOP before the end of the shared TXOP
  Send a CF-end frame with TA set to the shared AP (AP2) and Duration set to 0
If the sharing AP (AP1) receives this CF-End frame during the TXOP shared to AP2, the sharing AP may use/share the remaining TXOP in SIFS/PIFS
AP1
STA1
STA2
DATA to STA1
BA to AP1
TXOP won by AP1
AP2 (shared)
Time allocated to AP2 for DL/UL TB PPDU
TXOP Owner
MU-RTS TXS' for AP2
CTS to AP1
DATA to STA2
BA to AP2
Share TXOP to AP2
CF-End TA=AP2
TXOP return to AP1

## Slide 7: Will CF-End based TXOP return have backward compatibility issue?
11meD3.0P1911L38: “The TXOP holder that transmits a CF-End frame shall not initiate any further frame exchange sequences within the current TXOP.”
  This rule prohibits a shared AP (AP2) from using the rest of the TXOP
  But it doesn’t block the sharing AP that hasn’t transmitted a CF-end
11meD3.0P1911L50: “In a non-DMG BSS, a non-S1G non-HE STA(11ax) shall interpret the reception of a CF-End frame as a NAV reset, i.e., it resets its NAV to 0 at the end of the PPDU containing this frame. After receiving a CF-End frame with a matching BSSID(TA) without comparing Individual/Group bit, an AP may respond by transmitting a CF-End frame after SIFS."
  This is a precedence for a sharing AP to continue using the TXOP after receiving a CF-end

## Slide 8: Summary
This contribution tried to identify TXS functionalities that may need further expansion and candidate solutions:
  Challenge1: Handling different processing delays at APs
    Proposal 1: use padding in MU-RTS TXS’ Trigger frame
    Proposal 2: introduce a new frame to indicate schedule allocation upfront
  Challenge2: Handling hidden APs
    Proposal: introduce a new frame to indicate schedule allocation upfront
  Challenge3: TXOP return between APs
    Proposal: reuse existing CF-end frame for TXOP return

## Slide 9: References
[1] Yanjun Sun and et al. (Qualcomm), “Considerations on Coordinated TDMA (C-TDMA)”, 23/0041r0, Jan 2023.
[2] Dibakar Das and et al. (Qualcomm), “C-TDMA procedure in UHR”, 23/0216r0, Apr 2023.