## Slide 1: AIML Assisted Complexity Reduction For Beamforming CSI Feedback Using Autoencoder
Date: 2023-05-15

## Slide 2: Recap: Legacy beamforming scheme

## Slide 3: Recap: Existing AIML Beamforming schemes
K-means based schemes (e.g., [1]-[2])
  The scheme feedbacks an index which represents a codeword in a pre-trained codebook
  The codebook design in [1] is in angles obtained from V matrix
  The codebook design in [2] is in either angles (scheme I) or steering matrix (scheme II)
Autoencoder based schemes (e.g., [3]-[4])
  Neural network is used to compress feedback information
  In [3], angles are compressed, and the feedforward neural network (FNN) is used for autoencoder
  In [4], convolutional neural network (CNN) or transformer is used for autoencoder

## Slide 4: Proposed autoencoder-based scheme
Advantages:
Steering matrix is compressed directly to avoid angle computation using Givens rotation
FNN is used in the encoder to reduce computational complexity
CSI feedback at beamformee
Parameters Nae and NQ need to be optimized to
trade-off between model precision and feedback overhead

## Slide 5: Considered system parameters for performance evaluations
Parameters | Values
Packet format | 11ax
BW | 20 (MHz)
Channel Model | 802.11 Channel-D
Subcarrier Grouping ( | 4
Number of feedback subcarriers | 64
Number of bits to compress () | 4 (bits)
Number of Antennas at BFer () | 8
Number of Antennas at BFee () | 2
Number of angles for or ) | 13
Number of Spatial Streams | 2
NDPA duration | 28 (s)
NDP duration | 168 (s)
SIFS duration | 16 (s)
Parameters | Values
Packet format | 11ax
BW | 20 (MHz)
Channel Model | 802.11 Channel-D
 | 4
Number of feedback subcarriers | 64
 | 4 (bits)
 | 8
 | 2
 | 13
Number of Spatial Streams | 2
NDPA duration | 
NDP duration | 
SIFS duration | 

## Slide 6: Goodput evaluation method
Goodput definition:
,
where , denotes the MPDU size of beamfored data transmission, the duration used for a model update, the duration of a beamforming cycle.
The AIML model is updated once within a period of containing beamforming cycles.
A beamforming cycle
MCS for both BFed data transmission and CSI reports are selected according to mean SNR
Model sharing uses legacy beamforming

## Slide 7: Goodput comparison
= 1KB
For the proposed scheme, the format of the output from the encoder is half-precision floating-point (16 bits)

## Slide 8: PER performance comparison
= 1KB
MCS4
MCS7
MCS8
MCS10
MCS11

## Slide 9: Comparisons of overhead and complexity for CSI reports
Scheme | Communication overhead per CSI report (bits) | Number of required multiplications per CSI report
Legacy scheme | 8320 (130 per subcarrier) | 225K
K-means scheme in [1] | 704 (11 per subcarrier) 768 (12 per subcarrier) 1024 (16 per subcarrier) | 3633K (11 per subcarrier) 7041K (12 per subcarrier) 109277K (16 per subcarrier)
K-means scheme II in [2] |  | 3932K (11 per subcarrier) 7864K (12 per subcarrier) 125829K (16 per subcarrier)
Proposed autoencoder scheme | 3840 (60 per subcarrier, ) 7680 (120 per subcarrier, ) | 86K () 96K ()
Scheme | Communication overhead per CSI report (bits) | Number of required multiplications per CSI report
Legacy scheme | 8320 (130 per subcarrier) | 225K
K-means scheme in [1] | 704 (11 per subcarrier) 768 (12 per subcarrier) 1024 (16 per subcarrier) | 3633K (11 per subcarrier) 7041K (12 per subcarrier) 109277K (16 per subcarrier)
K-means scheme II in [2] |  | 3932K (11 per subcarrier) 7864K (12 per subcarrier) 125829K (16 per subcarrier)
Proposed autoencoder scheme |  | 
Note: complexity of k-mean schemes mainly comes from codeword index searching (Euclidean distance as the metric); complexity of the legacy scheme comes from angle computation (Givens rotation)

## Slide 10: Summary
We have presented a beamforming CSI feedback scheme with low computational complexity, the key purpose is to enable faster feedback and lower power consumption at non-AP STAs (e.g., mobile devices).
This is different from the existing use case in [5] whose main purpose is CSI compression and goodput improvement.

## Slide 11: Question
Do you agree that “Complexity reduction for CSI feedback” should be considered as a separate use case for AIML TIG?

## Slide 12: References
[1] M. Deshmukh, Z. Lin, et al., “Intelligent Feedback Overhead Reduction (iFOR) in Wi-Fi 7 and Beyond,” IEEE Vehicular Technology Conference (VTC), Jun. 2022
[2] 11-23/0275r1, Improved AIML Enabled Index Based Beamforming CSI Feedback Schemes
[3] P. Sangdeh, H. Pirayesh, A. Mobiny and H. Zeng, “LB-SciFi: Online Learning-Based Channel Feedback for MU-MIMO in Wireless LANs,” 2020 IEEE 28th International Conference on Network Protocols (ICNP), Oct. 2020.
[4] 11-23/0290r1, Study on AI CSI Compression
[5] 11-22/1934r5, Proposed IEEE 802.11 AIML TIG Technical Report Text for the CSI Compression Use Case