## Slide 1: M-AP Coordination Agreement
Date: 05-01-2023
Authors:
Name | Affiliation | Address | Phone | Email
Arik Klein | Huawei Technologies |  |  | arik.klein@huawei.com
Genadiy Tsodik |  |  |  | genadiy.tsodik@huawei.com
Shimi Shilo |  |  |  | Shimi.Shilo@huawei.com
Oded Redlich |  |  |  | oded.redlich@huawei.com

## Slide 2: Introduction
802.11be discussed Multi-AP coordination as a set of features that will yield additional efficiency gain and increased throughput when multiple OBSS share resources for a coordinated transmission
There were several high-level discussions and analyses of various M-AP coordination schemes; however, the main development phase was not carried out within the scope of 802.11be
Preliminary discussions in the UHR SG show high interest in this topic
In this contribution we want to share our thoughts on the benefits that M-AP coordination should provide (regardless of the coordination scheme) and the principles that lead to an efficient coordinated M-AP transmission in UHR and beyond

## Slide 3: Short Recap
In [1] and [2] TGbe agreed on the following two main roles for APs that participate in a coordination [3]:
  Sharing AP – the TXOP holder that shares its resources with other APs
  Shared APs – all the APs allocated with resources for coordinated transmission by the Sharing AP
The roles above are dynamic: A single AP is designated as a Sharing AP in a TXOP it obtains and can be designated as a Shared AP in a TXOP obtained by other APs
There are several coordination schemes discussed and considered as candidate schemes: Co-TDMA ,Co-OFDMA, Co-SR, Co-BF, JT and Co-UL MU-MIMO [4], [7] – [9]
In most of the discussions it was assumed that all the coordinated transmissions are triggered by the Sharing AP
Some contributions also discussed the overhead required to manage the coordinated transmissions

## Slide 4: Benefits of M-AP Coordination
The following benefits are expected as a result of Multi-AP coordination:
  More efficient use of resources – when the AP obtains the TXOP, it proposes to share its resources with other (OBSS) APs that have not obtained the TXOP; this yields more opportunities for every AP to transmit or trigger a transmission within its BSS.
  Lower OBSS Interference – coordinating the resources (e.g. time, frequency, spatial) between APs leads to reduced interference in each of the involved OBSSs and therefore improves the reliability
  Handling latency-bounded traffic – since each BSS gains access to the WM more often, we can address dynamic latency-bounded traffic patterns.
From the perspective of an individual AP, there is motivation to coordinate with OBSS APs in order to achieve the benefits listed above

## Slide 5: Schematics for M-AP coordinated transmissions
No Coordinated transmissions
Co-TDMA
Co-SR
Notes:
  AP5 and AP6 are not taking part in the coordination
  We can see that it is in the best interest of an AP to cooperate
  For simplicity, the duration of TXOP holder remains unchanged in all diagrams.

## Slide 6: (Reciprocal) Resource Sharing Guarantee
In the context of a single TXOP, the M-AP coordination gains are realized by the shared APs when they use the resources shared with them by the sharing AP (in practice, the sharing AP is “giving up” some of its resources)
An AP would agree to become a sharing AP and “give up” part of the resources in the TXOP it obtains only if there is a guarantee – by other APs - that they will share some of their resources with it when they will obtain a TXOP
A key factor here is that an AP knows that if it shares its resources (acts as a Sharing AP) with other APs, then these APs will share resources with it later on (so it will become a Shared AP)
This key factor might be achieved if some kind of mutual agreement between APs is implemented – if you get some resources now, you will also share your resources in the future

## Slide 7: M-AP Coordination Agreement
A M-AP coordination agreement is established between all the APs that will participate in the coordinated transmission.
  An AP enters into an agreement with an intent to take part in the coordinated transmission.
Once the agreement is established, each AP guarantees to share its resources with other APs that are part of the agreement - when it obtains the TXOP (i.e. when it becomes the sharing AP)
This way, each AP that is a member of a M-AP coordination agreement is guaranteed that resources will be shared with it in TXOPs obtained by OBSS APs (that are members of this agreement).

## Slide 8: Summary
This contribution presents the benefits of M-AP coordinated transmission
The guarantee that an AP can be a Shared AP during TXOPs obtained by an OBSS AP is a key motivation for the AP to share its resources when it obtains the TXOP (act as a Sharing AP)
We present a M-AP coordination agreement as a pre-requisite for a M-AP coordinated transmission

## Slide 9: References
[1] 11-20-0566-99-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[2] 11-20-1935-66-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2
[3] 11-20-1895-02-00be-setup-for-multi-ap-coordination
[4] 11-20-0560-00-00be-multi-ap-configuration-and-resource-allocation
[5] 11-19-1931-02-00be-multi-ap-group-formation-follow-up
[6] 11-19-1582-02-00be-coordinated-ap-time-and-frequency-sharing-in-a-transmit-opportunity-in-11be
[7] 11-19-1919-03-00be-coordinated-ofdma
[8] 11-20-0548-02-00be-discussion-on-coordinated-ul-mu-mimo
[9] 11-22-1895-00-00uhr-thoughts_on_map_assumptions
[10] 11-23-0293-00-00uhr-Follow-up on TWT-based Multi-AP Coordination