## Slide 1: Discussion on C-OFDMA
Date: 2023-05-15
Authors:
Name | Affiliation | Address | Phone | Email
Jinyoung Chun | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jiny.chun@lge.com
Eunsung Park |  |  |  | 
 |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | 
 |  |  |  | dongguk.lim@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
SunHee Baek |  |  |  | sunhee.baek@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10225 Willow Creek Rd, San Diego, CA, USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
In March Meeting, UHR PAR was finalized with the below scopes in scenarios of an isolated BSS or of overlapping BSSs [1].
  increasing throughput at different SINR level
  improving the tail of the latency distribution and jitter with mobility between BSSs
  and improving efficient use of medium in scenario of overlapping BSSs.
C-OFDMA is the scheme that Multiple APs transmits/receives data in the allocated frequency resource of the whole bandwidth.
  It can increase SINR gain (1st scope) because the OBSS AP doesn’t use the frequency resource that BSS AP uses. Moreover, the efficient use of medium can be improved (3rd scope) with C-SR scheme, for OBSS AP by reusing the frequency resource.
Here we’d like to discuss some issues of C-OFDMA operation, especially about the size of the allocated frequency resource.

## Slide 3: Issues of C-OFDMA
C-OFDMA scheme has some benefits
  It has some throughput gain than SU, especially with wired backhaul [2].
  Combining C-SR and C-OFDMA can achieve even better system performance [3].
  We can get some latency improvement by transmitting latency-sensitive traffic in time.
Despite of the benefits, it still has some issues
  Sharing AP has to schedule and allocate the medium to Shared APs. It brings Sharing AP’s burden and backhaul burden.
  For that, some information such as channel status or buffer status of Shared APs is prepared and shared.
  PPDU for C-OFDMA may be newly needed. It’s related to the minimum frequency unit per AP.
Here, we discuss more about the 3rd issue in view of scheduling and PPDU format.

## Slide 4: Basic Procedure of C-OFDMA (1/2)
For the discussion, the basic Definition & Assumptions are as below.
  An UHR AP which obtains a TXOP and initiates the multi-AP coordination is the sharing AP.
  An UHR AP which is coordinated for the multi-AP transmission by the sharing AP is the shared AP.
  Sharing AP can be one of shared APs and can be changed.
  Some or all associated STAs can’t be hear the signal from Sharing AP and/or other Shared APs.
  The basic procedure of C-OFDMA is as below.
  The procedure can be changed (omitted or added some information or signalling) by several issues. (See the next slide.)

## Slide 5: Basic Procedure of C-OFDMA (2/2)
Preparation: Need some information sharing/negotiation before C-OFDMA operation
  between Sharing AP & Shared AP(s): e.g. request/report the channel status, request/announce/confirm the allocated frequency resource or service period of C-OFDMA operation, etc.
  and between Shared AP & the associated STA(s): e.g. request/report the channel status information, request/announce/confirm the operating frequency resource of Shared AP or service period of C-OFDMA operation, etc.
Set TXOP sharing: May set the TXOP sharing SP if C-OFDMA transmission is permitted in a certain service period
  There are several contributions to extend TWT for Multi-AP operation [3-4].
DL Trigger frame: Sharing AP triggers for the Shared APs to transmit their signals at the same time
  It’s new type of Trigger frame to trigger DL PPDU. And the existence depends on the scheduling method. (See the next slides.)
DL C-OFDMA PPDU: Shared AP transmits own signals in the allocated frequency resource in advance
  The format depends on the minimum allocated frequency resource per AP. See the next slide.
UL C-OFDMA PPDU: STA may transmit own signals in response of DL C-OFDMA PPDU
  The format is similar to TB PPDU.

## Slide 6: The Minimum Frequency Unit per AP
The C-OFDMA procedure can be applied differently by the minimum resource unit for C-OFDMA, which means the minimum frequency resource allocated to each Shared AP.
The resource unit has an effect on the DL C-OFDMA PPDU format (e.g. the SIG design), PPDU alignment, Scheduling method, and so on.
So we’ll analyse the scheduling method or PPDU format, etc in case that the resource unit is 80 MHz and 20 MHz, respectively.
  The case of under 20 MHz is not considered because
    it’s very hard that Sharing AP schedules the proper Small RU(s) to Shared APs every C-OFDMA operation
    and it may need to make new U-SIG and EHT-SIG of C-OFDMA PPDU to transmit the PPDU from several Shared APs in the same 20 MHz channel.
  Case 1: 80MHz unit
  Case 2: 20MHz unit

## Slide 7: 80 MHz Resource Unit (1/2)
Case 1: 80 MHz unit
  The signals from Shared APs are not mixed in 80 MHz channel. Sharing AP allocates the resource in unit of 80 MHz to each Shared APs, and the Shared APs communicates with the associated STAs within the unit(s).
  We can’t get the scheduling gain enough due to a few candidate units.
    Only 2 Shared APs can be operated if the operating BW is 160MHz.
    Shared AP supporting equal or larger 160 MHz operating BW can join the procedure.
  DL C-OFDMA PPDU
    We can use DL MU PPDU format. It means, we may use U-SIG design of 11be as it is.
      In 11be spec says “For EHT MU PPDU, the U-SIG field content shall be identical in all nonpunctured 20 MHz subchannels within each 80 MHz frequency subblock, and the U-SIG field content in different 80 MHz frequency subblocks may be different.”
    So each AP transmits AP-specific U-SIG with own BSS color and own contents in the allocated 80 MHz units.
  STA’s operation
    STA can receive the C-OFDMA PPDU from own BSS AP (Shared AP) by
      decoding U-SIG every 80 MHz channels and finding own BSS color.
      , decoding U-SIG in the indicated frequency resource from Shared AP during preparation such as SST operation.
      or decoding U-SIG in the primary 20 MHz if Shared APs has the different primary 20 MHz channel each other and the Sharing AP allocates the 80 MHz unit(s) including each Shared AP’s primary channel to Shared APs. (For that, primary channel switching can be considered.)

## Slide 8: 80 MHz Resource Unit (2/2)
  Scheduling method
    Static scheduling
      Shared AP can know its allocated unit(s) and C-OFDMA SP during the preparation by TWT operation.
        For example, Sharing AP and Shared AP may set up SST operation by negotiating a trigger-enabled TWT.
          The current SST is for AP and STA. But we can extend it for Sharing AP and Shared AP. (it needs FFS.)
        For example, Sharing AP can announce r-TWT SPs with the frequency unit to Shared APs.
          The current r-TWT is for AP and STA. But we also can extend it for Sharing AP and Shared AP. There are several contributions to apply it for Multi-AP operation [4-5].
      DL C-OFDMA PPDUs among shared APs may not need to be aligned if Shared AP communicates with the associated STAs freely without any control of Sharing AP during SP. (Strictly speaking, it’s C-FDMA, not C-OFDMA.)
      Some way needs for the associated STAs to know the allocated units in advance and camp to the units in SP. (refer the previous STA’s operation.)
    Dynamic scheduling
      Shared AP can be scheduled by RU allocation field in DL Trigger frame from Sharing AP.
      We need to define new DL Trigger frame to trigger DL PPDUs of Shared AP, which has to be aligned with OFDMA manner.
      It may be difficult that the associated STAs which can’t receive the DL Trigger frame, know the unit(s) before every DL Trigger frame (the ② method in the precious STA’s operation).
      The dynamic scheduling may not be useful in 80 MHz unit.

## Slide 9: 20 MHz Resource Unit (1/2)
Case 2: 20 MHz unit
  The signals from Shared APs are not mixed in 20 MHz channel. Sharing AP allocates the resource in unit of 20 MHz to each Shared APs, and the Sharing APs communicates with the associated STAs within the unit(s).
  We can get the scheduling gain than 80 MHz unit.
    The maximum 8 Shared APs can operated together if the operating BW is 160MHz.
    The channel information in unit of 20 MHz between Shared AP and the associated STA has to be shared to Sharing AP.
  DL C-OFDMA PPDU
    Shared APs transmit own C-OFDMA PPDUs in the allocated 20 MHz unit(s) by Sharing AP.
    If we follows the current U-SIG design with duplication, we can make a united U-SIG. Or we can make AP-specific U-SIG.
    Option1. United U-SIG
      U-SIG is duplicated on every 20 MHz and includes the united information of Shared APs such as
        a BSS color for the C-OFDMA transmission (e.g. set to Sharing AP’s BSS color, or set to pre-defined value for the C-OFDMA operation or the C-OFDMA group)
        A max. bandwidth among Shared APs or a bandwidth of Sharing AP
        A united punctured channel information among Shared APs. (e.g. channel information that all Shared APs puncture)
      Each Shared AP transmits own EHT-SIG with the information for the associated STAs in the allocated resource unit.
        It’s not good to make a united EHT-SIG because AID can’t be shared among Shared APs.

## Slide 10: 20 MHz Resource Unit (2/2)
      For the STAs to decode the EHT-SIG, Each ID info and the allocated 20 MHz unit(s) of each Shared AP may be signaled before.
        For example, it can be done by making a new SIG or by adding the info in disregards/validates bits of U-SIG or EHT-SIG, etc.
        The signaling may not be needed if the Shared APs has the different primary 20 MHz channel within the whole BW and sharing AP allocates frequency resource including own primary channel to each AP.
      DL C-OFDMA PPDUs among shared APs shall be aligned.
      STA can decode the U-SIG and EHT-SIG as 11be STA does.
    Option2. AP-specific U-SIG
      Each AP transmits own U-SIG with own BSS color and own BSS information in the allocated 20 MHz unit(s).
      STA can receive the C-OFDMA PPDU from own BSS AP by
        decoding all U-SIGs on every 20 MHz channels. It causes STA’s decoding burden.
        decoding U-SIG on own primary channel. It requires that all participating APs has the different primary 20 MHz channel within the whole BW and sharing AP allocates frequency resource including own primary channel to each AP.
        decoding U-SIG on BSS AP’s allocated unit(s). It requires that the STA has to know the resource unit(s) in advance by BSS AP’s signalling.
      PPDUs among shared APs may not need to be aligned.
  Scheduling method
    We can apply both of static and dynamic scheduling in the previous slide.
    The dynamic scheduling may be more useful in 20 MHz unit.

## Slide 11: Summary
The C-OFDMA operation is an useful scheme but still has some problems to be solved. Here, we addressed the issue by the minimum frequency unit per AP.
  If the unit is 80 MHz, we may not get scheduling gain enough. But we don’t need any PHY change and may use the static scheduling.
  If the unit is 20 MHz, We can get scheduling gain and both of dynamic and static scheduling can be applied. But it may need PPDU format change for DL C-OFDMA PPDU.
There’s some trade-off between scheduling gain and PPDU configuration. Therefore some discussion is needed in UHR group.

## Slide 12: Reference
[1] 11-23/0480r0, “UHR Proposed PAR”
[2] 22/1567r0, “C-OFDMA throughput analysis in various mesh backhaul scenarios”
[3] 11-23/0058r0, “Spatial Reuse in Coordinated M-AP for UHR”, Rui Yang
[4] 11-23/0297r0, “r-TWT for Multi-AP”, Laurent Cariou
[5] 11-23/0250r0, “AP coordination for R-TWT”, Liwen Chu