## Slide 1: Coordinated R-TWT Protection in Multi-BSS
Date: 2023-06-11
Authors:
Name | Affiliation | Address | Phone | Email
SunHee Baek | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | sunhee.baek@lge.com
Insun Jang |  |  |  | 
 |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | 
 |  |  |  | js.choi@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10225 Willow Creek Rd, San Diego, CA, USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
In 11be, the R-TWT is defined in perspective of transmission of latency sensitive traffic in a single BSS.
  It may be a problem when STAs exchange the latency sensitive traffic in an actual use environment (e.g. several adjacent BSSs are overlapping).
  If OBSS service period occupies channel in the single BSS, STA fails to take its TXOP because the channel is busy during the service period.
  However, R-TWT in the Multi-BSS is excluded because of the plenty of the considerations for R-TWT scenarios and defer of Multi-AP in 11be spec.
In this contribution, we share considerations of protection for R-TWT service periods in Multi-BSS.

## Slide 3: Re-cap: R-TWT in 11be
In EHT, R-TWT service period(SP) is scheduled to deliver latency sensitive traffic.
  The schedule information of R-TWT SPs assigned by only associated AP is announced through Beacon frame.
The important points of R-TWT in 11be are
  R-TWT SP Protection Methods
    For EHT STA supporting R-TWT, a TXOP holder ends its TXOP before the start time of R-TWT SPs that are advertised by its associated AP
    For Pre-EHT or EHT STA not supporting R-TWT, the overlapping quiet interval is scheduled by its associated AP at the same time as the R-TWT SP.
  R-TWT Traffic Indication Method
    R-TWT TIDs identify the TIDs that carry latency sensitive traffic for R-TWT membership being set up in the Restricted TWT Traffic Info field of TWT element.

## Slide 4: R-TWT in Multi-BSS(OBSS)
In the Multi-BSS environment, STAs in a BSS can get affected by the other neighboring BSSs.
There is no way to coordinate R-TWT SPs of each BSS in Multi-BSS.
  The current 11be spec focuses on protecting R-TWT SPs in the single BSS.
EHT STAs(APs) cannot handle the schedule information of R-TWT in Multi-BSS.
  To distinguish between R-TWT SP scheduled by the associated AP and R-TWT SP by the neighboring APs, the latter R-TWT SP named OBSS R-TWT SP in this contribution.
  Some contributions, [1] ~ [5], were presented about that UHR requires to consider OBSS R-TWT SPs.

## Slide 5: How to receive OBSS R-TWT schedule information
An AP can announce its R-TWT schedule information of the neighboring APs depending on the cases below;
  We can assume the AP can obtain the information through a management entity.
    The management entity means an entity to manage between APs.
  Otherwise, the APs can obtain the information through negotiation between APs.
    It is assumed that the negotiation between APs is possible.
An AP can obtain the neighboring APs’ schedule information of R-TWT through the associated STAs.
  The associated STAs located in the range of OBSS can check the R-TWT schedule information in the overhearing Beacon frame of the neighboring AP.
  Then, the STAs can announce the information to the associated AP.

## Slide 6: OBSS R-TWT SP protection - STA Types -
Based on whether STA supports (OBSS) R-TWT, the STAs can classify like below;
  Pre-EHT STA or EHT STA not supporting R-TWT
  EHT STA supporting R-TWT
  UHR STA not supporting R-TWT
    Although this STA type is one of the possible cases, the UHR STA is recommended to support mandatory R-TWT.
  UHR STA supporting R-TWT
  UHR STA supporting enhanced R-TWT
    Enhanced R-TWT means additional features defined in UHR, including OBSS R-TWT SP Protection.
Defined in 11be spec
Need to consider
possible cases

## Slide 7: OBSS R-TWT SP protection - Protection Rules -
The OBSS R-TWT SP can be protected depending on the type of STAs as follows;
  For Pre-EHT STA, EHT STA or UHR STA not supporting R-TWT, the overlapping quiet interval may be used to protect OBSS R-TWT SP as defined in 11be.
    However, it is expected that this can result in some issues, e.g., complex quiet IE, unnecessary protection in the case where the STA is not affected by the frame exchanges in the OBSS R-TWT SP.
    We may not handle them with the assumption where the STAs barely exist
  For EHT STA or UHR STA supporting R-TWT (not supporting enhanced R-TWT), we may design a method where the STAs can recognize OBSS R-TWT SP as R-TWT SP in 11be to protect OBSS R-TWT SP
    It is expected that the STAs can ensure their TXOP ends before the start time of (OBSS) R-TWT SPs

## Slide 8: OBSS R-TWT SP protection - Protection Rules -
  For UHR STA supporting enhanced R-TWT, its TXOP is stopped before the start time of OBSS R-TWT SP.
    Based on this rule, exceptional rules can be defined to schedule between BSS’s SP and OBSS R-TWT SP.
AP 1
AP 2
STA 1
STA 2
associated with AP 1
associated with AP 2
Beacon
= Neighboring AP
Announces R-TWT SPs in its own BSS and AP 1’s BSS
Beacon
Announces R-TWT SPs in its own BSS and AP 2’s BSS
R-TWT SP for STA2
TXOP of STA 1
Trigger
Data

## Slide 9: OBSS R-TWT SP protection - Further Consideration of Protection Rule -
The exceptional rules are needed to protect both associated STA’s SP and OBSS R-TWT SP.
  If STAs(STA1-1, STA1-3) are not located in the range of OBSS, they don’t follow the protection rules of OBSS R-TWT SP.
    The STA unsolicitedly announces that it isn’t located in the range of OBSS to the associated AP.
      For example, STA1-1 announces to AP1 that it has not received any data/traffic or received it with some threshold level(that is, doesn’t affect AP1’s BSS) having a different BSS color from AP1 for a certain period of time.
overhearing
association
AP 1
AP 2
STA1-1
STA1-2
STA1-3
STA2-1
STA2-2
STA2-3
STA2-4
When an AP schedules SPs to associated STAs based on OBSS R-TWT schedule information, it doesn’t make the SPs overlap if the neighboring AP’s SP affects the STAs(STA1-2) or if the BSS’s SP affects the STAs(STA2-4) associated with the neighboring AP.

## Slide 10: Summary
In UHR, the R-TWT is needed to cover to protect both R-TWT SP and OBSS R-TWT SP in Multi-BSS.
In this contribution, we shared the considerations about protection methods for OBSS R-TWT SP.
  Basic rules for protecting OBSS R-TWT SP per STA types.
  Exceptional rules to protect both BSS’s SP and OBSS R-TWT SP .

## Slide 11: References
  [1] 23/226 Coordination of R-TWT for Multi-AP Deployment
  [2] 23/250 AP coordination with R-TWT
[3] 23/297 rTWT for Multi-AP
[4] 23/291 R-TWT Multi-AP Coordination
[5] 23/293 Follow-up on TWT-based Multi-AP Coordination