## Slide 1: Performance of C-BF and C-SR
Date: 2023-06-21
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 
Karim Toussi | Broadcom |  |  | 

## Slide 2: Introduction
Previously analyzed joint transmission
In this contribution added simulation results for two coordinated schemes that can improve spectral efficiency, namely C-BF and C-SR. Scenarios and methodology is taken from our JT simulations (e.g. 22/2188)

## Slide 3: Simulation Assumptions
2-AP (4x4), each with 1, 2 or 3 STA (2x2), and 4-AP each with 1 STA 80MHz BW, 11nD,
  SNR measured between STA and stronger AP (“serving AP”): range 10:35dB
  Path-loss differential X between stronger AP and weaker AP: range 0:30dB
Baseline - single-AP (SU or MU-MIMO) + TDMA (implicitly assumes AP are not too far)
C-SR – both AP transmit at the same time with same power as in baseline (see Appendix A for discussion on maximizing sum capacity by maximizing Tx power).
C-BF: as with C-SR with additional spatial nulling to reduce OBSS interference
STA payload processing – assumes knowledge of the per-tone interference for C-BF and C-SR with MMSE receiver (interference estimation during LTF of coordinated PPDU)
“Genie” MCS prediction: assuming full CSI, precoder knowledge and MMSE Rx, for both CBF and CSR (CBF: similar to DL MUMIMO, CSR: beyond just RSSI/path-loss info)
Generic impairments: as in our JT sims in 22/2188, e.g.
  Channel aging (-30dBc)
  NDP channel estimation error (no smoothing).
Simulation output: Throughput ratio (C-BF/baseline, C-SR/baseline) shown in a 2-D table: f(SNR, X). Each cell has C-BF results (on top), C-SR (bottom) and gains for different total Nss values.

## Slide 4: Notes on Nulling in C-BF
With 2x2 STA we can fully null a signal towards the STA’s two antennas or partially null in one certain direction
With 4x4 AP full nulling is quite limited (e.g. null towards one OBSS STA and transmit towards one BSS STA)  partial nulling provides a lot more options to use C-BF and higher gains as shown in the simulation results
For partial nulling used joint sounding for accurate precoder calculation (see Appendix B)
Simulations used an MMSE precoder  more suitable than ZF since MMSE de-weights the nulling based on I+N and enables higher BF gain.

## Slide 5: Scenario 1 - Two AP, One STA per AP
Baseline Nss = [1], [2]
  Nss = 2 best for SNR >= 20dB, Nss = 1 best for SNR <= 15dB
CBF/CSR Nss = [1; 1], [2; 2]
  A total of 2ss or 4ss across AP

## Slide 6: Scenario 1 - Tput Ratios
Throughput ratio for C-BF and C-SR with a total of [2ss, 4ss] (higher number in bold), (red C-BF>1.1xC-SR)
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (dB) | 0 | 1.17, 1.19 | 1.18, 1.12 | 1.33, 0.99 | 1.35, 0.85 | 1.80, 0.79 | 1.63, 0.42
 |  | 1.13, 0.09 | 1.10, 0.10 | 1.19, 0.11 | 1.25, 0.13 | 1.45, 0.13 | 1.33, 0.03
 | 5 | 1.18, 1.34 | 1.21, 1.26 | 1.33, 1.10 | 1.35, 0.95 | 1.80, 0.99 | 1.68, 0.72
 |  | 1.14, 0.27 | 1.11, 0.30 | 1.20, 0.38 | 1.27, 0.47 | 1.53, 0.59 | 1.50, 0.46
 | 10 | 1.19, 1.41 | 1.23, 1.36 | 1.35, 1.25 | 1.35, 1.10 | 1.81, 1.20 | 1.84, 1.01
 |  | 1.15, 0.47 | 1.13, 0.53 | 1.22, 0.64 | 1.30, 0.78 | 1.68, 1.02 | 1.73, 0.96
 | 15 | 1.19, 1.47 | 1.24, 1.47 | 1.35, 1.48 | 1.35, 1.32 | 1.86, 1.41 | 1.98, 1.26
 |  | 1.15, 0.82 | 1.14, 0.90 | 1.26, 1.02 | 1.34, 1.12 | 1.82, 1.36 | 1.96, 1.24
 | 20 | 1.19, 1.58 | 1.24, 1.55 | 1.35, 1.66 | 1.39, 1.58 | 1.91, 1.54 | 
 |  | 1.17, 1.24 | 1.16, 1.33 | 1.31, 1.52 | 1.38, 1.53 | 1.91, 1.53 | 
 | 25 | 1.19, 1.72 | 1.25, 1.63 | 1.35, 1.86 | 1.47, 1.82 |  | 
 |  | 1.18, 1.46 | 1.21, 1.57 | 1.35, 1.83 | 1.46, 1.81 |  | 
 | 30 | 1.19, 1.85 | 1.29, 1.76 |  |  |  | 
 |  | 1.19, 1.76 | 1.27, 1.73 |  |  |  | 
Large difference of AP-STA paths loss relative to SNR

## Slide 7: Observations (1)
C-SR works well when X>=SNR (or SNR-5 in some cases)
  not exactly a function of AP-AP separation
  Logic – when the interference from AP2 is at the noise level or below
In the particular case of C-SR with Nss=[1; 1] the STA is able to cancel the rank-1 interference (note the stable gain at any X and SNR)
   That is one benefit of synchronization when compared to 11ax style opportunistic SR
AP1
AP2
STA
SNR
SNR-X  SNR from AP2<=0dB

## Slide 8: Observations (2)
C-BF shows particular strong gain for SNR<=15dB because the baseline only supported Nss=1 so potential for doubling with C-BF
C-BF provides significantly higher rates than C-SR for X<=SNR-10
   Logic – when the interference from AP2 is strong enough for nulling to provide benefit
AP1
AP2
STA
SNR
SNR-X  SNR from AP2 > =10dB

## Slide 9: Scenario 2 - Two AP, Two STA per AP
Baseline Nss = [1], [2], [1 1], [2 1]
  Nss = [2 1] best for SNR >= 25dB, Nss = [1 1] best for SNR <= 20dB
C-SR Nss = [1; 1], [1 1; 1 1], [2 1; 2 1]
C-BF: Nss = [1; 1], [1 1; 1 1] (with C-BF limited to a total of Nss=4)

## Slide 10: Scenario 2 - Tput Ratios
Throughput ratio for C-BF and C-SR with a total of [2ss, 4ss, 6ss] (higher number in bold), (red C-BF>1.1xC-SR)
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (dB) | 0 | 0.96, 1.16 | 0.99, 1.23 | 1.12, 1.28 | 1.07, 1.05 | 1.40, 1.08 | 1.39, 1.15
 |  | <1 | <1 | <=1 | <1 | 1.13, 0.76, 0.18 | 1.13, 0.92, 0.20
 | 5 | 0.97, 1.25 | 1.02, 1.30 | 1.13, 1.39 | 1.06, 1.19 | 1.40, 1.22 | 1.43, 1.43
 |  | <1 | <1 | <=1 | <=1 | 1.19, 1.04, 0.48 | 1.27, 1.35, 0.44
 | 10 | 0.98, 1.32 | 1.03, 1.34 | 1.14, 1.49 | 1.06, 1.38 | 1.40, 1.45 | 1.56, 1.62
 |  | <1 | <1 | <=1 | 1.02, 1.09, 0.73 | 1.30, 1.34, 0.91 | 1.47, 1.63, 0.82
 | 15 | 0.98, 1.41 | 1.04, 1.39 | 1.14, 1.59 | 1.06, 1.60 | 1.44, 1.76 | 1.68, 1.80
 |  | <=1 | 0.96, 1.14, 0.88 | 1.07, 1.38, 1.03 | 1.05, 1.46, 1.08 | 1.41, 1.71, 1.21 | 1.67, 1.86, 1.06
 | 20 | 0.98, 1.49 | 1.04, 1.51 | 1.14, 1.68 | 1.10, 1.79 | 1.48, 1.88 | 
 |  | 0.96, 1.22, 1.21 | 0.98, 1.35, 1.30 | 1.11, 1.62, 1.46 | 1.09, 1.74, 1.38 | 1.48, 1.87, 1.42 | 
 | 25 | 0.98, 1.55 | 1.05, 1.66 | 1.14, 1.77 | 1.16, 1.92 |  | 
 |  | 0.97, 1.45, 1.58 | 1.02, 1.57, 1.68 | 1.14, 1.75, 1.82 | 1.15, 1.91, 1.58 |  | 
 | 30 | 0.98, 1.63 | 1.08, 1.75 | 1.14, 1.92 |  |  | 
 |  | 0.98, 1.59, 1.79 | 1.07, 1.74, 1.90 | 1.14, 1.91, 1.98 |  |  | 
Large difference of AP-STA paths loss relative to SNR

## Slide 11: Observations
In this case the baseline never drops to SU Nss=1 so gains of both C-SR and C-BF are not as high for SNR=10 and 15dB
For C-SR Nss = [2 1; 2 1] is best only for SNR >= 25dB and X >= 25dB. Otherwise, Nss = [1 1; 1 1] is mostly best.
  However note unlike scenario 1 the interference is not rank-1 so STA can’t completely null it
As in the previous scenario C-BF is better than C-SR in the top left triangle, meaning X<=SNR-10 or 15 ( SNR from AP2 is at least 10 or 15dB)
Notes:
  For C-BF we also simulated the case of limiting to two STA with full rank nulling but the gains were much lower (see Appendix C)  high benefit for partial-rank nulling
  The scenario with 3STA per AP is in Appendix D – gains are more muted but still exist for C-BF even at low values of X

## Slide 12: Scenario 3 - Four AP, one STA per AP
Baseline Nss = [1], [2]
  Nss = 2 best for SNR >= 20dB, Nss = 1 best for SNR <= 15dB
C-SR Nss = [1; 1], [1; 1; 1], [1; 1; 1; 1], [2; 2; 2; 2]
C-BF: Nss = [1; 1], [1; 1; 1], [1; 1; 1; 1]

## Slide 13: Scenario 3 - Tput Ratios
Throughput ratio for C-BF and C-SR with a total of [2ss, 3ss, 4ss, 8ss] (higher number in bold and x denotes lower number), (red C-BF>1.2xC-SR, 1.1xC-SR)
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (dB) | 0 | x, 1.42, 1.42 | x, 1.52, 1.51 | x, 1.63, 1.60 | x, 1.84, 1.45 | 1.80, 1.95, x | x, 1.82, 1.67
 |  | 1.13, 0.34, x, x | 1.10, 0.38, x, x | 1.19, 0.48, x, x | 1.25, 0.61, x, x | 1.45, 0.89, x, x | 1.33, 1.15, x, x
 | 5 | x, 1.54, 1.63 | x, 1.58, 1.61 | x, 1.70, 1.76 | x, 1.87, 1.71 | x, 2.07, 1.86 | x, 1.95, 2.08
 |  | 1.14, 0.61, x, x | 1.11, 0.67, x, x | 1.20, 0.82, x, x | 1.27, 0.98, x, x | 1.53, 1.34, x, x | x, 1.67, 1.68, x
 | 10 | x, 1.63, 1.79 | x, 1.61, 1.69 | x, 1.75, 1.91 | x, 1.92, 2.07 | x, 2.30, 2.39 | x, 2.27, 2.55
 |  | 1.15, 0.92, x, x | 1.13, 1.01, x, x | 1.22, 1.24, x, x | x, 1.47, 1.36, x | x, 1.92, 1.90, x | x, 2.12, 2.41, x
 | 15 | x, 1.68, 1.88 | x, 1.63, 1.87 | x, 1.81, 2.02 | x, 1.98, 2.38 | x, 2.59, 2.98 | x, 2.81, 3.15
 |  | 1.15, x, 1.25, x | x, 1.25, 1.39, x | x, 1.51, 1.70, x | x, 1.84, 2.08, x | x, 2.47, 2.76, x | x, 2.76, 3.05, x
 | 20 | x, 1.72, 1.96 | x, 1.66, 2.06 | x, 1.92, 2.21 | x, 2.01, 2.62 | x, 2.81, 3.54 | 
 |  | x, x, 1.54, 1.42 | x, x, 1.69, 1.55 | x, x, 2.04, 1.85 | x, x, 2.56, 2.12 | x, 2.79, 3.48, x | 
 | 25 | x, 1.77, 2.10 | x, 1.73, 2.14 | x, 2.00, 2.52 | x, 2.10, 2.68 |  | 
 |  | x, x, 1.89, 2.33 | x, x, 2.07, 2.51 | x, x, 2.42, 2.90 | x, x, 2.68, 3.00 |  | 
 | 30 | x, 1.79, 2.31 | x, 1.83, 2.30 | x, 2.03, 2.69 |  |  | 
 |  | x, x, 2.15, 2.86 | x, x, 2.23, 3.12 | x, x, 2.68, 3.62 |  |  | 
Large difference of AP-STA paths loss relative to SNR

## Slide 14: Observations
The case of 4AP with one stream per STA exhibits even higher gains for C-BF.
Compared to scenario 1 the baseline performance is the same (1 STA per AP) but the STA needs to decode 2ss in scenario 1 versus 1ss in scenario 3
Compared to scenario 2 there are the same total number of STA and the difference is 2AP vs. 4AP:
  In scenario 2 each AP splits its power between 2 STA but in scenario 3 full power goes into one STA
  The baseline in scenario 2 (2 STA per AP) is higher which means lower gains
  In scenario 3 there are more total, across AP, antennas which can improve diversity

## Slide 15: Summary
We have provided simulation results for both C-BF and C-SR.
For C-SR gains are essentially dependent on the relative separation of a STA from its BSS vs. the OBSS.
  We observe that gains increase significantly as X crosses a threshold for mid to high SNR
  Gains will diminish if AP-AP link level <-82dBm as baseline isn’t TDMA anymore
For C-BF the two main observations are:
  With 4x4 AP and 2x2 STA it’s important to enable partial nulling to maximize the benefit of this technology
  Compared to C-SR, benefit is seen when the SNR to the OBSS is at least 10dB enabling the gains from spatial nulling  strong and consistent gains in this region
For both schemes interference nulling at the STA improves performance

## Slide 16: Appendix A – Sum Capacity of 2AP C-SR
C-SR - Unlike other presentations we don’t have excess (above highest MCS) SNR reduction in power = reduction in interference and desired signal equally
Plots below assume AP1 power normalized to 1. If AP2 power = 0 TDMA, if AP2 power = 1  simulated in this contribution.
Sum capacity (yellow) always maximized at either TDMA or AP2 power = 1, any AP2 power level in between leads to reduced sum capacity. If X<=SNR/2 (in dB) TDMA is optimal, can be extended to N AP: X <= SNR/N + ~10*log10(N-1).

## Slide 17: Appendix B – CBF with Joint vs. Sequential Sounding
AP1
AP2
STA
Joint – USV’ (e.g. 2x8)
AP1
STA
Sequential – U1S1V1’ (e.g. 2x4)
AP2
STA
Sequential – U2S2V2’ (e.g. 2x4)
As in DL MU-MIMO feeding back global S and V is optimal
If only part of SiVi are used for BF or Nulling,
feeding back per-AP SiVi is suboptimal due to loss of info in U1 and U2.
Can be solved with feedback of U1’ U2
For a given STA:

## Slide 18: Appendix C - CBF gains with 2 vs 4 STAs
Nss = [2+2, 1+1+1+1]
Why the gains of partial rank nulling? With rank-1 transmission 2x2STA MMSE Rx reduces interference. With rank-2 transmission and 4x4 AP, channel is not well conditioned as ‘2 antennas’ are spent on nulling.
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (db) | 0 | 0.98, 1.16 | 0.94, 1.23 | 0.83, 1.28 | 0.67, 1.05 | 0.61, 1.08 | 0.36, 1.15
 | 5 | 1.10, 1.25 | 1.06, 1.30 | 0.93, 1.39 | 0.75, 1.19 | 0.77, 1.22 | 0.61, 1.43
 | 10 | 1.16, 1.32 | 1.14, 1.34 | 1.05, 1.49 | 0.87, 1.38 | 0.93, 1.45 | 0.86, 1.62
 | 15 | 1.21, 1.41 | 1.24, 1.39 | 1.25, 1.59 | 1.04, 1.60 | 1.09, 1.76 | 1.07, 1.80
 | 20 | 1.30, 1.49 | 1.31, 1.51 | 1.41, 1.68 | 1.24, 1.79 | 1.19, 1.88 | 
 | 25 | 1.41, 1.55 | 1.37, 1.66 | 1.57, 1.77 | 1.43, 1.92 |  | 
 | 30 | 1.52, 1.63 | 1.48, 1.75 | 1.64, 1.92 |  |  | 

## Slide 19: Appendix D - Three STA per AP
Baseline Nss = [1], [1 1], [1 1 1]
  Nss = [1 1 1] best for SNR >= 20dB, Nss = [1 1] best for SNR <= 15dB
C-SR Nss = [1; 1], [1 1; 1 1], [1 1 1; 1 1 1]
C-BF: Nss = [1; 1], [1 1; 1 1] (with C-BF limited to a total of Nss=4)

## Slide 20: Tput Ratios
Throughput ratio for C-BF and C-SR with a total of [2ss, 4ss, 6ss] (higher number in bold), (red C-BF>C-SR)
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (dB) | 0 | 0.88, 1.06 | 0.90, 1.12 | 0.94, 1.07 | 1.01, 1.00 | 1.40, 1.08 | 1.39, 1.15
 |  | <1 | <1 | <=1 | <1 | 1.13, 0.76, 0.45 | 1.13, 0.92, 0.46
 | 5 | 0.89, 1.14 | 0.93, 1.18 | 0.94, 1.16 | 1.01, 1.13 | 1.40, 1.22 | 1.43, 1.43
 |  | <1 | <1 | <=1 | <=1 | 1.19, 1.04, 0.94 | 1.27, 1.35, 1.06
 | 10 | 0.89, 1.21 | 0.94, 1.22 | 0.95, 1.25 | 1.01, 1.31 | 1.40, 1.45 | 1.56, 1.62
 |  | <1 | <1 | <=1 | <=1 | 1.30, 1.34, 1.35 | 1.47, 1.63, 1.53
 | 15 | 0.89, 1.28 | 0.95, 1.27 | 0.95, 1.33 | 1.01, 1.53 | 1.44, 1.76 | 1.68, 1.80
 |  | <=1 | 0.87, 1.04, 1.05 | 0.89, 1.15, 1.13 | 1.00, 1.39, 1.33 | 1.41, 1.71, 1.66 | 1.67, 1.86, 1.81
 | 20 | 0.89, 1.36 | 0.95, 1.37 | 0.95, 1.40 | 1.04, 1.71 | 1.48, 1.88 | 
 |  | 0.87, 1.11, 1.33 | 0.89, 1.23, 1.47 | 0.93, 1.36, 1.56 | 1.03, 1.66, 1.71 | 1.48, 1.87, 1.84 | 
 | 25 | 0.89, 1.41 | 0.96, 1.51 | 0.96, 1.48 | 1.10, 1.82 |  | 
 |  | 0.89, 1.32, 1.59 | 0.93, 1.43, 1.74 | 0.95, 1.47, 1.84 | 1.09, 1.81, 1.96 |  | 
 | 30 | 0.89, 1.48 | 0.99, 1.59 | 0.96, 1.60 |  |  | 
 |  | 0.89, 1.45, 1.80 | 0.97, 1.58, 1.88 | 0.96, 1.60, 1.97 |  |  | 
Large difference of AP-STA paths loss relative to SNR

## Slide 21: Observations
With 3 STA per AP the baseline performance is better than scenario 2 at SNR>=20dB which leads to reduction in gains of both C-SR and C-BF. However C-BF still shows gains at low values of X at those SNR
As in the previous scenario C-BF is better than C-SR in the top left triangle, meaning X<=SNR=10 or 15 ( SNR from AP2 is at least 10 or 15dB)
For C-SR Nss = [1 1 1; 1 1 1] is largely the best for X >= 15dB. Nss = [1; 1] is best for low SNR, low X.