## Slide 1: Low Latency Traffic Report
Date: 2023-07-05
Authors:

## Slide 2: Abstract
This contribution discusses the low latency traffic report procedure.
  An AP and STA can preempt channel access based on the low latency traffic report signaling.

## Slide 3: Low Latency Traffic Report
An AP is a TXOP holder
  If a STA should be able to report the low latency data presence within the TXOP, the AP can schedule the resource to that STA. It can improve the low latency data of the STA.
A STA is a TXOP holder
  If an AP should be able to report the low latency data presence within the TXOP, the AP can use the remaining TXOP. It can improve the low latency data of the STA.
On this purpose, we propose a Low Latency Traffic Report procedure based on the uplink OFDMA random access.

## Slide 4: Low Latency Traffic Report
An AP sends a downlink low latency data to a recipient STA.
  If the recipient STA has an uplink low latency data, it can piggyback the low latency data presence report (LLR) with the BlockAck response.
  If 3rd party STA has an uplink low latency data, it can send the LLR through the uplink OFDMA random access.
LL DATA
(Ack Policy = 00)
BA+LLR
LL
LLR
Trigger
LL DATA
LL DATA
AP
STA1
STA2
SIFS
SIFS
Low latency data arrival
Low latency data arrival

## Slide 5: Low Latency Traffic Report
An AP sends a downlink non-low latency data to a recipient STA.
  If the recipient STA and 3rd party STA have an uplink low latency data, it can send the LLR through the uplink OFDMA random access.
  Otherwise, the AP continues the downlink non-low latency data transmission after the PIFS recovery.
non-LL DATA1
(Ack Policy = 11)
LLR
LL
LLR
non-LL DATA2
(Ack Policy = 11)
Trigger
PIFS
SIFS
AP
STA1
STA2
Low latency data arrival
Low latency data arrival

## Slide 6: Low Latency Traffic Report
A STA sends an uplink low latency data to an AP.
  If the AP has a downlink low latency data address to the originator STA, it can piggyback the LLR with the BlockAck response.
  The AP uses the remaining TXOP and sends a downlink low latency data.
LL DATA
(Ack Policy = 00)
BA+LLR
SIFS
AP
STA1
STA2
LL DATA
(Ack Policy = 00)
BA+LLR
LL
LLR
SIFS
Low latency data arrival
Low latency data arrival

## Slide 7: Low Latency Traffic Report
A STA sends an uplink non-low latency data to an AP.
  If the AP has a downlink low latency data, it sends the LLR.
  Otherwise, the STA continues the uplink non-low latency data transmission after the PIFS recovery.
non-LL DATA1
(Ack Policy = 11)
LLR
non-LL DATA2
(Ack Policy = 11)
PIFS
SIFS
AP
STA1
STA2
LL DATA
(Ack Policy = 00)
Low latency data arrival

## Slide 8: Discussion
An uplink OFDMA random access dedicated for the low latency traffic report should be defined.
  Option 1) LLR Trigger frame with the UORA can be defined.
  Option 2) The UORA RU for the LLR is pre-configured. Then, the PHY header indicates the related information (like Group ID concept of VHT MU-MIMO).
LL DATA
BA+LLR
LLR
AP
STA1
SIFS
Trigger
LL DATA
BA+LLR
LLR
SIFS
Trigger Information of UORA RU for the low latency traffic report
<Option 1>
<Option 2>
STA2
AP
STA1
STA2

## Slide 9: Conclusion
802.11 be mainly focused a scheduling based low latency support mechanisms (e.g., R-TWT, QoS Characteristics element).
In this contribution, we briefly discussed a potential features for supporting low latency application in more general environment (including aperiodic low latency traffic).

## Slide 10: References
https://mentor.ieee.org/802.11/dcn/21/11-21-0628-00-00be-wireless-tsn-in-802-11-and-new-requirements-for-802-11be-and-802-1.pptx
https://mentor.ieee.org/802.11/dcn/20/11-20-1217-04-00be-rts-trigger-su-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/23/11-23-0018-01-0uhr-low-latency-support-in-uhr.pptx
https://mentor.ieee.org/802.11/dcn/22/11-22-1926-00-0uhr-challenges-to-achieve-low-latency.pptx