## Slide 1: AMP PAR Scope Text
Date: 2023-05-10
Authors:
Name | Affiliation | Address | Phone | email
David Halasz | Morse Micro |  |  | dave.halasz@morsemicro.com
Ganesan Thiagarajan | Morse Micro |  |  | ganesan.thiagarajan@morsemicro.com

## Slide 2: Abstract
IEEE 802.11 AMP Study Group is to produce an IEEE Project Authorization Request. This submission contains some proposed text for the PAR Scope.

## Slide 3: The AMP Technical Report of AMP IoT devices in WLAN[1] & IEEE 802.11ba (WUR) Wake-up Radio
[1]In summary, the standardization work in order to support AMP device in WLAN should enable AMP devices to be ultra-low complexity and operate battery free, and may include:
PHY: WUR (100x uW) + Simplified UL PHY (10x uW~100x uW)
In the DL, WUR (802.11ba) like design as a starting point.
  Reuse legacy design as much as possible, such as OOK, channel structure, waveform, PPDU formats, etc.
  Additional signaling in WUR to transmit additional signaling or payload data.
  Some re-design may be necessary if AMP in WLAN is implemented in frequency band other than 2.4GHz, e.g., S1G.
Note: Other schemes than 802.11ba are not precluded if useful.
In the UL, legacy design as a starting point for the UL PHY, e.g., 802.11ba OOK, 802.11b DSSS modulation, etc.
  Both active transmitter and backscatter transmitter can be supported.
    The carrier for backscattering shall be specified considering the regulation requirement
    Optimizations for full-duplex operation in case of backscatter modulation can be considered
Note: other schemes, e.g., FSK/PSK are not precluded if useful.
  The carrier and bandwidth of backscattering signal should be specified including signal of narrow bandwidth or wide bandwidth and carrier signal using the existing signal can also be considered.
MAC: Simplified MAC + Enhanced power saving/ power management (Note 2, Note 3), e.g.,
  Efficient PLCP and MAC for limited payload message sizes, e.g., 100bits.
Coordination of AMP device channel access (e.g., may not be able to use conventional CSMA-like approaches since backscattering devices potentially undetectable by other devices)

## Slide 4: AMP & WUR
[1]During the March 2023 IEEE 802 plenary meeting, a contribution on ambient communication in WLAN (11-23/0406r1) was presented and discussed in AMP session with the following straw poll:
Straw Poll: Do you agree on the following features/requirements for AMP WLAN as the baseline for future discussion?
  Support ultra-low complexity and ultra-low power consumption transmission and reception for device using ambient power sources:
    WUR-similar design could be as the starting point for downlink receiver
    Simplified UL PHY
      Both active transmitter and backscatter transmitter can be supported
  Simplified MAC (on top of existing WLAN technologies) + Enhanced power saving/ power management
  Consider frequency bands of Sub-1 GHz and 2.4GHz
  Optimized security mechanism
  Coexistence with existing 802.11 devices when operating in the same frequency band.
  The PAR/CSD scope could be further harmonized during SG discussion.
Result: 61Y/2N/28A

## Slide 5: WUR & Sub 1 GHz
IEEE Std 802.11ba-2021 defines operation in the 2.4 GHz and 5 GHz bands.
The AMP PAR Scope should include text indicating that defining WUR for the Sub 1 GHz band is within scope.

## Slide 6: Additional text for AMP PAR Scope
This amendment will also define a physical (PHY) layer specification and defines modifications to the medium access control (MAC) layer specification that enables operation of a wake-up radio (WUR) for the Sub 1 GHz band.

## Slide 7: References
IEEE 802.11 23/436r0 Technical Report on support of AMP IoT devices in WLAN
"IEEE Standard for Information Technology--Telecommunications and Information Exchange between Systems--Local and Metropolitan Area Networks-Specific Requirements--Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications - Amendment 3: Wake-Up Radio Operation," in IEEE Std 802.11ba-2021 (Amendment to IEEE Std 802.11-2020 as amendment by IEEE Std 802.11ax-2021, and IEEE Std 802.11ay-2021) , vol., no., pp.1-180, 8 Oct. 2021, doi: 10.1109/IEEESTD.2021.9570110.
IEEE 802.11-2020