## Slide 1: Consideration of Industrial Automation Scenarios
Date: 2023-05-DD
Authors:
Name | Affiliations | Address | Phone | e-mail
Akira Kishida | NTT | 1-1, Hikarinooka Yokosuka-Shi, Kanagawa 239-0847, Japan | +81-46-859-2093 | akira.kishida@ntt.com
Yusuke Asai | NTT |  |  | 
Yasushi Takatori | NTT |  |  | 
Kengo Nagata | NTT |  |  | 
Ryo Nagatsu | NTT |  |  | 

## Slide 2: Introduction
The UHR PAR & CSD [1] are confirmed in the 2023 March Plenary, and UHR SG / TGbn will proceed to realize the Scope of the Project in the PAR.
TGax created Simulation Scenarios [2] and Evaluation Methodologies [3] documents. Creating these documents needs a lot of effort and time. Therefore, TGbe did not create these.
In the UHR, scenarios of each use case should be considered to provide materials to clarify the purpose and effect of the technologies under consideration, such as multi-AP and low latency technologies, etc.
  These efforts are different from creating simulation scenarios or evaluation methodologies.
This contribution initiates discussions regarding scenarios of industrial automation [4] which is the target use case of the UHR.

## Slide 3: UHR PAR [1]
5.2.b Scope of the project: This amendment defines modifications to both the IEEE Std 802.11 physical
layers (PHY) and the IEEE Std 802.11 Medium Access Control (MAC) that enhance Wireless Local Area
Network (WLAN) reliability by enabling, in scenarios of an isolated Basic Service Set (BSS) or of
overlapping BSSs:
􀀀at least one mode of operation capable of increasing throughput, as measured at the MAC data service
Access Point, at different Signal to Interference and Noise Ratio (SINR) levels (Rate-vs-Range), compared
to Extremely High Throughput MAC/PHY operation
􀀀at least one mode of operation capable of improving the tail of the latency distribution and jitter
compared to Extremely High Throughput MAC/PHY operation, with mobility between BSSs and
􀀀at least one mode of operation capable of improving efficient use of the medium compared to Extremely
High Throughput MAC/PHY operation.
5.5 Need for the Project: Use of WLANs based on IEEE 802.11 technology continues to grow and diversify
over many market segments including residential, enterprise, industrial and agriculture. More stringent
requirements are needed to meet the demands of new applications (including metaverse [1], augmented
and virtual reality [2], robotics, industrial automation for industrial IoT, logistics and smart agriculture [3])
and to improve reliability (i.e., stable and consistent connectivity and quality of service).

## Slide 4: Recap: TGax Simulation Scenarios [2]
The Simulation Scenarios document in TGax [2] analyzes and summarizes topologies of distribution of APs and STAs in dense environment scenarios.
Though these considerations are also beneficial for the UHR, the enterprise scenario in the document cannot apply to industrial automation scenarios as is.
Therefore, we should consider a new topology for industrial automation.
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
1 | Residential | A - Apartment building e.g. ~10m x 10m apartments in a multi-floor building ~10s of STAs/AP, P2P pairs | Unmanaged | Indoor | Flat | Home
2 | Enterprise | B - Dense small BSSs with clusters e.g. ~10-20m inter AP distance, ~100s of STAs/AP, P2P pairs | Managed | Indoor | Flat | Enterprise
3 | Indoor Small BSS Hotspot | C - Dense small BSSs, uniform e.g. ~10-20m inter AP distance ~100s of STAs/AP, P2P pairs |  |  |  | Mobile
4 | Outdoor Large BSS Hotspot | D - Large BSSs, uniform e.g. 100-200m inter AP distance ~100s of STAs/AP, P2P pairs | Managed | Outdoor | Flat | Mobile
4a | Outdoor Large BSS Hotspot + Residential | D+A | Managed + Unmanaged |  | Hierarchical | Mobile + Home

## Slide 5: Considerations for Industrial Automation Scenarios
For industrial automation scenarios, the following use cases are considered by several white papers[5]-[11] for future industrial automation.
  AGV (Automated Ground Vehicle) / AMR (Autonomous Mobile Robot)
    Delivering parts, products, and materials. Involving communication between robots and a control system, including guidance control, process data exchange, video/image, and emergency stop.
  Sensors
    Periodical report of information to the control system. Numerous sensors are deployed densely.
  Robot/drone motion control
    Remote operation with haptics communication, programmed robot operation with emergency stop.
  Video transfer
    High-definition video transferring from cameras.
  AR/VR/XR
    Walk-by health monitoring, combining video feed with overlaid contextual information.
  Assembly line
    Combination of AGV/AMR, sensors, robot/drone motion control, and video transfer.

## Slide 6: KPIs and Requirements for AGV/AMR in Whitepapers
 | RTA report[5] | WBA[6] | Avnu Alliance[7][8] | 5G-ACIA[9] | IOWN GF[10]
Latency | 10-50 ms | < 10-20 ms | 1-10 ms (cyclic) 10-100 ms (events) | 10-100 ms (Video-operated remote control) | 10-100 ms
Jitter |  | < 1ms | - | - | -
Reliability | 99 to 99.9% | 99.9999% | 99 to 99.99% | 99.9999% | 99.9999%
Speed | - | < 50 km/h | - | - | -
Number of AGVs/AMRs per area | - | - | 100 | 100 | 100 (300)
Note | Values are from Class A applications (AGV). | Another KPI (Handoff times) depend on latency and speed. | Values are cited by combining two documents [6] and [7]. | Cyclic time is adopted as latency, and availability is adopted as reliability. | Values are cited by combining two “Robot manipulator” domains in [9].

## Slide 7: Gap Analysis
Taking AGV/AMR as an example, UHR needs to consider technologies that meet the following requirements.
  Latency
    Almost whitepapers indicate that AGV/AMR use case requires 10 ms at the lowest. (with cyclic control or motion control, the requirement becomes strict for 1-10 ms)
    Though this value will be achieved using existing Wi-Fi technologies, mixed traffic in which different communication requirements coexist, such as sensor and AGV/AMR, will be supported in future industrial automation scenarios[11]. We should fulfill the requirement in such a mixed traffic environment.
    Moreover, we should consider supporting the mobility of AGV/AMRs, vast traffic from numerous sensors, and interferences.
    Besides, two types of latency-sensitive traffic (periodic/cyclic, sporadic/event) should be considered.
  Reliability
    Requirement of reliability varies according to each whitepaper (99 to 99.9999% will be required).
    Almost whitepapers define reliability as the percentage of packets expected to be received within the latency bound (or not defined precisely).
    Wi-Fi systems are unlicensed; therefore, it isn’t easy to guarantee the requirement of that reliability. However, we should challenge to cover the condition in the UHR. (The UHR indicates Ultra High “Reliability.”)

## Slide 8: Challenges for industrial automation in UHR
For the technology proposed in the UHR to be effective in industrial automation scenarios, it is necessary to consider the following items.
  Candidate features that can fulfill the requirements of industrial automation.
    Channel access enhancement (including enhancement of R-TWT, triggered access, and OFDMA)
    Preemption
    Multi-AP enhancement
    Overhead reduction
    Wireless TSN
    And other novel technologies
  Topologies for industrial automation
    Network topologies simulating factories or plants.
    Adopting multi-APs, AGVs/AMRs, and sensors for the topologies.

## Slide 9: Summary
Though TGax Simulation Scenarios analyzes and summarizes topologies of Wi-Fi dense environment scenarios, they do not correspond to some use cases of the UHR, such as industrial automation.
For the technology proposed in the UHR to be effective in industrial automation scenarios, it is necessary to consider candidate technologies and network topologies.

## Slide 10: SP
Do you agree that continuing consideration of network topologies for industrial automation in the UHR is helpful?
  -Yes
  -No
  -Abstain

## Slide 11: References
[1] Laurent Cariou, et al., “UHR proposed PAR,” IEEE 802.11-23/0480r0
[2] Simone Merlin, et al., “Simulation Scenarios,” IEEE 802.11-14/0980r16
[3] Ron Porat, et al., “Evaluation Methodology,” IEEE 802.11-14/0571r12
[4] Akira Kishida, et al., “Considerations on UHR PAR and KPIs,” IEEE 802.11- 22/1919r5
[5] Kate Meng, et al., “RTA report draft,” IEEE 802.11-18/2009r6
[6] “Wi-Fi 6/6E for Industrial IoT,” WBA (Wireless Broadband Alliance), May 2018.
[7] “Wireless TSN — Definitions, Use Cases & Standards Roadmap White Paper,” Avnu Alliance, Mar 2020.
[8] “Wireless TSN: Market Expectations, Capabilities, & Certification,” Avnu Alliance, Feb 2022.
[9] “5G for Connected Industries and Automation,” 5G-ACIA, Feb 2019.
[10]“IOWN GF-Cyber-Physical System Use Case,” IOWN Global Forum, 2021.
[11]“5G Evolution and 6G,” NTT DOCOMO, Jan 2023.