## Slide 1: Discussion on AMP PAR Scope
Date: 2023-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 2: Abstract
The purpose of this presentation is to kick off the discussion on AMP PAR scope.
Doc.: IEEE 802.11-23/0837r0

## Slide 3
Consensus on the Scope of AMP Study
  In the end of the AMP TIG, the following consensus has been made on the scope of future study for AMP SG [1],
  Support ultra-low complexity and ultra-low power consumption transmission and reception for device using ambient power sources:
    WUR-similar design could be as the starting point for downlink receiver
    Simplified UL PHY
      Both active transmitter and backscatter transmitter can be supported
  Simplified MAC (on top of existing WLAN technologies) + Enhanced power saving/ power management
  Consider frequency bands of Sub-1 GHz and 2.4GHz
  Optimized security mechanism
  Coexistence with existing 802.11 devices when operating in the same frequency band.
  The PAR/CSD scope could be further harmonized during SG discussion.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 4
PHY Design
A new PHY needs to be developed with ultra-low complexity and ultra-low power consumption, e.g., less than 1mW transmission and reception
  For DL, WUR-similar design with OOK waveform can be as the starting point for downlink transmitter/receiver
  For UL, WUR-similar design with OOK waveform can also be used for uplink transmitter/receiver
    Both active transmitter and backscatter transmitter can be supported
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 5
MAC Design
  MAC can be further simplified to minimize the power consumption in order to facilitate the AMP devices to operate relying on only ambient power, e.g.,
    Further reduced MAC header, reduced signaling
    Simplified/optimized MAC procedure
    Refined power management, trying to reduce the awake time for AMP devices
  Proposed Text
  Specify PHY and MAC that supports ultra-low complexity and ultra-low power consumption, i.e., less than 1mW transmission and reception
  The supported function includes identification, inventory and positioning.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 6
Frequency Band
  S1G is preferred due to its better coverage performance for both RF energy harvesting and data transmission/reception
  For S1G, regulation requirements are different in USA, EU, China and other countries/areas, which needs to be considered when developing AMP technology.
  Proposed Text
  Operates in at least S1G frequency band
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 7
Other Issues
  Security mechanism needs to be developed to be compatible with ultra-low power consumption and low complexity.
    It needs to be checked whether the existing security mechanism exceeds the AMP device capability and power consumption constraint.
  In S1G, coexistence with existing 802.11ah devices needs to be considered in some countries, e.g., USA.
  In other countries/areas, e.g., EU/China, clean slate design can be considered since there is no or little 802.11ah deployment
  Proposed Text
  Develop security mechanism optimized for ultra-low power consumption if necessary
  Supports coexistence mechanisms with legacy 802.11 stations but clean slate design can also be considered.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 8
Summary
  Proposed PAR
  Specify PHY and MAC that supports ultra-low complexity and ultra-low power consumption, i.e. less than 1mW transmission and reception
    The supported function includes identification, inventory and positioning.
  Operates in at least S1G frequency band
  Develop security mechanism optimized for ultra-low power consumption if necessary
  Supports coexistence mechanisms with legacy 802.11 stations but clean slate design can also be considered.
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-23/0837r0
May 2023

## Slide 9: Reference
IEEE 802.11-23/0063r4, Proposal for consensus straw poll
Doc.: IEEE 802.11-23/0837r0
May 2023