## Slide 1: Client Frame Tracking Countermeasures (CFTC)
Date: 2023-07
Authors:

## Slide 2: Summary
Background
  Unencrypted predictable frame fields can enable “client frame tracking” = identifying a set of frames for which a single client (non-MLO non-AP STA or combination of a non-AP MLD) is transmitter or intended receiver… can allow tracking presence or location of the person using that client, compromising privacy.
  This ppt: Client frame tracking countermeasures (CFTC) mitigate client frame tracking.
Proposal
  Partition time into epochs ~ 10 min. Duration may be variable.
    Goal: prevent tracking associated clients across epoch boundaries (within each Epoch is acceptable).
    Epoch may be initiated by AP or client.
  CFTC applied after MPDU encryption in TX (before MPDU decryption in RX)
    Core CFTC obfuscates link-independent fields: PN, SN, AID.
    Per-link CFTC obfuscates per-link client identifiers: MAC Address
    Random values are generated from KDK for each epoch w/ minimal input from AP
  At epoch transition:
    Retransmission of old MPDU uses param from old epoch.
    A-MPDU Aggregation, TXOP contains either only old MPDUs or only new MPDUs
    Suggests either a hard transition, or soft transition duplicating parts of TX “stacks” (old + new)

## Slide 3: Terminology
AP:
  AP or the combination of an AP MLD and its Affiliated APs.
Client:
  non-AP STA or the combination of a non-AP MLD and its Affiliated STAs.
Client frame tracking:
  identifying a set of frames for which a single client is the transmitter or intended receiver
  can allow tracking presence or location of person using that client, compromising privacy.
Client frame tracking countermeasures (CFTC)
  Mechanisms mitigating client frame tracking.
Epoch:
  Time for which a set of obfuscation parameters applies.

## Slide 4: Preview
# | Guiding Principles | Rationale | Implications
1 | Partition time into epochs |  | Prevent client frame tracking across epoch boundaries
2 | CFTC applied after encryption at TX (before decryption at RX) | Keep same processing (MLD MAC, A1, A2, A3, PN, TID, SN) | Prevent tracking predictable fields across epoch boundary
3 | Replace trackable values with OTA values un-trackable across epoch boundaries | Prevent tracking predictable fields across epoch boundaries | Per-epoch params controlling replacement/modification
4 | Don’t mix old & new parameters at epoch transition | Consider retransmissions, TXOP A-MPDU aggregation, | Hard transition, or soft transition duplicating part of TX “stacks”
5 | Where possible, generate per-epoch params from KDK w/ minimal AP input | Minimal reliance on AP assigning “good” random values | Avoid conflicts in OTA AID & MAC Address (details in future)
6 | Epochs can be common across associated clients, or client-specific | Synch transition = better privacy | AP can pre-prime clients, even multiple epochs in advance

## Slide 5: 1. Epochs
Partition time into epochs (~ 10 min?).
  Duration can vary
CFTC Goals:
  CFTC prevents client frame tracking across epoch boundaries
    “Re-randomize” MAC address & other fields every epoch
  CFTC does not prevent client frame tracking within an epoch

## Slide 6: 2. CFTC below MPDU encryption
Rationale: Minimal change
Analysis
  Per-client TID, SN, PN are already assigned before CFTC, predictable, & TX in the clear
    Can track using SN & PN.
    Currently difficult to track using TID - as statically mapped to Access Classes
  Client per-link MAC Addresses (A1/A2) are static & in clear
  Per-client AID is static & in clear
    Can track using AID & MAC.
Implication:
  Prevent tracking AID, MAC, SN & PN across epoch boundaries

## Slide 7: 3. Replace trackable values with un-trackable OTA values (1/2)
Goal: Over-the-air values cannot be correlated across Epoch boundaries
  Core (link-independent) fields: otaAID, otaPN, otaSN
    Still evaluating obfuscating TID.
  Per-Link fields: otaMAC (Address)
  Current proposal: UL & DL use identical values
    Expect negligible implementation impact if UL & DL use independent values
Core fields
  otaAID, w/ otaAID changing randomly each Epoch
  otaPN = PN + PN_Offset (mod 248), w/ PN_Offset changing randomly each Epoch
  otaSN = SN + SN_Offset (mod 212), w/ per-TID SN_Offset changing randomly each Epoch
  Analysis on XOR vs Addition in backup slides.
Per-Link fields
  otaMAC, w/ otaMAC changing randomly each Epoch
Random per-Epoch params: SN_Offset, PN_Offset, otaAID, Num Link x otaMAC
  Client and AP generate per-TID SN_Offset, PN_Offset , otaMAC from KDK and epoch start time (TSF).
  otaAID is assigned & distributed by the AP.

## Slide 8: 4. Don’t mix old and new at Epoch transitions (1/2)
Suppose client has just transitioned from old Epoch to current Epoch
  In below scenarios, attacker determines old params & current params (for old & current Epoch) correspond to a single client = client frame tracking = !!! BAD !!!.
    Epoch Parameters = {SN_Offset, PN_Offset, otaAID, Num Link x otaMAC}
MPDU initial transmission (TX) & retransmissions (reTX) use mix of old & current params
  Fact: Initial transmission & retransmissions have identical encrypted payloads
  Detection: Attacker looks for retransmitted MPDUs by looking for MPDUs with identical encrypted payloads to previous transmissions while having differing values of PN, SN or otaMAC
MPDUs aggregated in an A-MPDU use mix of old & current params
  Fact: A-MPDU is always to or from a single client.
  Detection: Attacker looks for an A-MPDU with MPDUs using mix of old and new values for otaMAC
A-MPDU/MPDUs in a TXOP use mix of old & current params
  Fact: TXOP is always from a single client.
  Detection: Attacker looks for an TXOP with A-MPDU and/or MPDUs using mix of old and new values for otaMAC
  Note: additional concerns if Block ack reveals internal SN values

## Slide 9: 4. Don’t mix old and new at Epoch transitions (2/2)
Requirements solving issues on previous slide (Primarily a retransmission problem)
  Retransmitted MPDUs use param (SN/PN Offsets, MAC, AID) from same epoch as original transmission.
  Then A-MPDU Aggregation & TXOP, process old MPDUs separately from new MPDUs
  Block Ack carries obfuscated otaSN (not internal SN)
Options
  Soft Transition: concurrent new & old MPDUs. Challenges
    Additional state/stack for some functions to retransmit old MPDUs
    Client has 2 concurrent otaAID, halves max # clients an AP can support
  Hard Transition: Prohibit concurrent new & old MPDUs. Options:
    Discarding pending retransmission buffer at each epoch start (Simple)
    Stop accepting frames & flush pending retransmission buffer (Complex)
    No duplicated state/stack

## Slide 10: 5. Generate per-epoch params from KDK: minimize AP input
Preference is to avoid relying on AP to generate “good” random values
  Overview only here - details in future contribution
AP & client generate CFTC params from KDK, epoch start TSF & minimal additional AP input
Some privacy params have no additional AP input
  PN_Offset[47:0] generated from KDK, epoch start TSF
  SN_Offset[11:0] generated from KDK, epoch start TSF, direction bit (UL/DL), 4-bit TID
Some privacy params have minimal additional AP input
  otaMAC[47:0] generated from KDK, epoch start TSF, 4-bit Link ID
    Expected number of collisions per epoch is less than 2-20.
      Unlikely to happen for a given AP, but always guaranteed to be happening somewhere due to number of AP!
    Still need a way to avoid collisions when they do occur
Some privacy params completely determined by AP
  AID: For efficiency reasons, AP needs to keep AID within a small set while avoiding collisions. Needs to be coordinated by AP and communicated to client.

## Slide 11: 6. CFTC Epochs (Common across clients) (1/2)
AP coordinates synchronizes all associated clients to transition together
AP selects common epoch start TSF, per-client AID & other params (details in future)
  AP unicasts to clients - AP can pre-prime clients, even multiple Epochs in advance
  AP & clients generates other CFTC params from KDK & epoch start TSF
Advantages
  Synchronizing epochs across all associated clients provides more privacy
    If a single client changes CFTC parameters, then attacker easily tracks that client across epoch boundary
      This is less of an advantage when an attacker makes only infrequent observations of the BSS
  Using TSF means no real-time signaling is needed at time of change (can pre-prime clients).
Disadvantage: Client can’t control how often CFTC parameters change.
  “Individual” control must be balanced against advantage of “not standing out in the crowd”

## Slide 12: 6. CFTC Epochs (Client Specific) (1/2) NEW Slide
A client can initiate an AP transition at a client-specific epoch start time TSF
AP or client can select epoch start TSF
AP selects AID & other params (details in future)
  AP & Client derive other CFTC params from KDK, epoch start time (details in future)
Advantages
  Client can control how often CFTC parameters change
  Using TSF means no real-time signaling is needed at time of change (client is pre-primed)
Disadvantages
  Attacker easily tracks client across client-specific epoch boundary

## Slide 13: Review
# | Guiding Principles | Rationale | Implications
1 | Partition time into epochs |  | Prevent client frame tracking across epoch boundaries
2 | CFTC applied after encryption at TX (before decryption at RX) | Keep same processing (MLD MAC, A1, A2, A3, PN, TID, SN) | Prevent tracking predictable fields across epoch boundary
3 | Replace trackable values with OTA values un-trackable across epoch boundaries | Prevent tracking predictable fields across epoch boundaries | Per-epoch params controlling replacement/modification
4 | Don’t mix old & new parameters at epoch transition | Consider retransmissions, TXOP A-MPDU aggregation, | Hard transition, or soft transition duplicating part of TX “stacks”
5 | Where possible, generate per-epoch params from KDK w/ minimal AP input | Minimal reliance on AP assigning “good” random values | Avoid conflicts in OTA AID & MAC Address (details in future)
6 | Epochs can be common across associated clients, or client-specific | Synch transition = better privacy | AP can pre-prime clients, even multiple epochs in advance

## Slide 14: Backup slides

## Slide 15: Rough calculation of expected number of collisions
Model: AP with  212 clients with  4 links each
Expected number of collisions per epoch ~ (# pairs of otaMAC addresses in BSS) x 1/(# available MAC addresses)
# pairs of otaMAC addresses in BSS ~ (# otaMAC addresses in BSS)2/2
# otaMAC addresses in BSS = #clients x # links per client  212 x 4 = 214
 # pairs of otaMAC addresses in BSS  (214)2/2=227
# available MAC addresses = 248
 Expected number of collisions per epoch  227 x 1/248 = 227-48 = 2-21

## Slide 16: 3. Replace trackable values with un-trackable OTA values (2/2) Why Addition instead of XOR for SN/PN?
Security
  XOR: otaSN[i] = SN[i]  R for a secret value R reveals at least part of SN[i]. Exercise:
    Take an incrementing sequence for SN[i] starting at a random value e.g. 5 {5,6,7 etc.},
    Compute otaSN[i] = SN[i]  R a random value R to each value in SN[i]
    Now look at sequence [i] = otaSN[i]  otaSN[i+1]. [i] has form of zero or more 0 bits followed by one or more1 bits in the LSbs, e.g. [i] 0..01111. If [i] is 1 in j LSbs, then SN[i] is 1 in (j-1) LSbs 1. e.g. [i] 0..01111  SN[i] =?...?111.
  Addition: otaSN[i] = SN[i] + R (mod 212) for a secret value R does not reveal SN.
    otaSN is still an incrementing sequence, but you can’t recover SN
  Same applies for PN
Block Ack
  If using otaSN[i] = SN[i]  R then otaSN[i] is not an incrementing sequence.
    Receiver would need to recover SN[i] prior to performing Block Ack
  If using otaSN[i] = SN[i] + R (mod 212) then otaSN[i] is an incrementing sequence:
    Block Ack can use otaSN[i] without recovering SN[i] (faster).