## Slide 1: Considerations on QoS Enhancement in UHR
Date: 2023-04-12
Authors:

## Slide 2: Abstract
In this contribution, we discuss the benefits of timing information sharing for traffic urgency assessment

## Slide 3: Background
UHR has considered several areas of improvement for next generation Wi-Fi networks [1]:
  Increased reliability of WLAN connectivity
  Lower latencies and deterministic latency support
  Increased manageability and mobility support
  Increased performance in congested environments
  Throughput enhancements
  Power savings enhancements
The approved PAR intends to consider at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation [2]

## Slide 4: Background
Support for new use cases with extremely low latency applications have been proposed previously:
  A number of applications that can potentially have very low latency requirements have been considered and discussed by the group [3]-[5]
  Applications in these categories can have a last hop latency requirements on the scale of a few milliseconds [3], [4]
  Many such use cases have also been analysed in the RTA report
  For some of the applications near lossless performance is also expected
Use cases |  | Intra BSS latency [ms] | Jitter variance [ms] | Packet loss | Data rate [Mbps]
Real-time gaming |  | < 5 | < 2 | < 0.1 % | < 1
Cloud gaming |  | < 10 | < 2 | Near-lossless | < 0.1 (Reverse link) > 5Mbps (Forward link)
Real-time video |  | < 3 ~ 10 | < 1~ 2.5 | Near-lossless | 100 ~ 28,000
Robotics and industrial automation | Equipment control | < 1 ~ 10 | < 0.2~2 | Near-lossless | < 1
 | Human safety | < 1 ~ 10 | < 0.2 ~ 2 | Near-lossless | < 1
 | Haptic technology | < 1 ~ 5 | <0.2~2 | Lossless | <1
 | Drone control | < 100 | <10 | Lossless | <1 >100 with video

## Slide 5: Motivation
Spec provides a number of frameworks for scheduling STA side uplink transmission.
However, AP may have many STAs associated with it. AP does not know which STA needs to be prioritized for such triggering
One of the key pieces of information missing at the AP-side today is the timing information from the STA side. E.g., enqueue timestamp
Knowledge of STA-side timing information can enable an AP to take timely action for an STA and ensure that its latency requirement are met.
…
AP
AP
STA1
STA2
STA20
AP -> STA1
AP -> STA2
AP -> STA50
…
STA 20 has dropped the packet as delay bound exceeded!
STA20
STA2
STA1

## Slide 6: Prior Work
There has been discussion on this topic in TGbe [5]-[7]. Unfortunately the group could not reach consensus on this issue.
A few works have also raised this issue in UHR in the context of specific features. E.g. R-TWT [8]
In this presentation we provide discussion on some factors that need to be considered when designing the framework and signaling for such timing information sharing

## Slide 7: Timing Information Sharing Approaches
Two approaches to share timing information
  Historical data based assessment
  Real time assessment
Historical data based assessment
Real time assessment
AP
Timing information provided for one or more frames
Based on past data, AP can predict that STA is likely to face problems in the near future and prioritizes it
Timing information provided for one or more frames
AP action was effective and no further action necessary or AP can further attempt to improve
AP
Timing information provided to AP
Based on delay bound knowledge AP can compute when packet will be dropped.
AP takes action to prevent packet drop at STA side. E.g., STA is triggered prior to the point where packet can be dropped.
STA transmit packet before expiration
Delay bound
AP triggers STA for uplink transmission

## Slide 8: Signalling Approaches
Two approaches:
  Timing information can be shared in a cross link manner
  Timing information can be shared on the same link for which information is relevant
AP1
AP2
AP3
STA1
STA2
STA3
Timing info for link 3 provided on link 1.
Timing info is tagged with link ID
link1
link2
link3
AP1
AP2
AP3
STA1
STA2
STA3
Timing info for link 3 is provided on link 3 itself
No need to tag the info with link ID
link1
link2
link3

## Slide 9: High Level Procedure
STA shares timing information to the AP (same link or cross link)
Based on timing information and delay bound information, AP computes how urgently STA needs to send its packet
AP can prioritize STAs that has higher urgency first in any scheduling decision that it makes

## Slide 10: Summary
UHR intends to improve latency and reliability.
Timing information can be crucial for helping the AP to reduce the latency and packet loss for uplink traffic.
This presentation provides discussion on some factors that can be considered for timing information sharing in UHR

## Slide 11: References
[1] Beyond be – Proposed Next Step, IEEE 802.11-22/0708r3
[2] UHR proposed PAR, IEEE 802.11-23/480
[3] Considerations on UHR PAR and KPIs, IEEE 802.11-22/1919
[4] Cloud VR Use Case and Requirements, IEEE 802.11-22/0952
[5] 802.11bx: Enabling Metaverse -- Metaverse, AR/VR, and Wearables, IEEE 802.11- 22/0779
[4] RTA report draft, IEEE 802.11-18/2009
[5] CR for Low-Latency BSR, IEEE 802.11-21/1577
[6] Resolution for CID 10674, IEEE 802.11-22/1454
[7] LB266 CR for CIDs 10710, 12711, IEEE 802.11-22/1278
[8] Urgency-based Delivery of Latency Sensitive Traffic, IEEE 802.11-23/0045