## Slide 1: AIML Use Cases and Features for WLAN
Date: 2023-06-26
Authors:

## Slide 2
Authors (continued):

## Slide 3: Abstract
The AIML TIG has been working on AIML use cases for IEEE 802.11 systems and devices. This contribution provides an overview of use cases and (by extension) some identified features that the AIML TIG has worked on.
Some TIG members expressed desire to integrate AIML use cases and features in UHR SG.
Straw polls will be run to gauge UHR SG members’ interests towards working on AIML related features in UHR and 802.11bn.

## Slide 4
Overview
AIML TIG and its mandate
AIML TIG goals and activities
Highlights of AIML use cases identified for IEEE 802.11 WLANs
Summary
Straw polls
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 4

## Slide 5
AIML TIG and its mandate
The AIML TIG is formed by the following WG motion in the July 2022 session [1]:
  Motion 5: TIG Re: AI/ML use in 802.11
  Approve formation of a Topic Interest Group (TIG) to:
  (a) describe use cases for Artificial Intelligence/Machine Learning (AI/ML) applicability in 802.11 systems and
  (b) investigate the technical feasibility of features enabling support of AI/ML.
  The TIG is to complete a report on this topic at or before the March 2023 session.
  Moved: Stephen McCann, Second: Marc Emmelmann
  Result: Yes: 119, No: 22, Abstain: 27 (Motion passes)
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 5

## Slide 6
AIML TIG Goals and Activities
The goals for the AIML TIG are NOT to develop AIML models for the 802.11 specifications
The goals and work for the AIML TIG closely follow our mandate
Study and describe AIML use cases that are applicable to 802.11 networks
  Some of the use cases are closely related to what are being considered for UHR/802.11bn
With a strong focus on standards impact on IEEE 802.11 specs
For each use case, the following aspects are being defined:
  Standards impact
  KPIs
  Requirements
  Technical feasibility
We want to present the use cases to the UHR SG to see whether UHR members are interested in working on these use cases and features
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 6

## Slide 7
Highlights of AIML Use Cases Identified for WLANs (1)
We highlight in this report AIML use cases that have already been motioned into the AIML TIG Technical Report [2]
  AIML-based CSI feedback compression/enhancement [3]
  Deep-learning based distributed channel access [4]
  Efficient AIML model sharing [5]
  AIML-based roaming enhancement [6]
Additional use cases have been studied and may be included in the technical report
  AIML-based multi-AP coordination [7]
  AIML-based dynamic spectrum sharing [8]
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 7

## Slide 8
Highlights of AIML Use Cases Identified for WLANs (2)
AIML-based CSI Feedback Compression/enhancement [3]
Sounding procedures in WLANs represent large overhead particularly with potential new features:
  Higher number of spatial streams, e.g., 16
  Multi-AP features such as joint transmissions
Studies show that AIML algorithms may efficiently reduce CSI feedback/improve system throughput
  using unsupervised learning algorithms to significantly reduce CSI feedback into clusters while maintaining similar PER performance
  E.g., AIML-aided dual CSI compression combines codebook and Givens Rotation which leverage K-means ML algorithm
  E.g., AIML algorithm may be used to reduce the computation complexity for CSI feedback
Standards impact:
  Additional signaling (or new signaling design) between AP an STAs required by AIML process to provide (e.g., newly designed) feedback and cluster information
KPIs:
  CSI airtime reduction/additional AIML process overhead
  PER
  Computation complexity/latency
  Storage needed for AIML models
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 8

## Slide 9
Highlights of AIML Use Cases Identified for WLANs (3)
Deep-learning based distributed channel access [4]
Performances of traditional WLAN channel access designs such as DCF degrade in dense deployment, unable to support stringent QoS requirements such as
  Ever increasing throughput
  Low latency
Study has shown that deep learning algorithms can efficiently increase throughput and reduce latency and jitter while maintain fairness to other devices
  E.g., using Deep reinforcement learning for contention window optimization
  E.g., AIML algorithm selects whether to transmit after the channel has been idle for DIFS
Standards impact:
  Signaling and protocols related to parameter exchange between AP and non-AP STAs, e.g., capability indication, data report to facilitate training, neural networks parameters distribution, etc.
KPIs:
  Throughput improvement
  Latency and jitter reduction
  Additional complexity
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 9

## Slide 10
Highlights of AIML Use Cases Identified for WLANs (4)
Efficient AIML model sharing/distribution [5]
Efficient AIML model distribution is essential for many AIML-based operations in WLANs and for performance of WLANs
  In centralized learning/federated learning, large amount of traffic are used to distribute AIML models/training data among participating devices (STAs and APs), in UL, DL and P2P links
  Efficient AIML model distribution protocols are needed to enable support AIML operations
    Including sharing of all AIML models (e.g., for other applications; these model sharing is expected to be carried by WLANs anyway), not just for models used to improve WLAN performance (such as NN models)
Efficient AIML model distribution can leverage the broadcast nature of WLANs
  802.11bc defines UL/DL broadcast services for both associated and unassociated STAs/APs, providing a good set of baseline tools for AIML model distribution
Standards impact:
  Architecture that enables AL/ML model sharing on the MAC layer
  Signaling and protocols related to AIML model sharing support/capability indication and management
KPI: medium occupation time saving compared to model sharing using application layer data
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 10

## Slide 11
Highlights of AIML Use Cases Identified for WLANs (5)
AIML Enhanced Roaming [6]
Roaming may occur frequency in densely AP deployments, affecting device battery lifetime and user experience
  Multi-AP networks commonly see a high level of roaming events
  A large number of roaming candidate APs/channels in use can cause STA scanning process to take a long time
  Candidate APs in 802.11k neighbor report are useful, however, not all RF neighbor APs are equally relevant for roaming
Efficient AIML techniques may be applied to
  Augment 802.11k neighbor report with weight for each candidate AP for prioritization of scanning
  Assist the STA to find the optimal mid-point between APs to start scanning and roam
Standards impact:
  Enhanced 802.11k neighbor report with weight of roaming neighbor AP candidates
  Triggering STAs to scan at mid-point between APs may require enhancement of BTM request frame
  Feedback for roaming recommendation by using enhanced BTM response frame
KPI:
  Scanning/Roaming time
  Roaming failure rate
  MCS distribution/Retry rate during a BSS transition
  RSSI at reattach time
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 11

## Slide 12
Highlights of AIML Use Cases Identified for WLANs (6)
AIML based Multi-AP Transmission [7]
In OBSS scenarios, multi-AP coordinated transmissions can improve network performance
  Multi-AP coordinated transmission is expected to be a feature of UHR SG/802.11bn
  Configuring such transmissions is challenging due to varying network and radio conditions and outside interference (neighboring, non-coordinating BSS)
AIML models can learn and make decisions/predict
  Find AP-STA pairs, select transmission strategy and associated parameters, select when to transmit, etc.
  Exact multi-AP schemes depend on work in UHR/802.11bn but may include C-TDMA, C-OFDMA, C-SR, C-BF and JT
Standards impact:
  Additional signaling for exchanging training data/measurement reports/model sharing
KPI:
  Network performance metrics (throughput, latency and jitter, power efficiency) – measured at the BSS level but also aggregated over the whole multi-AP network
  Fairness – to ensure that all users are fairly served
  AIML overhead – additional signaling, computational complexity, and learning latency
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 12

## Slide 13
Highlights of AIML Use Cases Identified for WLANs (7)
AIML based Dynamic Spectrum Sharing [8]
802.11 systems operating in dense and high traffic environments, including other 802.11 systems as well as networks that operate using other standards
AIML-based solution: spectrum sensing and signal classification infer the presence of other wireless systems sharing the same spectrum, reacting by manipulating 802.11 parameters and techniques according to a given policy under a collaborative or uncollaborative scheme for interference mitigation and avoidance.
  802.11 parameters and techniques: key enhancements such as multi-link operation, multi-AP operation, and multiple network allocation vectors, under dense environments require dynamic automation of operations.
Standard Impact:
  AIML requires the specification of the required signaling, data format and protocols of inputs and outputs for AIML models.
KPI:
  Continuous throughput, latency and jitter measured at the MAC-SAP in high density scenarios. Network energy efficiency.
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 13

## Slide 14
Summary
The AIML TIG’s activities closely follow our mandate
Study and describe AIML use cases that are applicable to 802.11 networks
With a strong focus on standards impact on IEEE 802.11 specs
  i.e., changes needed to enable/utilize/facilitate AIML operations in current 802.11 specs
AIML TIG is not developing/specifying AIML models
The AIML TIG has worked on 6 AIML use cases for WLAN [2][7][8]
These use cases are very closely related to those considered for UHR/802.11bn
  AIML-based CSI feedback compression/enhancement [3]
  Deep-learning based distributed channel access [4]
  Efficient AIML model sharing [5]
  AIML-based roaming enhancement [6]
  AIML-based multi-AP coordination [7]
  AIML-based dynamic spectrum sharing [8]
We presented these cases to gauge the interests of UHR SG members to study/work on these AIML based use cases and features in UHR and 802.11bn
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 14

## Slide 15: References
[1] 11-22/597r3: May 2022 Working Group Motions, May 18, 2022
[2] 11-22/987r7: AIML TIG Technical Report Draft
[3] 11-22/1934r5: Proposed AIML TIG Technical Report Text for the CSI Feedback Compression Use Case
[4]11-22/2119r1: Proposed AIML TIG Technical Report Text for the Distributed Channel Access Use Case
[5] 11-23/0050r2: Proposed AIML TIG Technical Report Text for the AIML Model Sharing Use Case
[6] 11-23/475r4: Proposed IEEE 802.11 AIML TIG Technical Report Text for the AIML-based Roaming Enhancements Use Case
[7] 11-23/227r4: Proposed IEEE 802.11 AIML TIG Technical Report Text for the Multi-AP Coordination Use Case
[8] 11-23/1072r0: AIML methodology for dynamic spectrum sharing and coexistence

## Slide 16
SP 1
Would you be interested to study/work on AIML related features in UHR SG/802.11bn?
Yes:
No:
Abstain:
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 16

## Slide 17
SP 2
Would you be interested to study/work on the following AIML related feature for UHR SG/802.11bn? Please choose one or more of AIML-based use cases/features:
AIML CSI Feedback compression/enhancement
AIML based distributed channel access
AIML model sharing
AIML-based roaming enhancement
AIML-based multi-AP coordination
AIML-based interference management
July 2023
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 17