## Slide 1: UHR Secondary Channel Access
Date: 2023-7-7
Authors:

## Slide 2: Problem
For any 802.11 transmission (20/40/80/160/320MHz),
  The primary 20 MHz channel must be idle to access a wideband channel (>20 MHz)
  A STA cannot transmit on any idle secondary channels if the primary channel is busy
This is not the best way to utilize < 7 GHz bands, especially for 160/320 MHz
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Available
Secondary channels available
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
Now STA can transmit a packet

## Slide 3: Goal
If the primary channel is busy and the secondary channel(s) are available, an AP/STA transmits on the available secondary channel(s)
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
STA can transmit a packet on the secondary channels while the primary channel is busy
60MHz PPDU
40MHz PPDU

## Slide 4: Design considerations
Need to be simple
Before using the secondary channels, an AP/STA needs to know idle/busy status of the secondary channels
No major additional receive capability on the secondary channels

## Slide 5: Proposal
AP behavior (transmitter)
  Monitors medium idle/busy on the second primary channel (P2)
    ED/PD CCA: e.g.,STF detection
  If the first primary channel (P1) is busy for NAV time duration and the second primary channel is idle for X (TBD) time duration
    On the second primary channel, AP does backoff and initiates TXOP with BSRP Trigger or RTS frame (a control frame) to target STA(s)
      RTS/CTS or BSRP/BSR type of control frame exchange is needed to know if the target STAs are on the second primary channel
      The TXOP ends before the NAV=0 set at the first primary channel
STA behavior (receiver)
  If the first primary channel is busy for NAV time duration
    Move to the second primary channel and wait for BSRP or RTS (a control frame) from the AP
    STA goes back to the first primary channel before NAV=0 of the first primary channel
Busy
P1 20MHz
S1.1 20MHz
OBSS frame exchanges (busy)
(both AP and STA received OBSS packet and set NAV)
Busy
Busy
frequency
P2 20MHz
S2.1 20MHz
40MHz PPDU (TX)
BSRP
BSR
BA
S2.2 20MHz
S2.3 20MHz
S1.2 20MHz
S1.3 20MHz
AP/STA decode OBSS packet or PHY preamble and sets NAV
ED/PD CCA Access secondary channels if medium Idle for > X time duration (a value >PIFS and < maxPPDU)
Frame exchanges end before NAV =0 on P1 (to keep the medium sync on P1)
80MHz PPDU (TX)
BSRP
BSR
BA
OBSS frame exchanges
(busy)
40MHz PPDU (TX)
BSRP
BSR
BA
NAV=0
PIFS
PIFS
1st primary
2nd primary
BO
(idle)

## Slide 6: When AP and STA have different views on channel idle/busy
From AP side P1 is busy (NAV set) but from STA side P1 is idle
  AP may send BSRP or RTS on P2 and available secondary channels
    STA is not monitoring P2 and does not respond to BSRP/RTS
  STA may send RTS on P1
    AP is monitoring P2 and does not respond to RTS on P1
From AP side P1 is idle but from STA side P1 is busy (NAV set)
  AP may send BSRP or RTS on P1 and available secondary channels (not including P2)
    STA is waiting on P2 and does not respond to BSRP/RTS on P1
  AP may send BSRP or RTS on P1 and available secondary channels (including P2)
    STA is waiting on P2 and may respond to BSRP/RTS on P2
  STA may send RTS on P2
    AP is monitoring P1 and does not respond to RTS on P2
For simplicity, frames on P2 while P1 is idle is ignored to avoid decoding OBSS frames on secondary channels (while decoding OBSS frames on secondary channels create blindness on the primary)
  Decode frames on P2 only when P1 is busy

## Slide 7: Summary
The current secondary channel access mechanism is inefficient for a wideband channel (e.g., 160 or 320 MHz)
UHR needs a better secondary channel access scheme to fully utilize a wideband channel