## Slide 1: Further Discussion on Requirements for AMP Use Cases
Date: 2023-06-27
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/1603r0
June 2023

## Slide 2: Abstract
The purpose of this presentation is to further discuss the key requirements.
Doc.: IEEE 802.11-23/1603r0

## Slide 3
Initial Table for the Requirements
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/1603r0
June 2023
 | Coverage (dBm) | Maximum payload size (bit) | Peak device power consumption (mWatts) | Device density (per m2) | Horizontal Positioning accuracy (m) | Peak data rate (Kbps) | Others
UC1: Smart Manufacturing | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC2: Data Centre | Type1: -30 Type2: -82 | 256 | 1 | 3 | 1-3 | 51.2 kbps | 
UC3: Smart Home | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC4: Logistics and Warehouse | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
UC5: Smart Agriculture | Type1: -30 Type2: -82 | 256 | 1 | 1 | 10 | 51.2 kbps | 
UC6: Indoor Positioning | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC7: Smart Power Grid | Type1: -30 Type2: -82 | 256 | 1 | 10-2 | 10 | 51.2 kbps | 
UC8: Fresh Food Supply Chain | Type1: -30 Type2: -82 | 256 | 1 | 1.5 | 3 | 51.2 kbps | 
Note 1: Coverage is calculated based on AWGN Channel Note 2: Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc. Note 3: Others include requirements only applicable to a subset of use cases |  |  |  |  |  |  | 

## Slide 4
Device Density (1/2)
  UC1 Smart Manufacturing:
    1.5/m2
    A typical car manufacturing plant takes up to 600 000 m2 in surface. Around 1 million units of materials are used in the manufacturing area, but they are not used at the same time.
  UC2 Data Centre
    3/m2
    Assuming the same density as UC1 but with 2-tier shelf
  UC3 Smart Home:
    0.25/m2
    Based on the deployment assumption of 1 AMP device every 2 meter.
  UC4 Logistics and Warehouse
    1.5/m2
    Assuming the same density as UC1
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/1603r0
June 2023
Notes: [

## Slide 5
Device Density (2/2)
  UC5 Smart Agriculture
    1/m2
    Assuming 1 device per meter for collecting sensing data
  UC6 Indoor Positioning:
    0.25/m2
    Based on the deployment assumption of 1 AMP device every 2 meter.
  UC7 Smart Power Grid:
    10-2/m2
    The device density is calculated based on an individual substation, where typically several hundreds of Ambient IoT devices are required to monitor the environmental parameters.
  UC8 Fresh Food Supply
    1.5/m2
    Same as UC1.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/1603r0
June 2023

## Slide 6
Device Density: Warehouse
  AMP is expected to target only at high-value items, e.g., pallets, but not for every items, e.g., small boxes/cartons.
  Taking most common items, i.e., pallets as an example
    Typical pallet size is around 1m-by-1.2m
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/1603r0
June 2023
  Standard Pallet Size [1]
Notes: [1] https://www.bestforworld.com/the-complete-guide-of-standard-pallet-definition-size-and-dimensions-classification-loading-load-selection-attention-usage-method2022
Typical pallet size is 1-by-1.2, 1 per m2 for single layer, 5 per m2 for multiple layers
[2] https://crownlspgroup.com/how-to-calculate-warehouse-space-needs/
50%-80% space efficiency
[3] https://pplusglobal.com/2018/03/23/use-standard-pallet-sizes-stacking-height/#:~:text=Safe%20Stacking&text=When%20you%20stack%20them%2C%20don,layers%20to%20hold%20them%20tight.
<=60inches, 5 feet, 1.52m,
[4] https://www.miebach.com/en/publications/whitepapers/pallet-heights-in-logistics/
Up to 6 layers

## Slide 7
Device Density: Warehouse
  Pallets can be stacked in single layer or multiple layer on the shelf
  According to [2], shelf layers can normally be up to 6 levels and 2.5m due to safety reasons.
  Assuming one AMP tag is attached to each pallet, the AMP tag density is around 0.83/m2 for single layer and 5/m2 for multiple layers.
  It should be noted that the space within one warehouse cannot be fully used for the reasons including unusual shapes of the products, space for maneuver around shelfs, etc.
    Typical space usage is 40%-80% [3]
  Average density is around 0.56/m2 for single layer and 4/m2 for multiple layers.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/1603r0
June 2023
Notes: [1] https://www.bestforworld.com/the-complete-guide-of-standard-pallet-definition-size-and-dimensions-classification-loading-load-selection-attention-usage-method2022
Typical pallet size is 1-by-1.2, 1 per m2 for single layer, 5 per m2 for multiple layers
[2] https://crownlspgroup.com/how-to-calculate-warehouse-space-needs/
50%-80% space efficiency
[3] https://pplusglobal.com/2018/03/23/use-standard-pallet-sizes-stacking-height/#:~:text=Safe%20Stacking&text=When%20you%20stack%20them%2C%20don,layers%20to%20hold%20them%20tight.
<=60inches, 5 feet, 1.52m,
[4] https://www.miebach.com/en/publications/whitepapers/pallet-heights-in-logistics/
Up to 6 layers

## Slide 8
Requirements
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-23/1603r0
June 2023
 | Coverage (dBm) | Maximum payload size (bit) | Peak device power consumption (mWatts) | Device density (per m2) | Horizontal Positioning accuracy (m) | Peak data rate (Kbps) | Others
UC1: Smart Manufacturing | Type1: -30 Type2: -82 | 256 | 1 | 4 | 3 | 51.2 kbps | 
UC2: Data Centre | Type1: -30 Type2: -82 | 256 | 1 | 3 | 1-3 | 51.2 kbps | 
UC3: Smart Home | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC4: Logistics and Warehouse | Type1: -30 Type2: -82 | 256 | 1 | 4 | 3 | 51.2 kbps | 
UC5: Smart Agriculture | Type1: -30 Type2: -82 | 256 | 1 | 1 | 10 | 51.2 kbps | 
UC6: Indoor Positioning | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC7: Smart Power Grid | Type1: -30 Type2: -82 | 256 | 1 | 10-2 | 10 | 51.2 kbps | 
UC8: Fresh Food Supply Chain | Type1: -30 Type2: -82 | 256 | 1 | 4 | 3 | 51.2 kbps | 
Note 1: Coverage is calculated based on AWGN Channel Note 2: Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc. Note 3: Others include requirements only applicable to a subset of use cases |  |  |  |  |  |  | 

## Slide 9: Summary
For warehouse, the products/items size and stacking should follow regulations.
Device density in logistics and warehouse is updated based on such regulations.
Doc.: IEEE 802.11-23/1603r0

## Slide 10: Reference
https://www.bestforworld.com/the-complete-guide-of-standard-pallet-definition-size-and-dimensions-classification-loading-load-selection-attention-usage-method2022
https://www.miebach.com/en/publications/whitepapers/pallet-heights-in-logistics/
https://pplusglobal.com/2018/03/23/use-standard-pallet-sizes-stacking-height/#:~:text=Safe%20Stacking&text=When%20you%20stack%20them%2C%20don,layers%20to%20hold%20them%20tight.
Doc.: IEEE 802.11-23/1603r0
June 2023