## Slide 1: Discussion on Frequency Band, Channel Bandwidth and Data Rate
Date: 2023-06-27
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/1064r0
June 2023

## Slide 2: Abstract
The purpose of this presentation is to define the operation frequency band, channel bandwidth and data rate for AMP.
Doc.: IEEE 802.11-23/1064r0

## Slide 3
Operation Frequency Band (1/5)
  Option 1: Single band
    Option 1a: both RF energy harvesting and communication at S1G
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/1064r0
June 2023
Option 1a | 
Pros | Cons
sufficient transmission power for RF energy harvesting | different channelization design might be needed due to regulation requirements
good coverage for communication | 
less impacts on co-existence, potential clean-slate design in some areas/countries, e.g., EU and China | 
low complexity with potential symmetric design for UL and DL | 
narrow band operation with less complexity and power consumption | 
Notes: [

## Slide 4
Operation Frequency Band (2/5)
  Option 1: Single band
    Option 1b: both RF energy harvesting and communication at 2.4GHz
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/1064r0
June 2023
Option 1b | 
Pros | Cons
less implementation efforts since existing APs can operate on 2.4GHz | stringent transmission power limit for RF energy harvesting
potential backward compatibility if legacy design, e.g. DSSS is adopted | reduced communication coverage
potential uniform design across different areas/countries | higher complexity with potential asymmetric design for UL and DL
 | high power consumption due to wideband operation
Notes: [

## Slide 5
Operation Frequency Band (3/5)
  Option 1: Cross band
    Option 2a: RF energy harvesting at S1G and communication at 2.4GHz
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/1064r0
June 2023
Option 2a | 
Pros | Cons
sufficient transmission power for RF energy harvesting | higher complexity and cost since AMP devices need to support both S1G and 2.4GHz
less implementation efforts since existing APs can operate on 2.4GHz | reduced communication coverage
potential uniform design across different areas/countries | higher complexity for AP if AP needs to support RF energy harvesting
potential backward compatibility if legacy design, e.g. DSSS is adopted | 
Notes: [

## Slide 6
Operation Frequency Band (4/5)
  Option 2: Cross band
    Option 2b: RF energy harvesting and DL communication at S1G, UL communication at 2.4GHz
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/1064r0
June 2023
Option 2b | 
Pros | Cons
less implementation efforts in UL since existing APs can operate on 2.4GHz in UL | For DL different channelization design might be needed due to regulation requirements
potential backward compatibility in UL if legacy design, e.g. DSSS is adopted | higher complexity and cost since AMP devices need to support both S1G and 2.4GHz
potential uniform design across in UL different areas/countries | AP also needs to support S1G and 2.4GHz at the same time
sufficient transmission power for RF energy harvesting | reduced UL communication coverage
 | lack of accuracy using incoming S1G to calibrate outgoing 2.4GHz
Notes: [

## Slide 7
Operation Frequency Band (5/5)
  Proposal 1: Option 1a is adopted as baseline design and other options as optional design
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/1064r0
June 2023
Notes: [

## Slide 8
Channel Bandwidth
  S1G
    USA: 1MHz coexistence with 802.11ah devices
    EU: 200kHz, 250kHz, 400kHz, 800kHz, 1MHz
    China: 250kHz
    Chanel bandwidth: 200kHz (EU), 250kHz (China), 1MHz (USA)
    Proposal 2: For S1G, flexible channel bandwidth should be supported, at least 200kHz, 250kHz and 1MHz channel bandwidth should be supported
  2.4GHz
    DL: 4MHz for AMP with 20MHz legacy preamble
    UL:
      Alt1: 4MHz for AMP with 20MHz legacy preamble
      Alt2: 22MHz with DSSS
  Proposal 3: If 2.4GHz is adopted as operation frequency band, 4MHz is baseline channel bandwidth and 22MHz can be optional.
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-23/1064r0
June 2023
Notes: [

## Slide 9
Data Rate
  Up to 51.2 kbps is needed based on the analysis in [1]
  S1G
    Chanel bandwidth: 200kHz, 250kHz, 1MHz
    Data rate: considering 31.25kHz SCS with symbol duration 40us, multiple bits can be mapped to one OOK symbol
      50kbps
      100kbps
    Proposal 5: For S1G, 50 and 100 kbps data rate should be supported.
  2.4GHz
    DL: channel bandwidth 4MHz, data rate 62.5kbps and 250kbps
    UL:
      Alt1: 4MHz channel bandwidth, data rate 62.5kbps and 250kbps
      Alt2: 1Mbps with DSSS
    Proposal 6: If 2.4GHz is adopted, 62.5kbps data rate for 4MHz channel bandwidth can be supported as baseline and 250kbps and 1Mbps as optional.
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-23/1064r0
June 2023
Notes: [

## Slide 10: Summary
Various options for operation frequency bands are explored with each option’s pros and cons and channel bandwidth and data rate are proposed.
Proposals are as follows
  Proposal 1: Option 1a is adopted as baseline design and other options as optional design
  Proposal 2: For S1G, flexible channel bandwidth should be supported, at least 200kHz, 250kHz and 1MHz channel bandwidth should be supported
  Proposal 3: If 2.4GHz is adopted as operation frequency band, 4MHz is baseline channel bandwidth and 22MHz can be optional.
  Proposal 5: For S1G, 50 and 100 kbps data rate should be supported.
  Proposal 6: If 2.4GHz is adopted, 62.5kbps data rate for 4MHz channel bandwidth can be supported as baseline and 250kbps and 1Mbps as optional.
Doc.: IEEE 802.11-23/1064r0

## Slide 11: Reference
IEEE 802.11-23/1005r0, Discussion on Requirements for AMP Use Cases
Doc.: IEEE 802.11-23/1064r0
June 2023