## Slide 1: TB Ranging with EHT and HE TB PPDU
Date: 2023-06-20
Authors:

## Slide 2: Use 320 MHz BW in TB Ranging
Requires the creation of the EHT TB Ranging NDP
Open questions
Can we mix EHT and HE TB frames (poll/sound/report)?
Review of Facts
11be does not allow mixing non-EHT (HE) and EHT TB operation (in the same TF/RU allocation)

## Slide 3: Decision Tree
Do we allow use of EHT TB Ranging NDP for 320 MHz only?
  Yes: Limit number of combinations to reduce testing/implementation
  No – go to slide (7)
This means polling and sounding will solicit either
  EHT TB PPDUs when using 320 MHz BW, or
  HE TB PPDUs when using < 320 MHz BW

## Slide 4: Overview of TB Ranging
EHT frames

## Slide 5: Decision Tree
Do we keep allowing to reduce bandwidth for LMR?
  Yes, to keep in line with 11az
  No, done – all frames are either EHT or HE (no mixing)
This means
  R2I LMR can be transmitted as either EHT MU PPDU or HE SU/MU PPDU
  IR2 LMR can be transmitted as either EHT TB PPDU or HE TB PPDU

## Slide 6: Decision Tree
Do we want all frames in same sequence to be either HE or EHT
  Yes, to keep it simpler
  No, allow all combinations or keep EHT for 320 MHz only?
This means
  Keep all frames in the same format in one sequence?
  IR2 LMR can be transmitted as either EHT TB PPDU or HE TB PPDU

## Slide 7: Decision Tree
Follow up to (1.)
If we allow frames < 320 MHz in EHT format
Keep sequences all EHT or all HE