## Slide 1: Vendor Specific SIG field
June 2023
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Ever since 802.11a, silicon vendors have added proprietary PHY-layer features to PPDUs despite the lack of conformant paths …
Hart et al (Cisco Systems)
Goals:
      Signal the presence of proprietary PHY-layer features in PPDUs
      Have the signaling be understood by devices in their eco-system
      Avoid confusing devices outside their eco-system
      And conform to the 802.11 standard
Practical reality
      Use reserved bit(s) in a SIG/Service field
      Use upper-layer vendor-specific capability signaling, and only enable the feature when nearby to other devices in the same eco-system
      Doesn’t conform to the 802.11 standard; the use of reserved bits might clash/conflict with the use of reserved bits by devices outside their eco-system
Stakes are raised with U-SIG
      This needs to support many generations of 802.11 MAC/PHY amendments and many vendors

## Slide 3: … and Vendor Specific Extensions nourish safe experimentation and prototyping
Hart et al (Cisco Systems)
The MAC has rich and mature mechanisms for safe feature experimentation, prototyping and deployment
      Vendor Specific elements
      Vendor Specific subelements
      Vendor Specific Action frames
      Vendor Specific Public Action frames
Some of these proprietary features didn’t work out, and did not burden the 802.11 standard
Some of these proprietary features created high value and were returned to 802.11 and have been proposed/accepted as standardized features
      i.e., vendor specific extensions support a rich and healthy 802.11 eco-system
However, the PHY lacks these facilities

## Slide 4: Proposal: define and signal the presence of a Vendor Specific SIG field to preserve the remaining reserved U-SIG bits for future PHY amendments …
Hart et al (Cisco Systems)
U-SIG field:
    a field to indicate the absence/presence of the VS SIG field
      and include new version (Validate) when present
VS-SIG field: traditional SIG design with BCC, 1SS and 20 MHz-duplication:
      Option A: MCS0, 1 OFDM symbol, or
      Option B: A small selection of low MCSs and numbers of OFDM symbols
LSTF
LLTF
LSIG
RLSIG
USIG
VS SIG
UHR SIG
UHR STF
UHR LTF
Data
PE
Two parts of U-SIG | Bit | Field | Number of bits | Description
U-SIG-1 | B20 / B20-B21 | VS SIG Info | 1 / 2 | 0: No VS SIG field 1: VS SIG field using MCS0 and 1 OFDM symbol / 0: No VS SIG field 1: VS SIG field using MCS0 and 1 OFDM symbol 2: VS SIG field using MCS1 and 1 OFDM symbol 3: VS SIG field using MCS0 and 2 OFDM symbols
 | B20B21/22-… | Disregard | … | Set to all 1s and treat as Disregard.
4 usec / 4 or 8 usec

## Slide 5: … wherein 1 / 2 examples of the potential VS SIG binary fields are:
Hart et al (Cisco Systems)
Bitwidth | Description
9 | Vendor ID
1 | VS Validate
6 | Vendor Specific Content
4 | CRC
6 | Tail
Bitwidth |  | Description
16 | 24 | Vendor ID
1 | 1 | VS Validate
25 | 17 | Vendor Specific Content
4 |  | CRC
6 |  | Tail
26 bits available
(MCS0, 1 OFDM symbol)
52 bits available
(MCS1 or 2 OFDM symbols)
Vendor ID:
      9-bit and 16-bit Vendor IDs are a finite resource and must be limited to genuine silicon vendors - might be assigned judiciously by 802.11 ANA and acclaimed by a WG vote
      24-bit Vendor ID = OUI; allocated in the usual way (no need to support OI)
VS Validate: 0 (continue receiving PPDU whether or not VS signaling is known), 1 (continue receiving PPDU if VS signaling known; otherwise just assert CCA busy required for the rest of the PPDU)
Vendor Specific Content = not specified by 802.11

## Slide 6: Receive Procedure
Hart et al (Cisco Systems)
A UHR STA that receives a UHR PPDU identifies the presence and duration of the VS SIG field
If the VS-SIG field is present:
  If the VS SIG CRC is bad:
    The STA may stop processing the PPDU or skip over the VS-SIG (with unchanged CCA requirements either way)
  Else:
    If the STA understands the VS signaling*, the STA processes the PPDU using the vendor extensions
    Elseif the VS Validate field equals 0, the STA processes the PPDU without the vendor extensions
    Else (VS Validate field equals 1) the STA stops processing the PPDU (with unchanged CCA requirements)
* VS signaling = Vendor ID + any portions of the Vendor Specific Content that have Validate semantics too.

## Slide 7: Summary
Hart et al (Cisco Systems)
We propose a way to future proof the U-SIG field even when there are vendors that seek to incorporate vendor specific features
The overhead is 1-2 bits in the U-SIG field for disinterested vendors
The overhead is 4-8 usec for vendors seeking to incorporate vendor specific features, and offers circa 6-17-25 bits for vendor specific content for signaling vendor specific PPDU extensions.

## Slide 8: Backup
Hart et al (Cisco Systems)

## Slide 9: Hypothetical Examples where Vendor Specific Signalling is needed for (UL/DL, VS Validate = 0/1):
Hart et al (Cisco Systems)
UL MU PPDU indicates VS Validate = 0 and:
TX reports it is currently moving at high speed; or not
TX reports is has extra-low low phase noise / amplitude wander / EVM transmitter; or not
…
UL MU PPDU indicates VS Validate = 1 and:
Sends a VS constellation/code rate/FEC
…
DL PPDU* indicates VS Validate = 0 and:
Sends standardized constellations/code rates/FECs to users outside the ecosystem and VS constellations/code rates/FECs to individual users (or groups of users) within the ecosystem
…
DL PPDU* indicates VS Validate = 1 and:
Uses an extra-short GI for the Data field
…
*For when BSS Color and STA-ID are not locally unique; or when the RX HW is virtualized and the RX is in communication with other APs/GOs, etc