## Slide 1: Security Enhancement Follow Up
Date: 2023-06-20
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Control Frame Protection and MAC Header Protection
At least Trigger and BA related Control frame are protected through integrity protection.
Per link CPTK/CGTK and related PN space are defined.
MAC header protection is used for unicast Data/Management frame only.
  If MAC header protection is applied for broadcast Management frame, the different format of MAC header protection should be defined.
The optional support announcement of Control frame and MAC header protection should be provided.

## Slide 3: RTS Consideration
Unless RTS is protected, the 3rd party STA can use unprotected RTS to solicit a STA in dynamic SM power save to use multiple RF chains.
One way to address this issue is that the RTS is not used to address to a STA/AP that supports Control frame protection.
  With this dynamic BW negotiation can’t be used.
  This means allowing the Tx of MU-RTS at the STA side. Another possibility is that the Tx of RTS is allowed at STA side.
Another way is that the RTS is not used to address to a STA/AP that supports Control frame protection with the following exception
  RTS can be used for dynamic BW negotiation
The third way is that the RTS is not used to address to a STA that supports Control frame protection with the following exception
  RTS can be used for dynamic BW negotiation

## Slide 4: PS Poll Consideration
Attack analysis
  For a STA that wakes up through listening interval, an attacker can transmit PS-Poll before the STA’s awaking to ask the AP to transmit the buffered frames for the STA.
    When the STA wakes up, the AP has no buffered frames for it.
  The other attack through PS-Poll could also be possible.
Solution:
  All STAs that support control frame protection need to support UAPSD.
    The protected UAPSD trigger frame is used instead of PS-Poll to notify the AP of STA’s awake state.

## Slide 5: Ack Consideration
All STAs that support control frame protection need to support the transmission and the reception of Multi-STA BA.
  The protected Multi-STA BA frame is used instead of Ack between AP and STA that support control frame protection.

## Slide 6: Compressed BA Consideration
Given that each STA that supports control frame protection needs to support the Multi-STA BA, the protected Multi-STA BA frame will be used instead of compressed BA between AP and STA that support control frame protection.

## Slide 7: CF-End CTS Consideration
It seems we don’t need to protect CF-End and CTS.

## Slide 8: Optional Support of Protected Control Frame Protection
We assume that UHR includes the protection of unicast control frame.
  The KID, PN, MIC are carried in the protected unicast frame.
    Such change means the new frame format to the STAs that doesn’t support Control frame protection.
      Such STAs may discard them that are addressed to such STAs.
With this consideration, UHR needs to support the announcement about whether a STA/AP supports the Control frame Protection.

## Slide 9: CPTK vs GPTK
With CPTK, the 3rd-party STA with GPTK can’t attack the STAs with broadcast Control frames through transmitting multiple protected/unprotected unicast Control frames to the STAs per the control frame protection capabilities of the STAs.
  This method can’t be used in EMLSR mode as the DL initiating Control frame.
  The AP’s implementation becomes complicated.
  The TXOP protection is weak in 2.4/5GHz band.
Protected broadcast Trigger frame
in non-HT duplicated PPDU
Protected broadcast Multi-STA frame
in non-HT duplicated PPDU
Protected unicast Trigger frames
in DL MU PPDU
Protected unicast BA frames
in DL MU PPDU

## Slide 10: CPTK vs GPTK (Cont’d)
An AP announces whether it will not transmit protected broadcast Control frame unless the protected Control frame is unavoidable.
A STA that supports the Control frame protection discards the protected Control frame addressed to it if its associated AP announce no transmission of the protected broadcast Control frame unless the protected Control frame is unavoidable.
Protected broadcast Trigger frame
in non-HT duplicated PPDU
Protected broadcast Multi-STA frame
in non-HT duplicated PPDU
Protected unicast Trigger frames
in DL MU PPDU
Protected unicast BA frames
in DL MU PPDU