## Slide 1: In-Device Interference Discussion
Date: 2023-06-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: In-Device Interference
In-device non-WiFi radio types:
  BT, BLE, 15.4, UWB, LTE/NR…
In-device non-WiFi radio application profiles:
  Periodic
    The different applications may have different intervals, durations with different granularities
  aperiodic.
Devices with non-WiFi radio
  Non-AP STA
  Soft/mobile AP

## Slide 3: Periodic In-device Interference Duration Report
An AP/STA with in-device non-WiFi radio whose application profiles include periodic traffic reports its periodic SPs of in-device non-WiFi radio to its peer device.
  the AP may broadcast its periodic SPs of in-device non-WiFi radio through Beacon or the other broadcast Management frame.
  The report of the periodic SPs in a new defined element should be adaptable to various application profiles, e.g.
    The start time, interval, SP duration should not be in unit of TU.
    The BW being affected should be in unit of 20MHz.
    The information of multiple application profiles can be reported in one element.

## Slide 4: Aperiodic Interference Analysis
When receiving a PPDU with an A-MPDU addressed to it, the in-device non-WiFi radio of the TXOP responder (AP or STA) may start the transmission of non-WiFi packet.
  The TXOP responder receives part of the A-MPDU in the PPDU.
If the TXOP holder solicits the immediate response from the TXOP responder (AP or STA) while the in-device non-WiFi radio of the TXOP responder is receiving a packet with higher priority, the TXOP responder may not transmit the immediate response.
When a STA’s in-device non-WiFi radio is transmitting a packet, the TXOP holder transmits a PPDU with the A-MPDU to the STA.
  The STA misses the whole A-MPDU.
When transmitting a responding frame other than the TXOP’s first frame exchange, the TXOP responder (AP or STA) knows the start time of the packet exchanges of its in-device non-WiFi radio that will overlap with the TXOP.
When receiving the first frame of the TXOP, the TXOP responder (AP or STA) knows the start time of the packet exchanges of its in-device non-WiFi radio that will overlap with the TXOP.

## Slide 5: Aperiodic Interference Mitigation (1)
An AP/STA announces whether it has active in-device non-WiFi radio.
  A STA may also report the BW being interfered by the active in-device non-WiFi radio in unit of 20MHz.
    The 20MHz channel bitmap can be used for such report.
An AP considers its associated STA’s active in-device non-WiFi radio information when doing MU transmission, link adaptation, rate/MCS selection.
A STA considers its associated AP’s active in-device non-WiFi radio information when doing link adaptation, rate/MCS selection.

## Slide 6: Aperiodic Interference Mitigation (2)
The BA frame carries the indication of in-device radio interference if the TXOP responder (AP or STA) figures out the in-device interference during the reception of an A-MPDU.
If a TXOP responder (AP or STA) can’t transmit the solicited immediate BA because of the packet Tx/Rx of the in-device non-WiFi radio, one of the following can be done
  the TXOP responder may transmit an unsolicited frame with the indication of not being able to transmit the solicited BA.
    The indication can be carried in HE Control field.
  The TXOP responder may transmit the BA after receiving the following BAR
    The BA carries the indication that the in-device interference during when BA is solicited.
If a TXOP responder (AP or STA) misses the whole A-MPDU solicited by a BAR, the TXOP responder may respond a BA with the announcement of the most recent in-device radio activity (start time, duration).
  The most recent in-device radio activity (start time, duration) can also be carried in HE Control frame of the QoS Null.
  A STA/AP may announce its most recent in-device radio activity without the soliciting in the HE Control of the QoS Null or the other frame.

## Slide 7: Aperiodic Interference Mitigation (3)
When receiving the first frame (e.g. RTS/MU-RTS) of the TXOP, the TXOP responder (AP or STA) knows the start time of the packet exchanges of its in-device non-WiFi radio that will overlap with the TXOP.
  In this case, the TXOP responder uses the Duration field in the first responding frame (e.g. CTS) of the TXOP to carry the expected ending time of the frame exchanges with it.
When transmitting a responding frame (e.g. QoS Data frames) other than the TXOP’s first frame exchange, the TXOP responder (AP or STA) knows the start time of the packet exchanges of its in-device non-WiFi radio that will overlap with the TXOP.
  In this case, the TXOP responder uses the Duration field in the responding frame (e.g. QoS Data frames) of the TXOP to carry the expected ending time of the frame exchanges with it.

## Slide 8: Impact Mitigation of In-device Coexisting Interference under MLD
The mitigation of in-device coexisting Interference is a link level feature when the STA/AP is affiliated with non-AP/AP MLD.
The related management frame, HE Control for one link can be transmitted in another link.
  The MLO Link Information element in the frame indicates the link where the management frame is applied.
  Any information of the coexisting radios other than Wi-Fi in one link can be reported in another link through Action, HE Control in Data/Management frame.