## Slide 1: Thoughts on seamless roaming
Date: 2023-7-10
Authors:

## Slide 2: Introduction
One of the scope of UHR is:
  “at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation and at least one mode of operation capable of reducing MAC Protocol Data Unit (MPDU) loss by 25% compared to the Extremely High Throughput MAC/PHY operation for a given scenario, especially for transitions between BSSs[1]”
Therefore, a transition method which enable fast and lossless transition between BSSs (seamless roaming) will be needed for UHR. There are some contributions discussing seamless roaming[2], but these contributions have different assumptions.
We summarize these from an architectural point of view and propose a start point for discussion.

## Slide 3: Architecture for MLO
The proposed architectures for seamless roaming are based on MLD architecture.
MLD can support more than one affiliated station (STA) and can operate using one or more affiliated STAs.
MLD has one upper MAC(UMAC) and several lower MACs(LMACs) per link. LMACs are corresponding to a STA affiliated with the MLD.
  The upper MAC performs functionalities that are common across all links.
  The lower MAC performs functionalities that are local to each link.
UMAC
LMAC
LMAC

## Slide 4: Expanding MLO architecture for seamless roaming
In multi-link operation, MLD is built on a single device.
  All STAs affiliated with same MLD are collocated.
However, MLD may support non-collocated STAs. In that case, UMAC will cooperate with non-collocated LMAC.
  Interface between UMAC and non-collocated LMAC is wired/wireless.
Collocated
UMAC
LMAC
LMAC
LMAC
UMAC

## Slide 5: Management entity for seamless roaming
UMAC may spit into upper UMAC and lower UMAC to support AP MLD specific function.
  Boundary between upper UMAC and lower UMAC is depending on functionality.
  For example, if TID is mapped locally in AP MLD, lower UMAC may perform TID-to-link mapping function.
In this contribution, we consider the case where UMAC is split.
  Logically, there is no big difference between single UMAC and separated UMAC.
Collocated
UMAC
LMAC
LMAC
LMAC
UMAC
Upper UMAC
LMAC
LMAC
Lower UMAC
Upper UMAC
LMAC
LMAC
Lower UMAC

## Slide 6: Collocated or Non-collocated Upper UMAC
Upper UMAC could be included in AP MLD (Collocated Upper UMAC), but another device could perform the function (Non-collocated Upper UMAC) [3, 4].
Main difference between these is existence of external device which has the upper UMAC, and these are not very different logically.
Collocated
Collocated upper UMAC
Lower UMAC
LMAC
LMAC
Lower UMAC
LMAC
LMAC
Upper UMAC
Upper UMAC
Lower UMAC
LMAC
LMAC
Lower UMAC
LMAC
LMAC
Upper UMAC
Upper UMAC
Upper UMAC
Non-Collocated upper UMAC

## Slide 7: Single Serving AP MLD Mode and Multiple Serving AP MLD mode
Usually, non-AP MLD communicates with one AP MLD(Single Serving AP MLD mode).
In the seamless roaming architecture, non-AP MLD uses links between multiple AP MLDs while roaming (transient Multiple Serving AP MLD mode).
Some contribution discuss about non-transient Multiple Serving AP MLD mode which allows non-AP MLD to communicate with multiple AP MLDs in steady state as well as during roaming.[4, 5]
Lower UMAC
LMAC
LMAC
Lower UMAC
LMAC
LMAC
Upper UMAC
LMAC
UMAC
LMAC
Lower UMAC
LMAC
LMAC
Lower UMAC
LMAC
LMAC
Upper UMAC
LMAC
UMAC
LMAC
Single Serving AP MLD mode
Multiple Serving AP MLD mode

## Slide 8: Non-transient Multiple Serving AP MLD mode
In some cases, non-transient Multiple Serving AP MLD mode is useful.
  When an AP MLD has few radios[4], AP MLDs can serve enough link for multi radio non-AP MLDs.
  When an AP MLD is an NSTR mobile AP MLD, AP MLDs can serve STR link pair.
  When some of the APs affiliated with the AP MLD are under maintenance, another AP MLD can serve links for non-AP MLDs.
  When some of the APs affiliated with the AP MLD are unavailable to use due to regulations, e.g., AP is prohibited to use 6 GHz by AFC(Automated Frequency Coordination), another AP MLD located on different place can serve link.
  Links to several distant STA can create spatial diversity to enhance reliability.
But there may be some things to discuss with this mode.

## Slide 9: Starting point of discussion
Upper UMAC collocated with AP MLD is good for starting point.
  The collocated upper UMAC architecture requires at least two AP MLDs and does not require external devices to be considered.
  There may be little or no difference in terms of logical entities.
For simplicity, single serving AP MLD mode and transient Multiple Serving AP MLD mode is good for starting point.
  Fast and lossless transition can be enabled by transient multiple serving AP MLD mode.
  To support some of the use cases listed in the previous page, we will discuss the non-transient multiple serving AP MLD mode later.

## Slide 10: Conclusion
Discussion points for a seamless roaming architecture are presented.
  Upper MAC(UMAC) may be split into upper UMAC and lower UMAC.
  Upper UMAC will be collocated or not collocated with AP MLD.
  Non-AP MLD may communicate with more than one AP MLD while roaming (transient Multiple Serving AP MLD mode) or not roaming(non-transient Multiple Serving AP MLD mode).
We propose to start discussion with simple architecture.
  Start with Upper UMAC collocated with AP MLD.
  Start with single serving AP MLD mode and transient multiple serving AP MLD mode but should extend to non-transient multiple serving AP MLD mode.

## Slide 11: References
[1] 11-23-0480-03-0uhr-uhr-proposed-par.pdf
[2] 11-22-1910-03-0uhr-seamless-roaming-for-uhr.pptx
[3] 11-23-0231-00-0uhr-thoughts-on-seamless-roaming-under-the-non-collocated-ap-mld-architecture.pptx
[4] 11-23-0705-00-0uhr-non-colocated-ap-mld-framework-for-uhr.pptx
[5] 11-23-0632-01-0uhr-smooth-roaming-follow-up.pptx