## Slide 1: Relay transmission in UHR
Date: 2023-07-07
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
July. 2023

## Slide 2: Introduction
In the previous meeting, we introduced the Relay operation in UHR to improve the transmission reliability as well as improve Throughput.
We also addressed the various consideration points described in [1] to support the Relay transmission in UHR.
  Definition of a type of Relay STA
  TXOP sharing for Relay transmission
  QoS enhancement method
  Etc.
In this contribution, we examine carefully the Relay transmission for DL and UL in UHR based on the introduced considerations.

## Slide 3: Relay operation in UHR(1/4)
The announcement of Relay operation
  In a BSS, the Relay operation is announced by the AP through the management frame such as the beacon.
    The following information may be contained in the beacon frame to notify the Relay operation.
      The support of Relay operation.
        It indicates whether AP supports Relay operation or not in a BSS. So. It can be defined as a AP’s capability.
      Enabling of Relay operation
        When Relay operation is supported, it indicates whether Relay operation is possible. Also, it can include the operation parameters that can be supported at a maximum in Relay operation.
          For example, Nss, MCS, BW, etc.
        Based on the association with Relay STA, AP may compose the information for the enabling of Relay operation transmitted on the beacon frame.
  Through receiving the beacon frame, the non-AP STA can recognize the support of Relay operation in a BSS. And, AP also can identify which non-AP STA has a capability for Relay operation through the association.

## Slide 4: Relay operation in UHR(2/4)
Identification of the Relay STA
  As described in [1], since Relay STA is defined as a non-AP STA, it also performs the association procedure for AP.
    So, AP can identify the Relay STA through the exchange of association frame including the Relay STA’s capabilities.
      The specific capability may indicate whether non-AP STA is Relay STA or not.
  The AID for the Relay STA may be set to in the range of 1 to 2007 as same with the non-AP STA or may be selected from a specific value or range that is not currently in use.
    This AID can be used to notify the Relay STA to non-AP STA in a BSS.
      If one of AID in the same range for non-AP STA is used, we may need to consider additional signaling to indicate the Relay STA with AID.

## Slide 5: Relay operation in UHR(3/4)
TXOP Sharing for Relay operation
  In Relay operation, we should consider the both transmission between AP and Relay STA and the transmission between Relay STA and non-AP STA(s).
  Herein, to protect and guarantee the transmission between Relay STA and non-AP STA, we can consider applying the TXOP sharing procedure defined in 11be in the Relay operation.
    By using the TXS TF, AP can allocate the time duration to Relay STA for transmission between Relay STA and non-AP STA.
    As a TXS TF, the MU-RTS TXS TF with Triggered TXOP Sharing Mode subfield value equal to 2 can be considered.
      It is a simple way and can leverage the frame format defined in the current spec.
    However, since it is not allowed the any transmission from the AP in this duration, we need to more consideration how to apply the TXOP sharing for the Relay operation.
TXS TF
AP
Relay STA
SIFS
CTS

## Slide 6: Relay operation in UHR(4/4)
Considerations for TXOP sharing on Relay operation
  As shown in [1], the transmission between AP and Relay STA and the transmission between Relay STA and non-AP STA is sequentially performed.
  Therefore, in order for the AP to efficiently manage two sequential transmissions, we can take into account defining a new TXS mode or a new TF variant for TXS for the Relay operation
    If a new TXS mode is considered, for example, a new TXS mode for Relay operation may be defined by using the 3 of Triggered TXOP Sharing Mode subfield value as defined with reserved in 11be.
      In this mode, the signal exchange with AP can be allowed. Therefore, it is possible to transmit a signal to Relay STA from AP and exchange the control signaling such as ack with AP.
    If the design of a new TF variant for Relay operation is considered, for example, it can be defined as one of the trigger frame variants by using a value of the Trigger type subfield.
      Since trigger frames used for Relay operation can be freely defined by using the new TF variant, we can newly design the TXS TF for Relay operation.

## Slide 7: DL Relay transmission (1/2)
The procedure of DL Relay transmission.
  After TXOP sharing, AP transmits the PPDU1 with the following information to Relay STA.
    Data for non-AP STA(s) participated in the Relay operation.
      To indicate that this PPDU is intended for Relay transmission, the indication can be included in the U-SIG/UHR-SIG.
    Transmission parameters per non-AP STA such as MCS, Nss, RA, etc.
      That information is used when the Relay STA transmits signal to each non-AP STA and can be indicated by using the user field of the UHR-SIG field.
  After confirming the received data(i.e., PPDU1), an Ack frame(i.e., Ack1) is transmitted to the AP, and the data (i.e., PPDU2) is transmitted to each non-AP STA after SIFS by Relay STA.
    The data per non-AP STA is encoded with MCS indicated by AP and transmitted on allocated RU.
AP
Relay STA
Non-AP STA(s)
SIFS
PPDU1
SIFS
Ack1
TXOP sharing for Relay operation
PPDU2
SIFS
Ack2
Ack3
SIFS
SIFS

## Slide 8: DL Relay transmission (2/2)
    As the confirmation of the successful receiving of the signal, the Ack frame(i.e., Ack2) can be transmitted from non-AP STA(s) to the Relay STA.
      For the case of Ack2, the current Ack policy can be used.
    After receiving the acknowledgment from the participating non-AP STA(s), the Relay STA transmits the acknowledgment(i.e., Ack3) generated based on the received acknowledgment(i.e., Ack2) to AP.
      It may be required a new ack policy to support the Ack3 because this does not relate to data transmission directly.
AP
Relay STA
Non-AP STA(s)
SIFS
PPDU1
SIFS
Ack1
TXOP sharing for Relay operation
PPDU2
SIFS
Ack2
Ack3
SIFS
SIFS

## Slide 9: UL Relay transmission (1/2)
The procedure of UL Relay transmission.
  After TXOP sharing, to initiate the UL Relay transmission, AP transmits the trigger frame.
    The trigger frame can be defined newly and may include the following information
      The parameters per the non-AP STA(s) including the Relay STA for transmission solicited by AP.
        In an aspect of the Relay STA, the received information is used when it transmits the data to AP after receiving the data from the non-AP STA(s).
  The non-AP STA(s) participated transmits the signal(i.e. PPDU1) to the Relay STA by using the received Trigger frame.
    Here, even though Relay STA received the trigger frame from the AP, it does not transmit anything after SIFS.
AP
Relay STA
Non-AP STA(s)
SIFS
Trigger frame
SIFS
Ack1
TXOP sharing for Relay operation
PPDU1
SIFS
Ack2
Ack3
SIFS
SIFS
PPDU2
SIFS

## Slide 10: UL Relay transmission (2/2)
  After receiving the PPDU1 from the non-AP STA(s), the Relay STA transmits an acknowledgment (i.e., Ack1) to the non-AP STA(s), and re-encode the data by applying the transmission parameters indicated through the trigger frame. And then, Relay STA transmits PPDU2 to AP a SIFS after.
  AP transmits the acknowledgment (i.e., Ack2) to Relay STA a SIFS after the PPDU2 is received. And, the Relay STA also transmits the acknowledgment (i.e., Ack3) to the non-AP STA(s) a SIFS after the acknowledgment (i.e., Ack2) is received.
    Unlike Ack1 and Ack2, Ack3 is not actually related to data transmission, so a new Ack policy may need to be defined to define it.
AP
Relay STA
Non-AP STA(s)
SIFS
Trigger frame
SIFS
Ack1
TXOP sharing for Relay operation
PPDU1
SIFS
Ack2
Ack3
SIFS
SIFS
PPDU2
SIFS

## Slide 11: Consideration of acknowledgment
  For the optimized procedure regarding the acknowledgment transmission in the Relay operation, we can consider the following.
    In the Relay operation, Relay STA may not be required to send the acknowledgment for received data.
      For example, in the Relay operation, the Relay STA may be not required to send the acknowledgement.
    According to the above, we can optimize the DL/UL Relay transmission as follow
      The Ack frame is only transmitted between AP and non-AP STA(s).
        Since the non-AP STA(s) participants is associated-STA, the non-AP STA can transmit the Ack frame to AP directly.
AP
Relay STA
Non-AP STA(s)
SIFS
PPDU1
SIFS
TXOP sharing for Relay operation
PPDU2
Ack1
SIFS
AP
Relay STA
Non-AP STA(s)
SIFS
Trigger frame
SIFS
TXOP sharing for Relay operation
PPDU1
SIFS
Ack3
PPDU2
SIFS
DL case
UL case

## Slide 12: Summary
In this contribution, we investigated the procedure for the Relay operation in DL and UL transmission.
  For the efficient transmission and management by AP, we can consider using the TXOP sharing in advance of the Relay transmission.
    In a TXOP sharing mode for Relay operation, both transmissions between AP and Relay STA and between Relay STA and non-AP STA are performed.
  In DL, to indicate that the transmitted PPDU is for the Relay operation, an indication can be included in the PPDU, for example, U-SIG or UHR-SIG.
  In UL, to initiate the Relay operation, AP sends the trigger frame to both Relay STA and non-AP STA(s).
    By using the Trigger frame, non-AP STAs can transmit the signal simultaneously and Relay STA can prepare the receiving from the non-AP STAs.
  Also, we considered how to transmit the acknowledgment for data exchange between Relay STA and non-AP STA(s) as well as AP and Relay STA.
    To improve the efficiency of Relay operation, we need to more discussion ways to transmit the ack frame in Relay operation.

## Slide 13: Reference
[1] 11-23-0042-00-0uhr-Thought for Range Extension in UHR