## Slide 1: Obfuscation Computation Procedure
Date: 2023-11-10
Authors:

## Slide 2: Abstract
The contribution is a follow-up of the computation procedure (based on a standardized PRF) presented in 22/114r3, 23/411 and 23/1147 and used to obfuscate the values of the CPE parameters (e.g. MAC Address, SN, PN, TID) transmitted OTA
As a reminder, a SP has been initiated with the following results :
“Do you support the use of a single PRF to generate new CPE parameters with inputs such as the current OTA MAC address and a shared private key?”
SP result: Yes:8, No:0, Abstain:3; Would more information:7
The objective of this contribution is to precise the CPE parameters involved in the computation procedure and the obfuscation method to be applied for each one

## Slide 3: Obfuscation
For reminder, according to the specified 802.11bi requirements, when the OTA MAC address of the CPE Client is changed (R7), the CPE Client changes the transmitted SN and the scrambler seed on downlink and uplink (R9), the transmitted PN on downlink and uplink (R10), its AID (R11) and the transmitted TID (R30)
The obfuscation consists in a change of the OTA values of theses CPE parameters at the start of each new epoch.
For this, the “internal” value of the CPE parameter is either
  reset and replaced by a new uncorrelated and randomized one (reset-based)
  obfuscated by an obfuscation operation as XOR, addition or an Offset (mask-based)

## Slide 4: Computation procedure
The computation procedure is based on a standardized PRF executed in parallel by the CPE Client and the CPE AP
It computes at once new reset values for each reset-based CPE parameter and new masks for each mask-based CPE parameter to be applied for the next epoch (n+1).
Only one execution of the computation procedure is necessary for each epoch

## Slide 5: Computation procedure
A standardized PRF (as specified in 12.7.1.2 -IEEE Std 802.11-2020) takes 3 input parameters (K,A,B) with K as a key, A as a purpose label and B as a variable length string
  K : ERCM key (Private parameter), typically derived from PTK established during the authentication exchange
  A : String “ERCM”
  B : Temporal Reference
The output CPE_PARAM corresponds to a sequence of pseudo random bits which is split into predetermined chunks, each chunk corresponding either to a new reset value for each reset-based CPE parameter or a new shared mask for each mask-based CPE parameter
CPE_PARAM (n+1) = PRF-M\L(K,A,B)
M = 128, 192, 256, 384, 512 or 704
L the leftmost bits corresponding to the sum of the lengths of the CPE parameters
Input parameters
Output parameters

## Slide 6: CPE parameters
If the list of CPE parameters has been specified in 802.11bi requirements, the obfuscation procedure for each one has not been yet specified
Moreover, it has not yet taken into account that 802.11bi devices that support STA MAC address change while associated shall be MLD capable.
CPE Parameters | Requirement
OTA MAC address | 7
UL/DL SN | 9
UL/DL Scrambler Seed | 9
UL/DL PN | 10
AID | 11
UL/DL TID | 30

## Slide 7: MLD Considerations - Proposal
CPE parameters of the MLD CPE Client (MLD Level Parameters) and these of its affiliated non-AP STAs (Link Level Parameters) are generated with a single execution of a standardized PRF
A reset-based obfuscation procedure is applied for
  OTA MLD MAC address and OTA MAC addresses of each affiliated non-AP STAs
  DL and UL Scrambler Seed
  AID
A Per-Link mask-based obfuscation procedure (a different mask for each link) is applied
  SN, PN
  TID

## Slide 8: Example of a CPE Parameters Obfuscation Computation
1 1 …. 0 1 …….. 1 0 ………1 0……..10 1……...1 0……... 1 1 ..…… 0 1 …… 1 0…… 1 ……….0 1 ……..1 1……… …..1
bit 1 ……. 47…… 63 ……… …………250 251… … 438
OTA UL
SS#1
OTA DL
SS#1
OTA MLD MAC (n+1) = CPE_PARAM (n+1) [1..46]
OTA AID (n+1) = CPE_PARAM (n+1) [47..62]
OTA MLD MAC
STA MLD
Affiliated STA #1
Affiliated STA #2
OTA
AID
OTA
MAC@#1
Mask
UL_SN#1
Mask
DL_SN#1
Mask
UL_PN#1
Mask
DL_PN#1
Mask
UL TID#1
OTA MAC STA#1 (n+1) = CPE_PARAM (n+1) [63..108]
OTA UL_SN#1 (n+1) = UL_SN + CPE_PARAM (n+1) [109..120]
OTA DL_SN #1 (n+1) = DL_SN + CPE_PARAM (n+1) [121..132]
OTA UL_PN #1 (n+1) = UL_PN + CPE_PARAM (n+1) [133..180]
OTA DL_PN #1 (n+1) = DL_PN + CPE_PARAM (n+1) [181..228]
OTA UL_TID #1 (n+1) = UL_TID + CPE_PARAM (n+1) [229..232]
OTA DL_TID #1 (n+1) = DL_TID + CPE_PARAM (n+1) [233..236]
OTA UL_SS #1 (n+1) = CPE_PARAM (n+1) [237..243]
OTA DL_SS #1 (n+1) = CPE_PARAM (n+1) [244..250]
OTA MAC STA#2 (n+1) = CPE_PARAM (n+1) [251..296]
OTA UL_SN#2 (n+1) = UL_SN + CPE_PARAM (n+1) [297..308]
OTA DL_SN#2 (n+1) = DL_SN + CPE_PARAM (n+1) [309..320]
OTA UL_PN#2 (n+1) = UL_PN + CPE_PARAM (n+1) [321..368]
OTA DL_PN#2 (n+1) = DL_PN + CPE_PARAM (n+1) [369..416]
OTA UL_TID#2 (n+1) = UL_TID + CPE_PARAM (n+1) [417..420]
OTA DL_TID#2 (n+1) = DL_TID + CPE_PARAM (n+1) [421..424]
OTA UL_SS#2 (n+1) = CPE_PARAM (n+1) [425..431]
OTA DL_SS#2 (n+1) = CPE_PARAM (n+1) [432..438]
Mask
DL TID#1

## Slide 9
Straw Poll #1
SP#1 : Do you support that MLD Level Parameters and Link Level Parameters are generated with a single execution of a standardized PRF ?
  Yes
  No
  Abstain

## Slide 10
Straw Poll #2
  SP#2 : Do you support a per-link mask-based obfuscation procedure for SN, PN and TID ?
  Yes
  No
  Abstain

## Slide 11: References
[1] IEEE 802.11-21/1848r16 : Requirements Document
[2] IEEE 802.11-22/0114r3 : Enhanced Randomized and Changing MAC address
[3] IEEE 802.11-23/0166r1 : Mechanism of simultaneous changes to SN scrambler seed PN AID and TID
[4] IEEE 802.11-23/336r1 : AID modification upon MAC address change
[5] IEEE 802.11-23/411r1 : Obfuscation of Multiple CPE Parameters
[6] IEEE 802.11-23/268r1 : OTA MAC Address Change
[7] IEEE 802.11-23/873r0 : Client Frame Tracking Countermeasures